## Slide 1: On Context Selection for significant_ coeff_flag coding (JCTVC-E362)
Jian Lou, Krit Panusopone, Limin Wang
Motorola Mobility

## Slide 2: Significant Coefficient Flag Coding
A map indicating if there is non-zero coefficients or not
Two schemes are used in HM-2.0
  Position related (small block, >16x16 TU, low frequency coefficient in large blocks)
  Coded neighbors related (high frequency coefficient in large blocks)

## Slide 3: Context selection using 5 coded neighbors information

## Slide 4: Context selection using 2 coded neighbors information

## Slide 5: Context selection using 3 coded neighbors information

## Slide 6: Context selection using 4 coded neighbors information

## Slide 7: Experimental Results configuration settings
Implemented in HM-2.0
Anchor using common test condition
  5 coef context model
Proposed context models
  Only apply to 16x16, 32x32 TUs
Results cross checked by I2R (E106)

## Slide 8: Experimental results (2 coef context model)
 | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.6 | 0.4 | 0.5 | 0.5 | 0.4 | 0.2 |  |  | 
Class B | 0.4 | 0.3 | 0.4 | 0.3 | 0.2 | 0.2 | 0.4 | 0.3 | 0.1
Class C | 0.3 | 0.2 | 0.2 | 0.3 | 0.1 | -0.1 | 0.5 | 0.3 | 0.3
Class D | 0.2 | 0.2 | 0.1 | 0.1 | 0.0 | 0.0 | 0.1 | -0.1 | -0.2
Class E | 0.5 | 0.3 | 0.2 |  |  |  | 0.1 | -0.8 | 0.8
All | 0.4 | 0.3 | 0.3 | 0.3 | 0.2 | 0.1 | 0.3 | 0.0 | 0.2
Enc Time[%] | 99% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 101% |  |  | 100% |  | 

## Slide 9: Experimental results (3 coef context model)
 | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.3 | 0.1 | 0.2 | 0.3 | 0.1 | 0.2 |  |  | 
Class B | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.1 | -0.1 | 0.3
Class C | 0.1 | 0.1 | 0.1 | 0.0 | -0.1 | -0.1 | 0.1 | 0.1 | 0.2
Class D | 0.1 | 0.1 | 0.1 | 0.1 | -0.3 | 0.0 | 0.0 | 0.1 | 0.1
Class E | 0.2 | 0.0 | 0.0 |  |  |  | -0.1 | -1.0 | 0.3
All | 0.2 | 0.1 | 0.1 | 0.1 | 0.0 | 0.1 | 0.0 | -0.2 | 0.2
Enc Time[%] | 99% |  |  | 99% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 10: Experimental results (4 coef context model)
 | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.3 | 0.4 | 0.5 | 0.2 | 0.5 | 0.6 |  |  | 
Class B | 0.3 | 0.2 | 0.4 | 0.3 | 0.3 | 0.4 | 0.4 | 0.3 | -0.2
Class C | 0.3 | 0.1 | 0.2 | 0.3 | 0.0 | 0.1 | 0.5 | 0.1 | 0.2
Class D | 0.2 | 0.1 | 0.1 | 0.2 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0
Class E | 0.4 | 0.2 | 0.3 |  |  |  | 0.3 | -0.6 | 1.8
All | 0.3 | 0.2 | 0.3 | 0.2 | 0.2 | 0.3 | 0.3 | 0.0 | 0.4
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 100% |  | 

## Slide 11: Conclusions
Current 5 coef context model requires 2 lines buffer
Proposed context model with reduced number of neighbors, fewer coded neighbors used for deriving contexts
Proposed 2 coef context model and 4 coef context model requires 1 line buffer
Average coding loss of 0.3% for context models with 1 line buffer
Average coding loss of 0.1% for context model with 2 line buffer