## Slide 1: JCTVC-380: CE7: Experimental results of ROT by Samsung
E. Alshina, A. Alshin , F. Fernandes, A. Saxena , V. Seregin, Z. Ma ,W.-J. Han (Samsung)

## Slide 2: ROT application scheme
<number>
Implemented as secondary transform
 no change to existing HM transform core
ROT doesn’t require change of HM quantization
 no additional Q/Q-1 matrices
Only low-frequency part of transform coefficients matrix is involved in ROT
 Implemented for 4x4 and 8x8 only, but applied for all TU sizes

## Slide 3: Sparse structure of ROT matrices
RHorizontal  input  RVertical = rotated output
ROT4 process
ROT8 matrix

## Slide 4: Number of operations
Because ROT matrices are very sparse, number introduced by ROT is small compare
to core transform:
  for 4x4 block: is comparable to 4x4 core transform
  for 8x8 block: is ~ ½ compared to 8x8 core transform.
  for larger TU sizes: ROT operations count becomes negligible compared to core transform.
 | Core HM transform |  |  |  | Additional operations for ROT |  |  |  | Total |  |  | 
TU size | “*” | “+” | “>>” | all | “*” | “+” | “>>” | all | “*” | “+” | “>>” | all
4x4 | 0 | 5 | 2 | 7 | 3.6 | 3.2 | 1.6 | 10.4 | 3.6 | 8.2 | 3.6 | 17.4
8x8 | 0 | 10 | 5.5 | 15.5 | 3.6 | 3.2 | 1.6 | 10.4 | 3.6 | 13.2 | 7.1 | 25.9
16x16 | 5.5 | 10.3 | 6.3 | 22.1 | 0.9 | 0.8 | 0.4 | 2.6 | 5.9 | 11.1 | 6.7 | 24.7
32x32 | 7.3 | 13.1 | 7.1 | 27.5 | 0.2 | 0.2 | 0.1 | 0.6 | 7.5 | 13.3 | 7.2 | 28.1
Avg | 18 |  |  |  | 6 |  |  |  | 24 |  |  | 

## Slide 5: Partial energy exchange
1=2=3=0  no change
1= , 2=3=0  1st and 2nd column switching with sign change for 2nd column
1=/2 , 2=3=0  sign change for 1st and 2nd row
{k}: |k|<, |k-|<  small change of main transform coefficients with possible sign change

## Slide 6: Additional memory usage 144 bytes
const Int g_INV_ROT_MATRIX_4[4][18]=
{
{ 248, -55, -28, -60, -244, -52, -16, 57, -249, 250, -49, -26, -54, -240, -71, -11, 75, -245,},
{ 255, 22, -8, -22, 254, -17, 6, 17, 255, 241, -84, -18, 69, 221, -110, 52, 98, 231,},
{ 237, -96, -9, 90, 229, -73, 35, 64, 245, 243, -80, -6, 70, 222, -107, 38, 100, 233,},
{ 250, -18, -54, -13, 220, -131, 55, 130, 213, 212, -143, 9, 134, 192, -103, 51, 90, 234,},
};
const Int g_INV_ROT_MATRIX_8[4][18]=
{
{ 251, -36, -31, 23, 237, -94, 42, 90, 236, 236, -100, 3, 100, 234, -25, 7, 24, 255, },
{ 243, -61, -50, -75, -230, -83, -25, 94, -237, 254, -27, -18, 22, 249, -56, 24, 54, 249, },
{ 243, -81, 12, 81, 232, -70, 11, 71, 246, 252, -41, -9, -42, -251, -28, -4, 29, -254,},
{ 174, -186, 23, 181, 158, -87, 49, 75, 240, 236, -99, -10, -99, -235, -25, 1, 27, -255,},
};
These matrices are enough for realization of 4 alternative transforms for any TU sizes
In total, 144 integers with absolute values less than 256 should be stored.
For comparison, consider Q/Q-1 matrices in HM:
  for 44 transform core: 192 elements,
  for 8x8 transform core: 768 elements.

## Slide 7: Test 1: ROT with matrix multiplications
 | Intra |  |  |  |  | Intra LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  |  | U BD-rate | V BD-rate
Class A | -1.7 |  | 0.1 |  | 0.1 | -2.7 |  |  | 1.2 | 1.1
Class B | -1.7 |  | 1.1 |  | 1.0 | -2.3 |  |  | 1.8 | 1.7
Class C | -1.7 |  | 1.6 |  | 1.5 | -2.3 |  |  | 1.8 | 1.8
Class D | -1.8 |  | 1.6 |  | 1.7 | -2.5 |  |  | 1.9 | 1.9
Class E | -1.5 |  | 0.3 |  | 0.3 | -2.2 |  |  | 1.1 | 1.1
All | -1.7 |  | 1.0 |  | 0.9 | -2.4 |  |  | 1.6 | 1.5
Enc Time[%] | 147% |  |  |  |  | 184% |  |  |  | 
Dec Time[%] | 105% |  |  |  |  | 104% |  |  |  | 
 | Random access |  |  |  |  | Random access LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.7 |  | 0.2 |  | 0.0 | -1.3 |  | 1.3 |  | 1.2
Class B | -1.0 |  | 0.8 |  | 1.0 | -1.5 |  | 1.0 |  | 1.1
Class C | -1.2 |  | 0.9 |  | 0.7 | -1.4 |  | 1.0 |  | 0.9
Class D | -1.1 |  | 0.7 |  | 0.7 | -1.3 |  | 0.9 |  | 0.7
Class E |  |  |  |  |  |  |  |  |  | 
All | -1.0 |  | 0.7 |  | 0.6 | -1.4 |  | 1.0 |  | 1.0
Enc Time[%] | 104% |  |  |  |  | 104% |  |  |  | 
Dec Time[%] | 103% |  |  |  |  | 100% |  |  |  | 

## Slide 8: Test 2: ROT with lifting
 | Intra |  |  |  |  | Intra LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  |  | U BD-rate | V BD-rate
Class A | -1.6 |  | 0.1 |  | 0.2 | -2.5 |  |  | 1.1 | 1.0
Class B | -1.6 |  | 1.1 |  | 0.9 | -2.2 |  |  | 1.7 | 1.6
Class C | -1.6 |  | 1.4 |  | 1.5 | -2.2 |  |  | 1.7 | 1.7
Class D | -1.7 |  | 1.6 |  | 1.6 | -2.3 |  |  | 1.8 | 1.8
Class E | -1.4 |  | 0.3 |  | 0.3 | -2.1 |  |  | 1.0 | 1.1
All | -1.6 |  | 0.9 |  | 0.9 | -2.3 |  |  | 1.5 | 1.5
Enc Time[%] | 163% |  |  |  |  | 204% |  |  |  | 
Dec Time[%] | 106% |  |  |  |  | 110% |  |  |  | 
 | Random access |  |  |  |  | Random access LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.7 |  | -0.1 |  | 0.1 | -1.1 |  | 1.4 |  | 1.4
Class B | -0.9 |  | 0.7 |  | 0.7 | -1.4 |  | 1.1 |  | 1.1
Class C | -1.1 |  | 0.8 |  | 0.8 | -1.4 |  | 0.8 |  | 1.0
Class D | -0.9 |  | 0.5 |  | 0.5 | -1.2 |  | 0.9 |  | 0.7
Class E |  |  |  |  |  |  |  |  |  | 
All | -0.9 |  | 0.5 |  | 0.6 | -1.3 |  | 1.1 |  | 1.0
Enc Time[%] | 109% |  |  |  |  | 106% |  |  |  | 
Dec Time[%] | 101% |  |  |  |  | 101% |  |  |  | 

## Slide 9: Test 3: ROT + DCT/DST (Best Coding Gain)
 | Intra |  |  |  |  | Intra LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  |  | U BD-rate | V BD-rate
Class A | -2.3 |  | -1.0 |  | -0.8 | -3.8 |  |  | 0.7 | 0.7
Class B | -1.7 |  | 0.4 |  | 0.2 | -2.6 |  |  | 1.0 | 0.9
Class C | -1.8 |  | 0.7 |  | 0.7 | -2.8 |  |  | 1.0 | 1.0
Class D | -2.0 |  | 0.9 |  | 0.9 | -3.0 |  |  | 1.2 | 1.2
Class E | -1.6 |  | -0.8 |  | -0.6 | -2.9 |  |  | 0.3 | 0.3
All | -1.9 |  | 0.1 |  | 0.1 | -3.0 |  |  | 0.9 | 0.9
Enc Time[%] | 157% |  |  |  |  | 198% |  |  |  | 
Dec Time[%] | 105% |  |  |  |  | 110% |  |  |  | 
 | Random access |  |  |  |  | Random access LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.8 |  | -0.5 |  | -0.4 | -1.5 |  | 1.1 |  | 1.1
Class B | -0.9 |  | 0.4 |  | 0.6 | -1.4 |  | 0.9 |  | 0.8
Class C | -1.3 |  | 0.5 |  | 0.5 | -1.6 |  | 0.6 |  | 0.8
Class D | -1.1 |  | 0.3 |  | 0.4 | -1.4 |  | 0.7 |  | 0.5
Class E |  |  |  |  |  |  |  |  |  | 
All | -1.0 |  | 0.2 |  | 0.3 | -1.5 |  | 0.8 |  | 0.8
Enc Time[%] | 108% |  |  |  |  | 106% |  |  |  | 
Dec Time[%] | 101% |  |  |  |  | 101% |  |  |  | 

## Slide 10: Test 4: ROT for MPM + DCT/DST
 | Intra |  |  |  |  | Intra LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  |  | U BD-rate | V BD-rate
Class A | -1.7 |  | -1.3 |  | -1.1 | -2.9 |  |  | 0.0 | 0,1
Class B | -1.3 |  | -0.4 |  | -0.4 | -2.0 |  |  | -0.2 | -0,1
Class C | -1.3 |  | -0.3 |  | -0.3 | -2.1 |  |  | -0.4 | -0,4
Class D | -1.4 |  | -0.2 |  | -0.2 | -2.1 |  |  | -0.3 | -0,3
Class E | -1.3 |  | -1.4 |  | -1.2 | -2.5 |  |  | -0.3 | -0,5
All | -1.4 |  | -0.7 |  | -0.6 | -2.3 |  |  | -0.2 | -0,2
Enc Time[%] | 123% |  |  |  |  | 130% |  |  |  | 
Dec Time[%] | 103% |  |  |  |  | 105% |  |  |  | 
 | Random access |  |  |  |  | Random access LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.7 |  | -0.3 |  | -0.3 | -1.1 |  | 0.6 |  | 0,6
Class B | -0.6 |  | 0.2 |  | 0.3 | -1.0 |  | 0.3 |  | -0,2
Class C | -0.9 |  | -0.1 |  | -0.1 | -1.2 |  | -0.1 |  | 0,2
Class D | -0.7 |  | -0.1 |  | 0.1 | -1.0 |  | -0.1 |  | -0,1
Class E |  |  |  |  |  |  |  |  |  | 0,1
All | -0.7 |  | 0.0 |  | 0.0 | -1.0 |  | 0.2 |  | 0,6
Enc Time[%] | 104% |  |  |  |  | 102% |  |  |  | 
Dec Time[%] | 100% |  |  |  |  | 100% |  |  |  | 

## Slide 11: Test 5: ROT + DCT/DST + 2nd Step MDT (JCTVC-E074)
 | Intra |  |  |  |  |  | Intra LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  | V BD-rate |  | Y BD-rate |  |  | U BD-rate | V BD-rate
Class A | -1,8 |  | -1,5 |  | -1,3 |  | -3,0 |  |  | -0,2 | -0,1
Class B | -1,5 |  | -0,4 |  | -0,5 |  | -2,2 |  |  | -0,3 | -0,3
Class C | -1,5 |  | -0,3 |  | -0,3 |  | -2,3 |  |  | -0,4 | -0,4
Class D | -1,5 |  | -0,2 |  | -0,2 |  | -2,2 |  |  | -0,3 | -0,3
Class E | -1,7 |  | -1,8 |  | -1,6 |  | -2,8 |  |  | -0,7 | -0,9
All | -1,6 |  | -0,8 |  | -0,7 |  | -2,5 |  |  | -0,4 | -0,4
Enc Time[%] | 125% |  |  |  |  |  | 134% |  |  |  | 
Dec Time[%] | 104% |  |  |  |  |  | 107% |  |  |  | 
 | Random access |  |  |  |  |  | Random access LoCo |  |  |  | 
 | Y BD-rate |  | U BD-rate |  |  | V BD-rate | Y BD-rate |  | U BD-rate |  | V BD-rate
Class A | -0.8 |  | -0.7 |  |  | -0.8 | -1,2 |  | 0,3 |  | 0,3
Class B | -0.8 |  | 0.1 |  |  | 0.1 | -1,2 |  | 0,1 |  | 0,0
Class C | -1,0 |  | -0,1 |  |  | -0,1 | -1,3 |  | -0,2 |  | 0,0
Class D | -0,8 |  | -0,1 |  |  | 0,0 | -1,0 |  | 0,1 |  | -0,1
All | -0.8 |  | -0.2 |  |  | -0.2 | -1,2 |  | 0,1 |  | 0,0
Enc Time[%] | 106% |  |  |  |  |  | 104% |  |  |  | 
Dec Time[%] | 101% |  |  |  |  |  | 101% |  |  |  | 

## Slide 12: Recommended alternative transform design
Average operations per pixel | 
Core Transform | 6
Proposed | 7
 | indexROT = 0 ¦¦ UDI mode != MPM | indexROT > 0 && UDI mode == MPM
4x4 | DCT/DST | HM core transform + ROT
8x8 | DCT/DST | HM core transform + ROT
16x16 | HM core transform + 2nd step MDT | HM core transform + ROT
32x32 | HM core transform + 2nd step MDT | HM core transform + ROT

## Slide 13: Tests 1…5 Summary (Test 5 is the best trade-off)
Test 5
Test 5
Test 1
Test 1
Test 2
Test 2
Test 3
Test 3
Test 4
Test 4

## Slide 14: Conclusion
Based on these test results
  2% (in average for All Intra test) and
  1% (in average for Random access test) performance improvement
we recommend HM adoption of following alternative transform design:
  DCT/DST for 4x4 and 8x8
  2nd step mode dependent transform for 16x16 and 32x32
  ROT for all block sizes restricted for MPM and no mode dependent transforms.
Only one alternative transform tool is applied for each Intra TU in this design.
No quantization part change is needed.