## Slide 1: JCTVC-D383 - CE5: coefficient coding with LCEC for large blocks

## Slide 2: Last Coding
Position of the last active coefficient last_pos is coded jointly with lev.
  The lev indicates whether the absolute value of that coefficient level is 1 (lev =0) or great than 1 (lev=1).
To code {lev, last_pos} pair for 4x4 and 8x8 blocks there are mapping tables, dependent on block type, between value of m=N∙N∙lev + last_pos and code number cn, where N is the block size.
The mapping tables are adaptive. Hence there are 2 sets of 3 tables, 32 elements each for 4x4 blocks and 2 sets of 8 tables, 128 elements each for 8x8 blocks.

## Slide 3: Last Coding (16x16, 32x32)
Assignment of the code number cn to {lev, last_pos} pair for 4x4 blocks is not modified.
For block sizes N=8,16 and 32 code number cn for {lev, last_pos} pair is calculated as follows:
if (lev ==0)
cn=((last_pos + (last_pos /(N∙N)))/(N∙N))+ last_pos;
else
if (last_pos <N)
cn= N∙N∙(last_pos +1);
else
cn = N∙N∙lev + last_pos;
lev | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
run | 0 | 1 | 2 | 3 | 0 | 4 | 5 | 6 | 1 | 7 | 8 | 9 | 2 | 10 | 11 | 12 | 3 | 13 | 14 | 15 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
cn | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31

## Slide 4: Run-Level Coding
Coefficients are coded in run mode followed by level mode.
In run mode for each coefficient pair {lev, run} is sent.
  Run is defined as the number of zero coefficients between the current nonzero coefficient at position k and the next nonzero coefficient in the reverse scanning order.
For inter/chroma blocks the mapping between {lev, run} pair and code number cn is dependent on value k:
  cn=g_auiLumaRun8x8[Min(k-1,28)][lev][run],
for intra blocks it is formula based.
The size of the g_auiLumaRun8x8 is 29∙2∙64.
  Optimized storage would require 968 bytes.

## Slide 5: Run-Level Coding (16x16, 32x32)
No changes to intra block coding. For 8x8, 16x16 and 32x32 inter blocks g_auiLumaRun8x8 table is used when k<29. Otherwise
if (lev==0)
cn=run;
else
cn=k +run+1;
Last 2 rows of table g_auiLumaRun8x8 are not used.
With some modifications to g_auiLumaRun8x8 entries we are able to store only its values for lev=0. The values for lev=1 can be obtained as follows:
cn=k + g_auiLumaRun8x8[k-1][run].
The modified table g_auiLumaRun8x8 can be stored using 434 bytes.
g_auiLumaRun8x8[4]={ // k=5
{1, 5, 3, 2, 4, 0}, // lev=0
{6, 10, 8, 7, 9, -1} // lev=1
}

## Slide 6
 | 16x16 |  |  | 32x32 |  |  | 32x32+adaptive scan |  | 
 | Intra LoCo |  |  | Intra LoCo |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -6.0 | 0.2 | -0.2 | -7.2 | 1.3 | 1.4 | -8.4 | -0.4 | -0.2
Class B | -2.4 | -1.0 | -1.3 | -2.6 | -0.6 | -0.8 | -3.4 | -1.4 | -1.7
Class C | -0.9 | -0.5 | -0.6 | -1.0 | -0.4 | -0.6 | -1.5 | -0.7 | -0.9
Class D | -1.0 | -0.5 | -0.7 | -1.1 | -0.5 | -0.7 | -1.1 | -0.5 | -0.8
Class E | -2.3 | -2.1 | -1.9 | -2.5 | -2.0 | -1.8 | -3.4 | -2.8 | -2.5
All | -2.5 | -0.7 | -0.9 | -2.9 | -0.4 | -0.5 | -3.6 | -1.1 | -1.2
Enc Time[%] | 109% |  |  | 113% |  |  | 117% |  | 
Dec Time[%] | 97% |  |  | 100% |  |  | 101% |  | 
 | Random access LoCo |  |  | Random access LoCo |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.7 | 6.9 | 5.4 | -3.6 | 11.9 | 11.9 | -4.3 | 10.7 | 10.8
Class B | -1.0 | 0.1 | -0.3 | -1.1 | 0.5 | 0.1 | -1.5 | 0.1 | -0.3
Class C | -0.5 | 0.1 | 0.1 | -0.5 | 0.2 | 0.1 | -0.7 | 0.1 | 0.0
Class D | -0.3 | 0.1 | -0.2 | -0.3 | 0.2 | -0.1 | -0.3 | 0.0 | -0.3
Class E |  |  |  |  |  |  |  |  | 
All | -1.1 | 1.7 | 1.2 | -1.4 | 3.0 | 2.8 | -1.7 | 2.6 | 2.4
Enc Time[%] | 105% |  |  | 105% |  |  | 106% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
 | Low delay LoCo |  |  | Low delay LoCo |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  |  |  |  | 
Class B | -1.0 | 1.3 | 1.1 | -1.2 | 1.7 | 1.6 | -1.2 | 1.6 | 1.5
Class C | -1.0 | 0.3 | 0.1 | -1.1 | 0.5 | 0.1 | -1.1 | 0.5 | 0.2
Class D | -0.5 | 0.1 | 0.0 | -0.5 | 0.0 | 0.2 | -0.5 | 0.5 | 0.2
Class E | -0.9 | -0.5 | 0.0 | -0.9 | 0.5 | 0.7 | -0.8 | 0.0 | 0.9
All | -0.8 | 0.4 | 0.4 | -1.0 | 0.7 | 0.7 | -0.9 | 0.7 | 0.7
Enc Time[%] | 105% |  |  | 104% |  |  | 104% |  | 
Dec Time[%] | 102% |  |  | 104% |  |  | 104% |  | 

## Slide 7
8x8 last not modified |  |  | 8x8 last modified |  | 
Intra LoCo |  |  | Intra LoCo |  | 
Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
-6.1 | 0.4 | 0.0 | -6.0 | 0.2 | -0.2
-2.5 | -0.6 | -0.9 | -2.4 | -1.0 | -1.3
-1.0 | -0.3 | -0.4 | -0.9 | -0.5 | -0.6
-1.0 | -0.5 | -0.7 | -1.0 | -0.5 | -0.7
-2.3 | -1.7 | -1.4 | -2.3 | -2.1 | -1.9
-2.6 | -0.5 | -0.7 | -2.5 | -0.7 | -0.9
Random access LoCo |  |  | Random access LoCo |  | 
Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
-2.7 | 7.1 | 5.7 | -2.7 | 6.9 | 5.4
-1.0 | 0.7 | 0.2 | -1.0 | 0.1 | -0.3
-0.4 | 0.3 | 0.3 | -0.5 | 0.1 | 0.1
-0.3 | 0.1 | 0.0 | -0.3 | 0.1 | -0.2
-1.1 | 2.0 | 1.5 | -1.1 | 1.7 | 1.2
Low delay LoCo |  |  | Low delay LoCo |  | 
Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
-1.0 | 1.8 | 2.0 | -1.0 | 1.3 | 1.1
-1.0 | 0.6 | 0.2 | -1.0 | 0.3 | 0.1
-0.5 | 0.2 | 0.3 | -0.5 | 0.1 | 0.0
-0.7 | 0.3 | 0.8 | -0.9 | -0.5 | 0.0
-0.8 | 0.8 | 0.9 | -0.8 | 0.4 | 0.4

## Slide 8
HM 2.0 | Bytes
{last_pos,lev} | 
g_auiLPTableE4 | 96
g_auiLPTableD4 | 96
g_auiLPTableE8 | 1024
g_auiLPTableD8 | 1024
{run,lev} pair | 
g_auiLumaRun8x8 | 968
g_auiLumaRunTr18x8 | 145
g_auiLumaRunTr14x4 | 75
Other | 
g_auiLastPosVlcNum | 136
g_auiVlcTable8x8Inter/g_auiVlcTable8x8Inter | 29
Sum: | 3593

## Slide 9
Proposal | Bytes
{last_pos,lev} | 
g_auiLPTableE4 | 96
g_auiLPTableD4 | 96
{run,lev} pair | 
g_auiLumaRun8x8 | 434
g_auiLumaRunTr18x8 | 145
g_auiLumaRunTr14x4 | 75
Other | 
g_auiLastPosVlcNum | 136
g_auiVlcTable8x8Inter/g_auiVlcTable8x8Intra | 29
g_auiVlcTable16x16 | 29
g_auiVlcTable16x16Inter | 29
Sum: | 1069