## Slide 1: JCTVC-E384 - LCEC coefficient coding table reduction

## Slide 2: Run-Level Coding
Coefficients are coded in run mode followed by level mode.
In run mode for each coefficient pair {lev, run} is sent.
  Run is defined as the number of zero coefficients between the current nonzero coefficient at position k and the next nonzero coefficient in the reverse scanning order.
  The lev indicates whether the absolute value of the next coefficient level is 1 (lev =0) or great than 1 (lev=1).
For inter/chroma blocks the mapping between {lev, run} pair and code number cn is dependent on value k:
  cn=g_auiLumaRun8x8[Min(k-1,28)][lev][run],
The size of the g_auiLumaRun8x8 is 29∙2∙64.
  Optimized storage would require 968 bytes.

## Slide 3: Run-Level Coding Modification
g_auiLumaRun8x8[4]={
{1, 5, 3, 2, 4, 0}, // lev=0
{6, 10, 8, 7, 9, -1} // lev=1
}
With some modifications to g_auiLumaRun8x8 entries we are able to store only its values for lev=0. The values for lev=1 can be obtained as follows:
cn=k + g_auiLumaRun8x8[k-1][run].
2 last rows of table g_auiLumaRun8x8 not used, table g_auiLumaRun8x8 is used when k<29. Otherwise
if (lev==0)
cn=run;
else
cn=k +run+1;
The modified table g_auiLumaRun8x8 can be stored using 434 bytes.

## Slide 4
BD-rate | Intra LoCo |  | 
 | Y | U | V
Class A | 0.0 | 0.0 | 0.0
Class B | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0
Class E | 0.0 | 0.0 | 0.0
All | 0.0 | 0.0 | 0.0
Enc Time[%] | 101% |  | 
Dec Time[%] | 100% |  | 
BD-rate | Random access LoCo |  | 
 | Y | U | V
Class A | 0.2 | 0.2 | 0.2
Class B | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.1 | 0.0
Class D | 0.0 | -0.1 | -0.1
Class E |  |  | 
All | 0.1 | 0.0 | 0.0
Enc Time[%] | 101% |  | 
Dec Time[%] | 99% |  | 
BD-rate | Low delay LoCo |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.1 | -0.1 | 0.4
Class C | 0.0 | 0.0 | -0.1
Class D | 0.1 | 0.0 | 0.3
Class E | 0.0 | 0.1 | 0.0
All | 0.0 | 0.0 | 0.2
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  |