## Slide 1: JCTVC-E396 Unified Motion Vector Predictor Selection for Merge and AMVP
Y. Zheng, W.-J. Chien, M. Karczewicz

## Slide 2: MVP for Merge and AMVP in HM2.0
Merge mode: check fixed neighboring blocks
AMVP: search neighboring blocks by matching refList and refIdx
Is there any unified solution for generate MVP candidate set?

## Slide 3: Proposed unified solution
Four neighboring blocks’ motion information for both merge and AMVP
A subset of neighboring blocks that checked by current merge mode
  Subset built based on partition shape and index (next slide)
Merge mode:
  Inherit motion information of the candidate that provide best RD performance
AMVP:
  Process the motion vector by scaling based on POC distance
  Use the processed motion vector as the MV prediction in AMVP

## Slide 4: Build neighboring block subset
Subset built based on partition shape and index

## Slide 5: Results (I)
HM 2.0
Common test condition defined in JCTVC-D600
Test the performance and complexity of proposed unified MVP
Configuration | BD rate saving (%) |  |  | Complexity | 
 | Y | U | V | Encoder | Decoder
HE Random Access | 0.4 | 0.2 | 0.3 | 91% | 101%
LC Random Access | 0.0 | -0.1 | 0.0 | 91% | 100%
HE Low Delay | 0.3 | 0.4 | 0.4 | 90% | 98%
LC Low Delay | 0.4 | 0.2 | 0.5 | 90% | 96%

## Slide 6: Conclusion
Unified motion vector prediction for merge and AMVP
  Subset of neighboring blocks based on partition shape and index
  Reduced the complexity by avoiding searching in AMVP
Performance
  Unified MVP:
    HE: RA 0.4% LD 0.0%; LC: RA 0.3% LD 0.4%
  Unified MVP + Ext_MVP :
    HE: RA 0.0%, LD: -0.5%; LC: RA 0.1%, LD: 0.2%
  Reduced around 10% encoder complexity
Cross verified by MediaTek
Recommend for study the unified MVP in CE

## Slide 7: Results (II)
HM 2.0
Common test condition defined in JCTVC-D600
Test the performance of proposed unified MVP and Extended MVP (JCTVC-E343)
Configuration | BD rate saving (%) |  |  | Complexity | 
 | Y | U | V | Encoder | Decoder
HE Random Access | 0.0 | -0.2 | -0.2 | 90% | 99%
LC Random Access | -0.5 | -0.6 | -0.5 | 91% | 98%
HE Low Delay | 0.1 | 0.3 | 0.3 | 91% | 98%
LC Low Delay | 0.2 | 0.1 | 0.1 | 90% | 96%

## Slide 8
Thank you!