## Slide 1
LCEC Coded Block Flag Coding Under Residual Quadtree
(JCTVC-E404)

## Slide 2: Original Coded Block Flag Coding
At CU root level
  Coded block flags for Y, U and V are coded jointly
At higher transform depth level
  CABAC — coded block flag of Y U and V components are interleaved.
  LCEC — Four flags of the same video component at the same transform depth level are jointly coded.
Blk0
Blk1
Blk2
Blk3
A coding unit

## Slide 3: Original Coded Block Flag Syntax
In the current working draft, there is transform tree syntax table and transform coefficient syntax table
In LCEC, the coded block flag syntax is located in the transform coefficient syntax table, while in CABAC it is located in the transform tree syntax table.

## Slide 4: RQT Related Syntax in HM-2.0 (Inter)
CABAC | LCEC
transform_tree (trafoDepth) { | transform_tree (trafoDepth) {
no_residual_data_flag(when at root level) | cbp_yuv_root(when at root level)
split_transform_flag( trafoDepth ) | split_transform_flag( trafoDepth )
coded_block_flag_cb(trafoDepth) | 
coded_block_flag_cr(trafoDepth ) | 
coded_block_flag_luma (when no further split) | 
… … … | … … …
} | 
CABAC | LCEC
transform_coeff (trafoDepth) { | transform_coeff (trafoDepth) {
 | cbp_luma (trafoDepth+1)
 | cbp_cb (trafoDepth+1)
 | cbp_cr (trafoDepth+1)
… … … | … … …
} | 
Transform tree syntax
Transform coefficient syntax

## Slide 5: Proposed Solution on Coded Block Flag
Move cbp syntax from transform coefficient syntax table to transform tree syntax table.
Transform split flag is jointly coded together with coded block flags.
In addition to CU root level, the joint coding of coded block flag and transform split flag is also performed at higher transform depth levels.
If only one coded block flag left in each block to be coded, the four flags at the same transform depth level are grouped and jointly coded as before.
To reduce the number of code words for the joint coding of Y, U, V and split flags, U and V are combined such that a one-bit flag is used to indicate whether both U and V are zero or not.

## Slide 6: Proposed RQT Related Syntax (Inter)
CABAC | LCEC
transform_tree (trafoDepth) { | transform_tree (trafoDepth) {
no_residual_data_flag(when at root level) | cbp_yuv_root(when at root level)
split_transform_flag( trafoDepth ) | cbp_yuv_split ( trafoDepth )
coded_block_flag_cb(trafoDepth) | 
coded_block_flag_cr(trafoDepth ) | 
coded_block_flag_luma (when no further split) | 
… … … | … … …
} | 
Transform tree syntax

## Slide 7: Test Conditions and Simulations
Test conditions
  Test 1: use default low complexity configurations
  Test 2: use default low complexity configurations, but change the maximum TU depth to 3 for both intra and inter blocks
Simulations
  Anchor : HM-2.0
  To-be-tested: proposed scheme

## Slide 8: Test Results on Coded Block Flag
Proposed method vs. HM-2.0

## Slide 9: Conclusions
The current CBP signaling clearly outperforms the original residual quadtree CBP signaling
Using the proposed scheme, coding performance can be further improved, especially in case with a maximum TU depth of 3
The syntax of CABAC and LCEC are more consistent to each other.
We recommend adopting the proposed scheme into HM and updating the working draft accordingly.