## Slide 1: LCEC Coded Block Flag Coding Under Residual Quadtree
JCTVC-E404

## Slide 2: Current Coded Block Flag Coding
At CU root level
  Coded block flags for Y, U and V are coded jointly
At higher transform depth level
  CABAC — coded block flag of Y U and V components are interleaved.
  LCEC — Four flags of the same video component at the same transform depth level are jointly coded.
  Transform split flag is signaled independently.
Blk0
Blk1
Blk2
Blk3
A coding unit

## Slide 3: RQT Related Syntax in HM-2.0
Transform tree syntax
Transform coefficient syntax
CABAC | LCEC
transform_coeff (trafoDepth) { | transform_coeff (trafoDepth) {
 | cbp_luma (trafoDepth+1)
 | cbp_cb (trafoDepth+1)
 | cbp_cr (trafoDepth+1)
… … … | … … …
} | 

## Slide 4: Proposed Solution on Coded Block Flag
Extend the joint coding of Y,U and V coded block flag to include transform split flag as well
Apply such joint coding not only at CU root level, but also at higher transform depth levels
If only one coded block flag left in each block to be coded, the four flags at the same depth level are grouped and jointly coded in the same way as in HM2.0.

## Slide 5: Considerations in VLC Table Reduction
In joint coding of Y, U, V cbf and transform split flag, U and V are combined such that a 1-bit flag is used to indicate whether both U and V are zero.
  16 codeword is reduced to 8.
A same VLC table may be shared under different cbf and transform split flag combinations.
Flag pattern (YUVS) | No. of codeword | Relative to HM2.0
8 | 15 | Same
9 | 4 | Additional
10,12 | 4 | Additional
11,13,15 | 8 | Additional
14 | 8 | Same

## Slide 6: Proposed RQT Related Syntax
CABAC | LCEC
transform_tree (trafoDepth) { | transform_tree (trafoDepth) {
no_residual_data_flag(when at root level) | cbp_yuv_split(when at root level)
split_transform_flag( trafoDepth ) | cbp_yuv_split ( trafoDepth )
coded_block_flag_cb(trafoDepth) | 
coded_block_flag_cr(trafoDepth ) | 
coded_block_flag_luma (when no further split) | 
… … … | … … …
} | 
Transform tree syntax

## Slide 7: Test Conditions and Simulations
Test conditions
  Based on that specified in CE5
Simulations
  Simulation 1: use default low complexity configurations
  Simulation 2: use default low complexity configurations, but change the maximum TU depth to 3 for both intra and inter block

## Slide 8: Results

## Slide 9: Conclusions
The proposed coding scheme improves coding performance, especially for cases with a higher TU depth.
The syntax of coded block flag and transform split flag signaling becomes more consistent between CABAC and LCEC.
We recommend adopting the proposed scheme into the next HM.