## Slide 1
Michael Horowitz
Cisco, eBrisk, TI
JCT-VC Meeting in Geneva, CH
March 16-23, 2011
Tiles

## Slide 2: Overview
Introduction
Tiles
Code Mods to HM 2.0-dev slices
Syntax
Experiments & Results
Conclusion & Recommendation

## Slide 3: Introduction
Picture partitioning introduces coding loss
Why partition a picture?
  High-level parallel processing
  MTU size matching
  Motion estimation with constrained on-chip memory
Goal: reduce coding loss due to partitioning

## Slide 4: Tiles
Vertical and horizontal boundaries partition picture into columns and rows
Boundary locations may be uniformly spaced or explicitly specified

## Slide 5: Tiles (continued)
Tile bounds may or may not break dependencies
Slice & tile boundaries may or may not coincide

## Slide 6: Mods to HM 2.0-dev-slices Source
LCU decoding order: raster scan in tiles
CU (un)availability across tile bounds
Entropy coding reset across tile bounds
PPS & SPS syntax
Notes: Emphasize simplicity

## Slide 7: Syntax (PPS and SPS)
tile_boundary_independence_idr | u(1)
uniform_spacing_idr | u(1)
if (uniform_spacing_idr == 1) { | 
column_width_minus1 | ue(v)
row_height_minus1 | ue(v)
} | 
else { | 
num_columns_minus1 | ue(v)
num_rows_minus1 | ue(v)
for (i=0; i < num_columns_minus1; i++) | 
column_width[i] | ue(v)
for (i=0; i < num_rows_minus1; i++) | 
row_height[i] | ue(v)
} | 

## Slide 8: Three Experiments
Expt. #1: MTU size matching
  Fixed number of bytes per slice
Expt. #2: High-level parallel processing
  Independent tile encoding
Expt. #3: Motion estimation with an on-chip memory constraint
  Sub-picture raster scan processing

## Slide 9: Expt. #1: MTU Size Matching
1500 bytes per slice
Columns introduced to create square-ish slices

## Slide 10: Experiment #1 Results
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -0.7 | -0.7 | -0.6 | -0.7 | -1.0 | -0.9
 | Random Access |  |  | Random Access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -0.4 | -0.3 | -0.3 | -0.4 | -0.5 | -0.5
 | Low Delay |  |  | Low Delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -0.3 | -0.4 | -0.3 | -0.3 | -0.4 | -0.5

## Slide 11: Expt. #2: High-level Parallel Processing
Several processors encode one picture
Introduce tiles (one slice per picture)

## Slide 12: Experiment #2 Results
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -1.6 | -1.7 | -1.7 | -1.7 | -2.2 | -2.1
 | Random Access |  |  | Random Access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -3.0 | -3.1 | -3.3 | -3.1 | -3.1 | -3.3
 | Low Delay |  |  | Low Delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -4.4 | -4.6 | -4.5 | -4.5 | -4.5 | -4.3
Notes: Average gain is 3.7% over all sequences and conditions. D227 results showed 2.1% gain. Actual gain somewhere between.

## Slide 13: Motion estimation with an on-chip memory constraint
Search range is adjusted for each PU based on growing search window size and the PU location
Code introduced to model on-chip memory constraint
Special very high vertical & horizontal motion sequences used
Reference frame
Current frame
2*srY+N
2*srY+N
2*srY+N
Notes: Picture resolutions increase faster than affordable on-chip memory size and DDR bandwidth

## Slide 14: Grow window within columns
Vertical search range
(SRy)
Growing search window
LCU
Column boundaries
Horizontal search range (SRx)

## Slide 15: Experiment 3 Results (N = 1)
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class FV | 12.8 | 15.5 | 15.6 | 12.8 | 15.3 | 15.2
Class FH | 0.3 | 0.3 | 0.1 | 0.3 | 0.5 | 0.5
All | 4.5 | 5.4 | 5.3 | 4.4 | 5.5 | 5.4
Enc Time[%] | 92% |  |  | 92% |  | 
Dec Time[%] | 93% |  |  | 88% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class FV | 3.5 | 3.2 | 2.8 | 3.3 | 2.4 | 2.5
Class FH | 0.1 | 0.3 | 0.1 | 0.0 | 0.1 | 0.1
All | 1.2 | 1.2 | 1.0 | 1.1 | 0.9 | 0.9
Enc Time[%] | 85% |  |  | 96% |  | 
Dec Time[%] | 81% |  |  | 100% |  | 
Reference: 1 slice/picture with unlimited search range

## Slide 16: Experiment 3 Results (N = 2)
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class FV | 3.1 | 4.9 | 4.5 | 3.4 | 4.3 | 4.0
Class FH | -0.1 | 0.1 | -0.4 | 0.0 | 0.0 | 0.0
All | 1.0 | 1.7 | 1.3 | 1.2 | 1.5 | 1.3
Enc Time[%] | 99% |  |  | 93% |  | 
Dec Time[%] | 100% |  |  | 90% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class FV | 0.2 | 0.2 | -0.1 | 0.2 | 0.3 | 0.0
Class FH | 0.0 | 0.5 | 0.5 | -0.1 | -0.3 | -0.2
All | 0.0 | 0.4 | 0.3 | 0.0 | -0.1 | -0.1
Enc Time[%] | 88% |  |  | 100% |  | 
Dec Time[%] | 83% |  |  | 108% |  | 

## Slide 17: Experiment 3 Results (N = 4)
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class FV | 0.2 | 1.7 | 0.9 | 0.4 | 0.7 | 0.6
Class FH | 0.0 | 0.2 | 0.0 | 0.2 | 0.3 | 0.1
All | 0.0 | 0.7 | 0.3 | 0.3 | 0.5 | 0.2
Enc Time[%] | 95% |  |  | 98% |  | 
Dec Time[%] | 93% |  |  | 96% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class FV | 0.0 | -0.1 | -0.1 | 0.0 | -0.1 | -0.1
Class FH | 0.1 | 0.5 | 0.3 | 0.0 | -0.2 | -0.2
All | 0.1 | 0.3 | 0.2 | 0.0 | -0.2 | -0.2
Enc Time[%] | 92% |  |  | 99% |  | 
Dec Time[%] | 88% |  |  | 102% |  | 

## Slide 18: Conclusions and Recommendation
Coding gains vs. HM 2.0 slice reference
  MTU matching -- gains from slice shape
  High-level parallel processing -- gains from slice shape and lower header overhead
  Motion search with constrained on-chip memory -- gains from effectively increasing search range
No additional computational complexity
Separates frame partitioning mechanisms
  Support for partitioning for packetization
  Support for partitioning for parallelization
Notes: We see contributions looking to localize: e.g., for adaptivity ALF and AIF, for parallel processing tiles

## Slide 19: Conclusions and Recommendation
Tiles enable…
  Compressed domain "stitching”
  Low delay parallel implementations
  Localization for adaptivity (e.g., ALF filter units)
Complementary with fine granularity slices, entropy slices, and wavefront processing
Cross-verification
  Sharp and Qualcomm
Recommendation: adopt Tiles into the HM
Notes: Special thanks to Sharp.

## Slide 20: Back-up Slides