## Slide 1: JCTVC-E409: New Results for periodic initializations for wavefront coding (JCTVC-D073)
Kiran Misra, Andrew Segall
<number>

## Slide 2: Goal (recap.)
Goal
  Provide support for wave-front processing in the HM design
  Others have proposed solutions to this problem that require transmitting LCUs out-of-order
  Here, we seek to maintain the raster-scan order within the picture
<number>

## Slide 3: Proposed Approach
Approach
  Re-initialize the entropy coder at the start of each LCU row using default HM-2.0 context tables.
  Transmit the locations of the “start of LCU row” location within the bitstream to decoder.
  Note, for the additional “start of LCU row” context initializations in forward predicted B-slice we use P-slice tables.
<number>

## Slide 4: Illustration for proposed approach
Raster-Scan Bitstream
Parallel Decoder
Decoder
Decoder
Decoder
Decoder
Decoder
Sequential Decoder
Decoder
<number>

## Slide 5: Syntax
Syntax
  LCU resets enabled in the SPS
  Location of entry points in the bit-stream signaled in the slice header (optional)
<number>

## Slide 6: Performance
Performance evaluation
  Technology integrated into HM 2.0
  Entry point at each LCU row
  Location of LCU rows written within slice header
<number>
Notes: <number>

## Slide 7: Performance
<number>
High-Efficiency:

## Slide 8: Conclusion
Conclusions
  System to enable wavefront coding/decoding
  Bit-stream maintains raster scan of LCU information
  Location information in the bitstream (better coding efficiency; requires bit-stream buffering at encoder)
  Compatible with all slicing methods under consideration
  Results: 0.3%, 2.1% and 2.6% for entry point for each LCU row (~32x parallelism for 4k)
  We propose adoption in HM
  Cross-check document: JCTVC-E470 by Orange Labs.
  Similar proposals: JCTVC-E196
<number>