## Slide 1: JCTVC-411: Enforcing the 16-bit inverse transform dynamic range
Kiran Misra, Louis Kerofsky, Andrew Segall
<number>
Notes: <number>

## Slide 2: Introduction
Introduction
  We propose a method to manage the bit-depth requirements of the transform
  Our approach
    We enforce bit-depth constraints prior to both inverse transforms
    This restricts/bounds the storage needs following the dequantization process
    This also restricts/bounds the storage needs of the transpose operation between the two transforms
<number>
Notes: <number>

## Slide 3: Proposed approach
<number>
Notes: <number>

## Slide 4: Proposed approach
<number>

## Slide 5: Advantages
Supports all tools in HM 2.0
  IBDI, TPE, all prediction modes etc.
Addresses all combinations of residue data and transform coefficients.
Improves decoder robustness to violation of dynamic range
  Due to Non-conforming encoder
  Due to bitstream error etc.
Negligible coding loss (reported on next slide)
General solution applicable to various transform designs.
<number>

## Slide 6: Results (average Y BD bitrate between +0.1% and -0.3%)
<number>
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0
Class B | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 105% |  |  | 102% |  | 
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.2 | -0.3 | 0.0 | 0.0 | -0.1
Class B | 0.0 | -0.1 | -0.1 | 0.0 | 0.0 | 0.1
Class C | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0
Class D | 0.0 | -0.1 | 0.0 | 0.0 | 0.0 | 0.1
Class E |  |  |  |  |  | 
All | 0.0 | -0.1 | -0.1 | 0.0 | 0.0 | 0.0
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 105% |  |  | 102% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.1 | -0.1 | 0.0 | 0.0 | 0.1
Class C | 0.0 | 0.0 | 0.0 | 0.0 | -0.2 | -0.2
Class D | -0.1 | 0.4 | -0.7 | 0.1 | 0.2 | 0.1
Class E | -0.3 | -0.4 | 0.7 | -0.1 | -0.4 | 0.2
All | 0.0 | 0.1 | -0.1 | 0.0 | -0.1 | 0.0
Enc Time[%] | 98% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 103% |  | 
Cross-check document:
JCTVC-E368 by Qualcomm
Common test
conditions

## Slide 7: Advantages
Generalization of this technique is possible
  Used by some of the proponents of core transform CE10 without impacting coding efficiency.
<number>

## Slide 8: Draft Text
Existing text, New text
Shiftdq = QP/6 (8-128.1)
daij = ( cij * LevelScale(nS)x(nS)[ qP%6 ][ i ][ j ] ) << ( qP%6 + trafoPrecisionExt- Shiftdq ), with i, j = 0..nS-1 (8-128.2)
dij = Clip3(- 215, 215,-1 daij ) << Shiftdq , with i, j = 0..nS-1 (8-128.3)
1. Each (horizontal) row of scaled transform coefficients dij (i, j=0..nS-1) is transformed to eij (i, j=0..nS-1) by invoking the one-dimensional transformation process as specified in subclause 8.5.4.1 to 8.5.4.4 according to the size of the transform unit nS, with the (nS)x(nS) array d as the input and the output is the (nS)x(nS) array e.
2. Each element of the array e is modified by shifting and clipping operations where the shift value depends on the transform unit size according to eij = Clip3(- 215, 215,-1 eij>> ShiftIT ) << ShiftIT where ShiftIT is determined by the block size nS as 1,0,6,7.for nS values 4,8,16,32.
3. Each (vertical) column of the resulting matrix eij (i, j=0..nS-1) is transformed to fij (i, j=0..nS-1) by invoking the one-dimensional transformation process as specified in subclause 8.5.4.1 to 8.5.4.4 according to the size of the transform unit nS, with the (nS)x(nS) array e as the input and the output is the (nS)x(nS) array f.
<number>

## Slide 9: Conclusion
We propose a method to manage the dynamic range of the inverse transform
  We observe that it is possible to enforce bit-limits after de-quantization and for transpose.
  Little impact on coding efficiency
  Benefit: we assert that this makes the video codec more accessible to architectures with hardware limitations on bus-width / memory.
We propose adoption in HM
<number>