## Slide 1: NAL unit header concept with support for bit stream scalability
JCTvc-E422
Rickard Sjöberg, Thomas rusert, Zhuangfei wu
ericsson AB

## Slide 2: background and summary
Background
  This document presents a concept for “hooks” in HEVC to support future scalability extensions
  This document is for information only, we do not propose any changes to HEVC at this time
  It is suggested to include the presented concept in the context of high-level syntax activities for the next meeting
Summary of proposed concept
  A NAL unit ID syntax element present in every NAL unit header that provides identification of layers
  Definition of a NAL unit parameter set to specify common properties of layers
  Introduction of a “representation parameter set” (RPS) that groups layers together into independently decodable representations

## Slide 3: scalability hooks for hevc
The AVC specification, especially the SVC and MVC parts, contains syntax elements to signal identification of layers
Base layer compatibility is in AVC achieved by NAL unit header extensions and prefix NAL units since the base layer specification was done without layered coding considerations
HEVC options for base layer compatible design of NAL unit headers
  Anticipate scalable scenarios and allocate syntax elements in the NAL unit headers.
    This may be difficult without actually introducing scalability
    To account for all combinations may lead to long NAL unit headers
  Introduce extensibility mechanisms into the NAL unit and slice headers
    This adds parsing complexity and could also lead to long NAL unit headers
The proposed concept
  Use indirection in the NAL unit design to signal NAL unit properties outside the NAL unit header -> NAL unit parameter sets (NPS)
    Short, fixed length NAL unit headers
    Still need syntax extensibility but in NPS instead of the NAL unit header

## Slide 4: NID and NPS
NAL unit type parameter sets (NPS) are sent in-band or out-of-band similar to SPS or PPS
  NPS may contain temporal_id, view_id etc.
  NPS should have extensibility mechanism (such as extension flags) to accommodate more identifiers as needed
Each NAL has a NAL ID syntax element.
  The NID ties each NAL with a NPS
  NID replaces the nal_ref_idc and can serve as priority_id
The following NPS could be defined in an exemplary scenario
  A first NPS for parameter sets (SPS, PPS, etc)
  A second NPS for random access slices
  One NPS for each temporal layer used in the stream

## Slide 5: extensibility
NAL unit signaling is extensible without requiring changes to the NAL unit header itself.
If new functionality that requires NAL unit level signaling is added in potential future amendments to HEVC, then only the specification of the NPS syntax structure has to be updated
The NPS syntax should be defined in an extensible way
  e.g. extension fields and/or version identifiers in the NPS syntax
NID is defined in such a way that it also reflects an abstract “priority”
  similar to nal_ref_idc and priority_id in SVC and MVC
  NID=0 is mandated to be associated with the “most important” layer etc
  A simple bit stream processor can discard NAL units of low priority considering NID values only, without having to inspect NPSs
  More advanced network elements can certainly inspect NPSs and filter out sub-streams more selectively

## Slide 6: the representation parameter set (RPS)
The RPS groups several sub-streams together into an independently decodable representation.
  each NAL unit has only a single NID
  But each sub-stream can belong to several video representations
The RPS contains a set of pointers to NPSs, i.e. a set of NIDs
  Additionally, it may contain indication of high-level properties of the represented video, such as frame rate or average bit rate
This concept of “video representations” is related to the concepts of operation points and scalability information SEI messages in AVC, and should be studied together

## Slide 7: the representation parameter set (RPS)
The sub-streams could potentially be completely separated
  This is similar to simulcast inside the video layer

## Slide 8: example
Multicast example
  WQVGA 60Hz
  1080p 60Hz
Both use 3 temporal layers
  For WQVGA there is only a 60Hz representation defined

## Slide 9: example – WQVGA 60Hz

## Slide 10: example – 1080p 30Hz