## Slide 1: JCTVC-E436 Sub-LCU QP representation
HKUST

## Slide 2: Introduction
In current HM, the delta-QP can be specified only at LCU-level. In last meeting, experts expressed that it is a bit too coarse for both subjective quality improvement and future rate control design. Therefore, one flexible approach of signaling the spatial granularity of QP change is necessary. In last meeting, it is suggested that the dQP information could be specified for each CU in [1]. In [2], by signaling minCUSizeDQP at SPS/PPS/Slice level to indicate the spatial granularity of QP change.

## Slide 3: Signaling the spatial granularity of dQP
High-level signaling of the spatial granularity of dQP
Let max_coding_unit_size be the LCU size. Given the value of lcu_qp_depth, each LCU can be divided into (2^lcu_qp_depth)^2 non-overlapped blocks. Let QPBlk_size denote the size of each block, then
QPBlk_size = max_coding_unit_size>> lcu_qp_depth
All the CUs within one block use the same quantization parameter. Hence, one dQP parameter is needed for each block to indicate the quantization parameter used.
To avoid decoding delay, the dQP is sent after cbf information in the first non-skip CU included in each block as specified in [1].

## Slide 4
Note that the proposed method is very similar to the method proposed in [2], QPBlk_size has the same meaning with minCUSizeDQP in [2]. However, the lcu_qu_depth indicates the QPBlk_size by the depth of the block size with respect to the LCU size, which we consider is an efficient representation of the minCUSizeDQP. Given the lcu_qu_depth, the minCUSizeDQP can be calculated by shift operation.

## Slide 5
LCU-level signaling of the spatial granularity of dQP
Different from the previous high-level signaling methodwhere all the LCUs have the same spatial granularity of QP change, in this approach, the lcu_qp_depth is introduced at LCU-level.
For each LCU, lcu_qp_depth is sent in the first non-skip CU in order to avoid extra bits incurred in case that all the CUs in the LCU are skip CUs.
The calculation of QPBlkSize is the same as described in (1).
The advantage of sending lcu_qp_depth at LCU level is that it can save the bits for dQP information for some LCUs. For example, if all the CUs in one LCU use the same QP, then we can just set the value of lcu_qp_depth for this LCU to 0, and only 1 dQP is sent.

## Slide 6
Examples
One LCU structure is as follows, with max_coding_block_size equals to 64 and lcu_qp_depth equals to 2.

## Slide 7
High-level signaling

## Slide 8
LCU-level signaling

## Slide 9: Conclusion
In this proposal, two possible solutions are proposed to improve the spatial granularity of QP change. To be more elaborate, the syntax element lcu_qp_depth is introduced at SPS/PPS/Slice level, or at LCU level to indicate the spatial granularity of QP change.

## Slide 10: References
[1] JCT-VC, CU adaptive quantization syntax change for better decoder pipelining, JCTVC-D258, 4th JCTVC meeting, Daegu, Jan. 2011
[2] JCT-VC, Delta QP signaling at sub-LCU level, JCTVC-D038, 4th JCTVC meeting, Daegu, Jan. 2011

## Slide 11
Thank you!