## Slide 1: JCTVC-E436: Sub-LCU QP Representation proposed by HKUST
PANG, Chao Oscar C. Au
Hong Kong Univ of Science & Technology

## Slide 2: Outline
Introduction
  Delta-QP
  Existing dQP signaling methods
Proposed sub-LCU QP representation
  High-Level signaling
  LCU-Level signaling
Conclusion

## Slide 3: Introduction
  Delta-QP
    In current HM, the delta-QP can be specified only at LCU level
    However, in Daegu meeting, experts expressed that it is a bit too coarse
  Existing dQP signaling methods
    JCTVC-D258: suggested that the dQP information could be specified for each CU and place “dQP” after the mode information of the 1st non-skipped CU
    JCTVC-D038: signaling minCUSizeDQP at SPS/PPS/Slice level to indicate the spatial granularity of QP change

## Slide 4: Signaling the spatial granularity of dQP
lcu_qp_depth
  a new syntax element lcu_qp_depth is introduced
  given the value of lcu_qp_depth, each LCU can be divided into non-overlapped quantization blocks with size of QPBlk_size by QPBlk_size
  QPBlk_size = max_coding_unit_size >> lcu_qp_depth
Notes: Note that QPBlk_size has the same meaning with minCUSizeDQP in [2]. However, the lcu_qu_depth indicates the QPBlk_size by the depth of the block size with respect to the LCU size, which we consider is an efficient representation of the minCUSizeDQP. Given the lcu_qu_depth, the minCUSizeDQP can be calculated by shift operation.

## Slide 5: Signaling the spatial granularity of dQP
  All the CUs within one block use the same quantization parameter. Hence, one dQP parameter is needed for each block to indicate the quantization parameter used
  To avoid decoding delay, the dQP is sent after cbf information in the first non-skip CU included in each block as specified in [JCTVC-D258]

## Slide 6: Signaling the spatial granularity of dQP
High-Level signaling of the spatial granularity of dQP
  lcu_qp_depth is specified at SPS/PPS/Slice-level
LCU-Level signaling of the spatial granularity of dQP
  lcu_qp_depth is specified at LCU level
  For each LCU, lcu_qp_depth is sent in the first non-skip CU
Notes: The advantage of sending lcu_qp_depth at LCU level is that it can save the bits for dQP information for some LCUs. For example, if all the CUs in one LCU use the same QP, then we can just set the value of lcu_qp_depth for this LCU to 0, and only 1 dQP is sent.

## Slide 7: Example
Examples of Two-Level Signaling
  One LCU structure
  max_coding_block_size (LCU size) equals to 64
  lcu_qp_depth equals to 2

## Slide 8: Example
(a) High-Level signaling
(b) LCU-Level signaling

## Slide 9: Conclusion
In this proposal, two possible solutions are proposed to improve the spatial granularity of QP change
  Suggest adopt into the next version of HM or adopt in new CE for further study

## Slide 10
Thank You
Q & A