## Slide 1: BoG report on the draft text for the combination of proposals JCTVC-E227, JCTVC-E338 and JCTVC-E344
JCTVC-E494
J. Sole, H. Sasai, C. Auyeung
Qualcomm, Panasonic, Sony

## Slide 2: Description
Combination of the 3 proposals:
JCTVC-E227
  Significance flag contexts of n1 case
  Context extension for 8x8 is not included (also in JCTVC-E489)
JCTVC-E338
  Parallelization of the significance map coding by explicit signaling of the last significant coefficient
  Additional contexts for significance flag for low frequencies are not included
JCTVC-E344
  Contexts for the last significant coefficient signaling
Detailed description of the algorithm is in the document

## Slide 3: Number of Contexts
 | JCTVC-E494 |  |  |  | ANCHOR |  |  | 
 | Sig | Last | coeff | total | sig | last | coeff | total
Intra only | 96 | 82 | 120 | 333 | 107 | 104 | 120 | 366
Random access | 96 | 82 | 120 | 376 | 107 | 104 | 120 | 409
Low Delay | 96 | 82 | 120 | 376 | 107 | 104 | 120 | 409
increase number of context | increase sig % | increase last % | increase coeff % | increase total %
Intra only | -10.3% | -21.2% | 0.0% | -9.0%
Random access | -10.3% | -21.2% | 0.0% | -8.1%
Low Delay | -10.3% | -21.2% | 0.0% | -8.1%

## Slide 4: Bin Count
 | Intra |  |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass
Class A | -7% | 32% | 9% | 30% | 84% | 16%
Class B | -5% | 33% | 11% | 24% | 85% | 15%
Class C | -5% | 27% | 12% | 24% | 85% | 15%
Class D | -5% | 26% | 12% | 25% | 84% | 16%
Class E | -5% | 26% | 11% | 24% | 86% | 14%
All | -5% | 29% | 11% | 26% | 85% | 15%
 | Random access |  |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass
Class A | -4% | 29% | 8% | 18% | 85% | 14%
Class B | -2% | 28% | 9% | 16% | 87% | 13%
Class C | -2% | 22% | 10% | 15% | 86% | 13%
Class D | -2% | 22% | 10% | 15% | 86% | 13%
Class E |  |  |  |  |  | 
All | -2% | 25% | 9% | 16% | 86% | 13%
 | Low delay |  |  |  |  | 
 | increase in bin % | % sig | % last | % coeff | % reg | % bypass
Class A |  |  |  |  |  | 
Class B | 0% | 29% | 10% | 13% | 88% | 11%
Class C | -1% | 25% | 10% | 13% | 87% | 12%
Class D | -1% | 25% | 10% | 12% | 88% | 12%
Class E | 0% | 22% | 8% | 8% | 89% | 9%
All | 0% | 26% | 10% | 12% | 88% | 11%

## Slide 5: BD-rate
BD-rate | Intra HE |  |  | Random access HE |  |  | Low delay HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.1 | 0.0 | -0.1 | 0.0 | -0.4 | -0.5 |  |  | 
Class B | 0.0 | 0.3 | 0.4 | 0.0 | -0.1 | -0.3 | -0.1 | -0.6 | -1.0
Class C | 0.2 | 0.4 | 0.3 | 0.0 | -0.3 | -0.4 | 0.1 | -0.8 | -0.9
Class D | 0.0 | 0.4 | 0.4 | 0.0 | -0.5 | -0.6 | -0.1 | -1.6 | -2.1
Class E | 0.2 | 0.2 | 0.3 |  |  |  | -0.1 | -2.3 | -0.5
All | 0.0 | 0.3 | 0.3 | 0.0 | -0.3 | -0.4 | -0.1 | -1.2 | -1.2
Enc T[%] | 98% |  |  | 98% |  |  | 97% |  | 
Dec T[%] | 98% |  |  | 96% |  |  | 100% |  |