## Slide 1: Scalable enhancement requirements for HEVC and AVC (m19968) (96th / E Meeting, Geneva) Ajay Luthra

## Slide 2: Background
“Convergence” of computer networks & platforms, digital TV networks & platforms, and telephone networks & platforms
  Widely discussed but did not happen, however
  It is beginning to happen now
    Mobile TVs
      Smart phones (e.g. Droid), Tablets (e.g. Xoom), Mobile Devices
    Commercialization of Internet Video
      Streaming and File Download
Instead of looking only in the rear-view mirror, let us also look ahead

## Slide 3: Environment
Homogeneous => Heterogeneous
Clients
  STB, TV
  Plus, Smart Phones (Droid), Tablets (Xoom)
Networks
  Mainly (Cable, Satellite, Telco) with fixed QoS
  Increasing use of internet without fixed QoS
    20% of Internet => 80%
  Wired
    And Wireless (Cellular, WiFi … )

## Slide 4: Impact
What was not used in the past may be needed in the future
Solutions that were great in the past may not be so great going forward
  Increased need for Scalability
    Scalability vs Transcoding
  Increased need for combination of scalabilities
Revisit scalability requirements and do not just copy them from the past

## Slide 5: List, so far
Temporal Scalability
Spatial Resolution Scalability
Quantization Noise (sometimes also called SNR) Scalability
Sharpness/Frequency Scalability
Robustness Scalability
Fine Granular Scalability
View Scalability
Frame Compatible Scalability for 3D TV
Bit Depth Scalability
Chroma Scalability
Picture Aspect Ratio Scalability
Interlace-to-Progressive Scalability
Others?

## Slide 6: Example of new possible needs
Spatial scalability
  1:1.5 ratio is appearing more frequently than 1:2
    HVGA => VGA, VGA=>720p, 720p => 1080p
Combination of Scalability tools
  Spatial and Temporal
    Base Layer HVGA (480x320) at e.g. 20 fps, enhancement layer(s) VGA (640x480) at 30 (25) fps to 720p30
    Base layer 720p30, enhancement to 720p60 and 1080p60
  And, Quantization (SNR)
    VGA at 1 Mbps to VGA at 2 Mbps
Design the syntax to allow various combinations

## Slide 7: Example of new possible needs
Devices with mixed aspect ratios
Wide range of variation in Network capacity is becoming real (Fine Granular Control may be needed)
View Scalability
  In combination of spatial and temporal resolution, e.g
    Base (half resolution per eye Stereoscopic) to Full Resolution per eye
    Base layer 1080p24 per eye (1080p48), enhancement 1080p60 per (1080p120)
    Base layer half res 720p60, enhancement to full res 720p120 to 1080p120
  Increasingly, larger number of movies converted from 2D to 3D
  Same may also be done for commercials as well as TV programs
    Excellent depth maps are being generated and may possibly be made available for compression

## Slide 8: Recommendation
Set up an adhoc group to flesh out the requirements
  Beyond the traditional (motherhood and apple pie) requirements – random access, low delay, complexity …
  Use cases
  Syntax elements and coding tools