## Slide 1: JCTVC-F026 Overview
A. Tabatabai, K. Chono, M. Budagavi, R. Joshi, A. Segall and H. Yu
July 12 2011
CE6: Intra Prediction Improvements Summary Report

## Slide 2: Intra Prediction Improvement CEs
<number>
JCTVC-F91
CE6.a: Block based Intra Prediction
CE6.b: Short Distance Intra Prediction (SDIP) Harmonization
CE6.c: Differential Coding of Intra Mode (DCIM)
CE6.d: Parallel Intra Coding
CE6.e: Intra Smoothing

## Slide 3: CE6.a: Block-based Intra Prediction
<number>
Intra prediction modes (IPM) 6 and 9 in current HM predict same texture zone
  Leads to a unified Intra prediction for specific texture direction of 45 degrees
Bi-directional UDI (BUDI) mode unifies IPM 6 and 9 by using linear interpolation from above and left reference samples
  both reference pixels from main and side arrays can be exploited to improve prediction accuracy
JCTVC-F91

## Slide 4: CE6.a: Bi-predictive Uni-Directional Intra (BUDI) Mode - Test List
<number>
JCTVC-F91
Core Experiments | Technology | Proponent(s) | Cross-checker(s)
CE6.a.1 | LUT-based BUDI for HM and HM-SDIP | HiSilicon, Huawei (JCTVC-F509) | NEC (JCTVC-F348) I2R (JCTVC-F151)
CE6.a.2 | LUT-free BUDI for HM and HM-SDIP | HiSilicon, Huawei (JCTVC-F509) | NEC (JCTVC-F348) I2R (JCTVC-F151)
CE6.a.3 | LUT-based different combinations of Intra mode signaling for (DC,BUDI,Planar)=(2,6,9). | HiSilicon, Huawei (JCTVC-F509) | NEC (JCTVC-F348) I2R (JCTVC-F151)
CE6.a.4 | LUT-free different combinations of Intra mode signaling for (DC,BUDI,Planar)=(2,6,9). | HiSilicon, Huawei (JCTVC-F509) | NEC (JCTVC-F348) I2R (JCTVC-F151)
CE6.a.5 | LUT-based different combinations of Intra mode signaling for (DC,BUDI,Planar)=(9,6,2) | HiSilicon, Huawei (JCTVC-F509) | NEC (JCTVC-F348) I2R (JCTVC-F151)
CE6.a.6 | LUT-free different combinations of Intra mode signaling for (DC,BUDI,Planar)=(9,6,2) | HiSilicon, Huawei (JCTVC-F509) | I2R (JCTVC-F151)
CE6.a.7 | LUT-based different combinations of Intra mode signaling for (DC,BUDI,Planar)=(2,9,6) | HiSilicon, Huawei (JCTVC-F509) | USTC/MS (JCTVC-F204)
CE6.a.8 | LUT-free different combinations of Intra mode signaling for (DC,BUDI,Planar)=(2,9,6) | HiSilicon, Huawei (JCTVC-F509) | USTC/MS (JCTVC-F204)
CE6.a.9 | LUT-based different combinations of Intra mode signaling for (DC,BUDI,Planar)=(6,9,2) | HiSilicon, Huawei (JCTVC-F509) | Qualcomm (JCTVC-F565)
CE6.a.10 | LUT-free different combinations of Intra mode signaling for (DC,BUDI,Planar)=(6,9,2) | HiSilicon, Huawei (JCTVC-F509) | Qualcomm (JCTVC-F565)

## Slide 5: CE6.a Test Results
<number>
JCTVC-F91
Note: Y-BD Rate is graphically presented
CE6.a Method combination | HM-HE | HM-LC | HM-SDIP-HE | HM-SDIP-LC
1) a.1 (LUT) BUDI | -0.17 | -0.18 | -0.19 | -0.2
2) a.2 (No LUT) BUDI | -0.13 | -0.14 | -0.14 | -0.15
3) a.3 (LUT) DC BUDI Planar | -0.17 | -0.23 | -0.15 | -0.2
4) a.4 (No LUT) DC BUDI Planar | -0.12 | -0.19 | -0.1 | -0.15
5) a.5 (LUT) DC BUDI Planar | -0.23 | -0.28 |  | 
6) a.6 (No LUT) DC BUDI Planar | -0.19 | -0.24 |  | 
7) a.7 (LUT) DC BUDI Planar | -0.16 | -0.21 |  | 
8) a.8 (No LUT) DC BUDI Planar | -0.12 | -0.18 |  | 
9) a.9 (LUT) DC BUDI Planar | -0.23 | -0.27 |  | 
10) a.10 (No LUT) DC BUDI Planar | -0.18 | -0.23 |  | 

## Slide 6: CE6.b: Short Distance Intra Prediction (SDIP) Harmonization
<number>
SDIP
  divides NxN block into lines or non-square blocks
    one CU smaller than 64x64 can be partitioned
  reduces distance of predicted pixel and its reference pixels
SDIP is harmonized with
  RQT syntax, MDDS, Planar, Deblocking Filter, DC prediction filter, MDIS
JCTVC-F91
8×8 CUs
8×2 SDIP PU
Current edge
Deblocking Filter and decision support region
Deblocking Filter and decision support region containing edge from 8×2 SDIP PU
SDIP partitioning
UDI prediction for 2x8

## Slide 7: CE6.b: Short Distance Intra Prediction (SDIP) Harmonization (JCTVC-E278) – Test List (1)
<number>
JCTVC-F91
Core Experiments | Technology | Proponent(s) | Cross-checker(s)
CE6.b | Comparison between SDIP and HM3.0 Anchor |  | 
CE6.b.1 | Test1 RQT Case1: Harmonization of SDIP and RQT Syntax | Tsinghua, USTC, HiSilicon, Microsoft, Huawei (JCTVC-F533) | NEC (JCTVC-F349) NEC / Motorola Mobility (JCTVC-F684) Sony (JCTVC-F308)
CE.6.b.2 | Test1 RQT Case2: Harmonization of SDIP and two-depth RQT of 8x32/32x8 | Tsinghua, USTC, HiSilicon, Microsoft, Huawei (JCTVC-F533) | NEC (JCTVC-F349) Sony (JCTVC-F308)
CE6.b.3 | Test2 DST Case1: Harmonization of SDIP and Mode-Dependent DCT/DST: SDIP=0, MDDT=0 | Huawei, HiSilicon (JCTVC-F506) | TI (?) Orange Lab (JCTVC-F139)
CE.6.b.4 | Test2 DST Case2: Harmonization of SDIP and Mode-Dependent DCT/DST: SDIP=1, MDDT=0 | Huawei, HiSilicon (JCTVC-F506) | NEC (JCTVC-F349) BBC (JCTVC-F630)
CE6.b.5 | Test2 DST Case3: Harmonization of SDIP and Mode-Dependent DCT/DST: SDIP=1, (MDDT=1 & SDIP_MDDT=1) | Huawei, HiSilicon (JCTVC-F506) | TI (JCTVC-F239) I2R (JCTVC-F155)
CE.6.b.6 | Test3 MDCS: Harmonization of SDIP and MDCS: SDIP=1, (MDCS=1&SDIP_MDCS=0) | USTC, Microsoft (JCTVC-F197) | NEC (JCTVC-F349) Sony (JCTVC-F309) INRIA (JCTVC-F231)
CE6.b.7 | Test4 LM: Harmonization of LM mode and the chroma prediction in SDIP: SDIP=1 | USTC, Microsoft (JCTVC-F196) | Sharp (JCTVC-F392) LGE (JCTVC-F195)
CE.6.b.8 | Test5 MDIS Case1: Harmonization of SDIP and MDIS: SDIP=0, MDIS=0 | Santa Clara University, HiSilicon (JCTVC-F336) | Qualcomm (JCTVC-F557)
CE6.b.9 | Test5 MDIS Case2: Harmonization of SDIP and MDIS: SDIP=1, MDIS=0 | Santa Clara University, HiSilicon (JCTVC-F336) | Qualcomm (JCTVC-F557)

## Slide 8: CE6.b: Short Distance Intra Prediction (SDIP) Harmonization (JCTVC-E278) – Test List (2)
<number>
JCTVC-F91
Core Experiments | Technology | Proponent(s) | Cross-checker(s)
CE.6.b.10 | Test5 MDIS Case3: Harmonization of SDIP and MDIS: SDIP=1, (MDIS=1&SDIP_MDIS=1) | Santa Clara University, HiSilicon (JCTVC-F336) | NEC (JCTVC-F349)
CE.6.b.10.1 | Test5 MDIS Qualcomm Test Case | Qualcomm (JCTVC-F556) | Ghent University (JCTVC-F411)
CE6.b.11 | Test6 Planar Case1: Harmonization of SDIP and PLANAR: SDIP=0, PLANAR=0 | HiSilicon, Tsinghua (JCTVC-F518) | Canon (JCTVC-F489)
CE.6.b.12 | Test6 Planar Case2: Harmonization of SDIP and PLANAR: SDIP=1, PLANAR=0 | HiSilicon, Tsinghua (JCTVC-F518) | Canon (JCTVC-F489)
CE6.b.13 | Test6 Planar Case3: Harmonization of SDIP and PLANAR: SDIP=1, (PLANAR=1&SDIP_PLANAR=1) | HiSilicon, Tsinghua (JCTVC-F518) | Canon (JCTVC-F489)
CE.6.b.14 | Test7 LF Case1 : Harmonization of SDIP and deblocking filter: SDIP=0, deblocking filter=0 | Tsinghua, USTC, HiSilicon, Microsoft, Huawei (JCTVC-F536) | Qualcomm (JCTVC-F557)
CE6.b.15 | Test7 LF Case2 : Harmonization of SDIP and deblocking filter: SDIP=1, deblocking filter=0 | Tsinghua, USTC, HiSilicon, Microsoft, Huawei (JCTVC-F536) | Qualcomm (JCTVC-F557) NEC
CE.6.b.16 | Test7 LF Case3 : Harmonization of SDIP and deblocking filter: SDIP=1, (deblocking filter=1&SDIP_deblocking filter=1) | Tsinghua, USTC, HiSilicon, Microsoft, Huawei (JCTVC-F536) | NEC (JCTVC-F349)
CE6.b.16.1 | Test 7: Harmonization of SDIP and deblocking filter | Qualcomm (JCTVC-F556) | Mediatek (JCTVC-F437)
CE6.b.17 | Test8 DC prediction filtering Case1: Harmonization of SDIP and DC prediction filtering: SDIP=0, DC prediction filter = 0 | Qualcomm (JCTVC-F556) | HiSilicon (JCTVC-F539 )
CE.6.b.18 | Test8 DC prediction filtering Case2: Harmonization of SDIP and DC prediction filtering: SDIP=1, DC prediction filter = 0 | Qualcomm (JCTVC-F556) | HiSilicon (JCTVC-F539)

## Slide 9: CE6.b Test Results
<number>
JCTVC-F91
CE6.b Method combination | Intra HE | Intra LC
1) b: Comparison between SDIP and HM3.0 Anchor | -1.4 | -2.1
2) b.1: Test1, Case1 | -0.03 | -0.24
3) b.1: Test1, Case2 | -0.16 | -0.43
4) b.1: Test2, Case1 MDDT | -0.79 | -1.09
5) b.1: Test2, Case2 | -0.59 | -0.69
6) b.1: Test2, Case3 | -0.03 | -0.09
7) b.1: Test3 MDCS | -0.08 | -0.08
8) b.1: Test4, LGE test case LM | -0.02 | -0.02
9) b.1: Test4, MS test case | -0.06 | -0.1
10) b.1: Test5, HiSilicon, Case1 MDIS | -0.16 | -0.25
11) b.1: Test5, HiSilicon, Case2 | -0.18 | -0.28
12) b.1: Test5, HiSilicon, Case3 | 0 | -0.01
13) b.1: Test5, Qualcomm Case | -0.01 | -0.01
14) b.1: Test6, Case1 Planar | -0.6 | -0.5
15) b.1: Test6, Case2 | -0.6 | -0.5
16) b.1: Test6, Case3 | -0.1 | -0.1
17) b.1: Test7, Tsinghua, Case1 Deblocking | -1.1 | 0.6
18) b.1: Test7, Tsinghua, Case2 | -1.1 | 0.7
19) b.1: Test7, Tsinghua, Case3 | 0.12 | 0.12
20) b.1: Test7, Qualcomm test | -0.08 | -0.12
21) b.1: Test8, Case1 DC Prediction | -0.09 | -0.14
22) b.1: Test8, Case2 | -0.15 | -0.19
Note: Y-BD Rate is graphically presented
Red-colored data: In the report, it says positive means gain. Is it so?

## Slide 10: CE6.c: Differentia Coding of Intra Mode (DCIM)
<number>
JCTVC-F91
DCIM Key Features
HM Proposal
Enhances current UIP
Efficient signaling of directional information
Significant Coding & Visual Improvements

## Slide 11: CE6.c: Differential Coding of Intra Modes (DCIM) JCTVC-E318 – Test List
<number>
JCTVC-F91
Core Experiments | Technology | Proponent(s) | Cross-checker(s)
CE6.c | DCIM | Sony, Sharp, Toshiba, Panasonic (JCTVC-F566) | TI (JCTVC-F240, JCTVC-F413) HiSilicon (JCTVC-F534)
CE6.c Method combination | Intra HE | Intra LC
1) c: Case1 | -0.8 | -0.7
2) c: Case2 | -0.4 | -0.4
3) c: Case3 | -0.7 | -0.5
4) c: Case4 | -0.4 | -0.1
Note: Y-BD Rate is graphically presented

## Slide 12: CE6.d: Parallel Intra Coding
<number>
Parallel prediction unit (PPU) defines a group of pixels intra-coded in a parallel fashion
Parallel intra prediction has three steps
  Partitions PPU into two sets
    Predicting 1st set blocks (shaded blocks) in parallel using PPU block neighbors
    Predicting 2nd set blocks (white blocks) in parallel using PPU block neighbors and also neighbors from 1st set blocks
  Three types of partitions tested
    Checker board, Stripe, 8x8 prediction with 4x4 residuals
JCTVC-F91
Fig. 1 - Parallel Prediction with checker board partition for PPU of 8x8
Fig. 2 - Parallel Prediction with stripe partition for PPU of 8x8
Fig. 3 - Parallel Prediction with stripe partition for PPU of 8x8

## Slide 13: CE6.d: Parallel Intra Coding – Test List
<number>
JCTVC-F91
Core Experiments | Technology | Proponent(s) | Cross-checker(s)
CE6.d | LUT-based BUDI for HM and HM-SDIP | SHARP (JCTVC-F605) | Toshiba (JCTVC-F328) Qualcomm (JCTVC-F583) ETRI (JCTVC-F628)
CE6.d Method combination | Intra HE | Intra LC | RA HE | RA LC | LD HE | LD LC
1) d: Parallel Intra with Stripe Partition | 1.3 | 1.5 | 0.5 | 0.6 | 0.2 | 0.2
2) d: Checker board | 1.5 | 1.8 |  |  |  | 
3) d: 8x8 prediction with 4x4 residuals | 3.9 | 5.3 |  |  |  | 
Note: Y-BD Rate is graphically presented

## Slide 14: CE6.e: Intra Smoothing
<number>
Qualcomm’s Mode-dependent intra smoothing (MDIS) scheme
  determines smoothing filter type according to prediction unit (PU) size and intra prediction mode
  MDIS orders intra prediction modes in a hierarchy mapped to PU size.
JCTVC-F91
IS filtering is indicated with a marker as a function of intra prediction direction and PU size. When the marker is absent, no filtering is applied.

## Slide 15: CE6.e: Intra Smoothing, JCTVC-D282, Qualcomm – Test List
<number>
JCTVC-F91
Core Experiments | Technology | Proponent(s) | Cross-checker(s)
CE6.e | JCTVC-D282: Adaptive intra smoothing, Qualcomm | Qualcomm (JCTVC-F126) | Mitsubishi (JCTVC-F171) Ghent University (JCTVC-F411)
CE6.e Method combination | Intra HE | Intra LC
1) e: Modified MDIS | -0.1 | -0.1
2) e: Class C BasketBallDrill | -0.9 | -1.8
3) e: Modified MDIS compared with HM3 Anchor+MDIS disabled | -0.3 | -0.4

## Slide 16
Notes: <number>