## Slide 1
<number>
<number>
JCTVC-F041 (CE8): Results on Combination of TI’s 7x5 Modified Diamond and eBrisk’s Cross 11x5 Shapes
Michael Horowitz, eBrisk Video
6th JCTVC Meeting in Torino
14-22 July 2011

## Slide 2: Proposed Technique
<number>
<number>
TI’s 7x5 Modified Diamond Shape
eBrisk’s Cross 11x5 Shape
Notes: Context: last meeting MD 7x5 & 19x5 cross in context of HM 2.0 adopted into HM SW for CE testing. We merged these shapes into HM 3.0 and released ACDS.
F041 is a modified ACDS where 19x5 cross -> 11x5
<number>

## Slide 3: Proposed ALF Algorithm
<number>
<number>
Notes: The first 1-pass is really 2x1 pass so there are 15 passes.
<number>

## Slide 4: Simulation Results (multi-pass)
<number>
 | Low Delay (P) HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.51 | 0.03 | -0.01
Class C | 0.11 | -0.12 | 0.07
Class D | 0.02 | 0.39 | -0.11
Class E | 0.54 | 0.17 | 0.08
All | 0.29 | 0.11 | 0.00
Enc Time[%] | 100.94% |  | 
Dec Time[%] | 95.26% |  | 
Notes: Small loss, 5% decrease in decoder execution time due to fewer coefficients … Worst case computational complexity is reduced even more
Gains are more relevant for SW implementations
WHAT IS THE ANCHOR HERE?
<number>

## Slide 5: Simulation Results (multi-pass)
<number>
 | Low Delay (B) HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.53 | 0.05 | 0.36
Class C | 0.18 | -0.10 | -0.18
Class D | 0.16 | -0.21 | -0.21
Class E | 0.75 | 0.58 | -0.23
All | 0.39 | 0.05 | -0.03
Enc Time[%] | 100.69% (100.74%) |  | 
Dec Time[%] | 96.02% (94.73 %) |  | 

## Slide 6: Simulation Results (multi-pass)
<number>
 | Random Access HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.41 | -0.30 | 0.16
Class B | 0.25 | 0.03 | 0.03
Class C | 0.04 | 0.04 | -0.01
Class D | 0.08 | 0.06 | 0.05
Class E |  |  | 
All | 0.20 | -0.04 | 0.06
Enc Time[%] | 101.07% (103.38%) |  | 
Dec Time[%] | 98.43% (96.75%) |  | 

## Slide 7: Simulation Results (multi-pass)
<number>
 | Intra Only HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.42 | -0.02 | -0.02
Class B | 0.13 | -0.05 | -0.05
Class C | 0.07 | -0.06 | -0.06
Class D | 0.09 | -0.06 | -0.06
Class E | 0.43 | -1.00 | -0.10
All | 0.22 | -0.05 | -0.05
Enc Time[%] | 102.38% (105.89%) |  | 
Dec Time[%] | 93.36% (93.51%) |  | 

## Slide 8: Complexity Analysis (multi-pass)
<number>
Configuration | Enc Time | Dec Time
Low Delay (P) HE | 100.94% | 95.26%
Low Delay (B) HE | 100.69% | 96.02%
Random Access HE | 101.07% | 98.43%
Intra Only HE | 102.38% | 93.36%
Average Encoder/Decoder Time
Worst-Case Decoder Time
Configuration | WC Dec Time (class D) | WC Dec Time (class C)
Low Delay (P) HE | 89% | 90%
Low Delay (B) HE | 91% | 92%
Random Access HE | 92% | 92%
Intra Only HE | 92% | 91%
Notes: <number>

## Slide 9
Summary
Average decoder complexity reduced by ~4.5% relative to HM 3.1.
Average coding efficiency loss of 0.27%
Vertical filter size reduced to 5 lines
Worst-case decoder complexity reduced by ~9% relative to HM 3.1.
When combined with AIF, the efficiency loss due to the less complex ALF filters goes to zero.
ALF (MD7x5+C11x5) |  |  | ALF + AIF |  | 
Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
0.27 | 0.02 | -0.01 | -0.01 | -0.14 | -0.26
 | ALF (MD7x5+C11x5) | ALF + AIF
Dec Time[%] | 96% (95%) | 96%
WC Dec Time[%] | 91% | 91%

## Slide 10: Backup Slides
<number>

## Slide 11: Consider ALF + AIF
Hypothesis: Combination ALF+AIF offers better complexity-coding performance
<number>

## Slide 12: Simulation Results (AIF + ALF)
<number>
 | Low Delay (P) HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.18 | -0.33 | -0.61
Class C | -0.35 | -0.27 | -0.59
Class D | -0.38 | -0.19 | -0.14
Class E | -0.30 | -0.18 | -0.71
All | -0.18 | -0.26 | -0.52
Enc Time[%] | 107% |  | 
Dec Time[%] | 95% |  | 

## Slide 13: Simulation Results (AIF + ALF)
<number>
 | Low Delay (B) HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0.27 | 0.00 | -0.09
Class C | -0.05 | -0.10 | -0.22
Class D | 0.03 | 0.17 | 0.12
Class E | -0.01 | 0.10 | -0.17
All | 0.08 | 0.03 | -0.09
Enc Time[%] | 106% |  | 
Dec Time[%] | 95% |  | 

## Slide 14: Simulation Results (AIF + ALF)
<number>
 | Random Access HE |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.15 | -0.75 | -0.35
Class B | 0.24 | -0.08 | -0.12
Class C | 0.04 | 0.10 | 0.03
Class D | 0.10 | 0.02 | -0.07
Class E |  |  | 
All | 0.06 | -0.18 | -0.17
Enc Time[%] | 104% |  | 
Dec Time[%] | 97% |  | 

## Slide 15: Complexity Analysis (AIF + ALF)
<number>
Configuration | Enc Time | Dec Time
Low Delay (P) HE | 107% | 95%
Low Delay (B) HE | 106% | 95%
Random Access HE | 104% | 97%
Average Encoder/Decoder Time
Worst-Case Decoder Time
Configuration | WC Dec Time (class D) | WC Dec Time (class C)
Low Delay (P) HE | 89% | 90%
Low Delay (B) HE | 91% | 92%
Random Access HE | 92% | 92%