## Slide 1: Complexity Assessment Methodology
Daniele Alfonso, STMicroelectronics
Justin Ridge, Nokia Research Center
Xing Wen, Hong Kong Univ. of Science and Technology
JCTVC-F043

## Slide 2: Problem statement
This contribution addresses the first two mandates of the Complexity Assessment AhG, which are
  Summarize and evaluate the various complexity assessment methods with regard to:
    computational complexity,
    parallelism,
    memory bandwidth,
    memory capacity,
    dynamic range requirements,
    any other aspects of complexity identified as being of interest.
  Develop and propose a set of general measurement metrics.

## Slide 3: Basic definitions
System = composition of interacting elements with the purpose of applying a process in order to produce a certain result or solve a certain problem.
Complexity = amount of resources consumed to realize and operate the system.
SYSTEM
X
Y=f(X)
PROCESS

## Slide 4: Resources
Resources consumed statically: resources needed to realize the system, like silicon footprint, memory size, number of elementary processing units, et cetera.
Resources consumed dynamically: resources needed to operate the system, in particular computation (amount of elementary operations performed per time unit) and communication (amount of data transferred per time unit).
Notes: <number>

## Slide 5: Remark
The same problem can be solved with several different systems, each one characterized by a different complexity.
For an exhaustive complexity assessment we need to consider several different implementations.
HEVC
encoder
HEVC
encoder
HEVC
encoder
HEVC
encoder(s)
HEVC
encoding
HEVC
encoder
HEVC
encoder
HEVC
encoder
HEVC
decoder(s)
HEVC
decoding
Scope of
standardization
Scope of
complexity assessment

## Slide 6: Three Level Complexity Assessment
Abstract
Architecture
GP CPU
Architecture
Technology
Abstract level
Software level
Hardware level
Software model
Algorithmic model
Hardware model

## Slide 7: Abstract modeling
Algorithmic model executed over abstract architecture.
Complexity assessment performed by algorithmic analysis:
  Elementary arithmetic operations count
  Storage memory requirements
  Elementary data transfer operations count
Further complexity dimensions
  Number of processing stages, to understand pipelining possibilities.
  Data dependency analysis, to understand possibility of data parallelization.
Remark: average, worst-case and best-case analysis recommended.
Abstract
Architecture
Abstract level
Algorithmic model

## Slide 8: Software modeling
Software model (HM) executed over general-purpose CPU architecture (e.g. Intel or ARM).
Complexity assessment by runtime measures
  Computation resources: HM execution user time or CPU clock cycles.
  Communication resources: HM bandwidth.
  Memory resources: HM memory allocated at runtime
Deeper complexity assessment can be done by profiling.
GP CPU
Architecture
Software level
Software model

## Slide 9: Hardware Modeling
Hardware Description Language implementation over technology library.
Complexity assessment by hardware performance:
  silicon area, or equivalently the number of logic gates or standard cells in the given technology
  Clock frequency
  Throughput
  Latency
Technology
Hardware level
Hardware model

## Slide 10: Conclusions
“Complexity” = amount of resources consumed to realize and operate a system.
Complexity assessment methodology based on three kinds of system modeling: algorithmic, software and hardware.
The Complexity Assessment AhG recommends considering the proposed methodology as JCT-VC project management practice for the HEVC standardization project.