## Slide 1: Unified Scaling with Adaptive Offset for Reference Frame Compression
Dzung Hoang JCTVC-F075
July 2011
Notes: <number>

## Slide 2: Summary
We propose two variants of reference frame compression (RFC) to:
  code and decode native N-bit video using same frame memory as 8-bit video, or
  code and decode video using N-bit IBDI using same frame memory as 8-bit video
  8 < N < 16
First variant is Unified Scaling with Adaptive Offset (USAO) previously proposed in JCTVC-D035, which is based upon Toshiba’s Adaptive Scaling JCTVC-C075.
Second variant adds DPCM coding and is referred to as USAO-D. Limitation is N < 15.
USAO cross-checked by MediaTek in JCTVC-F079.
USAO-D cross-checked by Santa Clara University in JCTVC-E463.

## Slide 3: Unified Scaling with Adaptive Offset
Introduced in JCTVC-D035
  Based upon Toshiba JCTVC-C075
  Remove fixed rounding
  Encoder computes scaling factor S
  Encoder computes reconstruction offset as the average of quantizer error and transmits offset using S bits
  Encoder computes and transmits the block minimum value (spatial predictor) using N-S bits

## Slide 4: USAO Storage Format
Store quantizer scale S using 2 to 4 bits, depends on N.
Store minimum and offset using total of N bits.
Indicate position of minimum sample using 4 bits.
Subtract minimum sample value and quantize (right shift by S) to form residuals.
Store 15 residuals using 7 bits.
u(ceil(log2(N-6))); /* S */
u(N-S); /* M */
u(S); /* offset */
u(4); /* M_index */
for (i=0; i<15; i++) u(8); /* P residual array */

## Slide 5: USAO Bit Count
N | bits used per 4×4 block
9 | 120
10 | 121
11 | 123
12 | 124
13 | 125
14 | 126
15 | 128

## Slide 6: Computation of Offset
Least squares method yields optimal offset to be average of error.
Empirical data suggests using 7 as rounding constant instead of 8 given in JCTVC-D035:
  offset = (sum(error) + 7) / 16
  Exhaustive search on offset compared to above and did not find any differences.

## Slide 7: USAO with DPCM
With USAO, scale factor S decided using block minimum and maximum so that residual can always be coded using 7 bits.
For smoothly varying block content, above decision can be too conservative.
Idea: use DPCM to signal delta between successive pixels. Might be able to use lower S, but not guaranteed.
Requires a scan pattern and delta coding:
  scan start at minimum pixel and cyclic scan
  use adaptive excess-N to code delta using 7 bits

## Slide 8: Cyclic Scan Pattern
Use cyclic scan pattern so that every delta is computed on adjacent pixels when we start with minimum pixel.

## Slide 9: Adaptive Excess-N
Idea: make best use of 7 bits to code differences when we know block minimum and maximum.
  cur_pel = (sample at current scan position) >> S
  prev_pel = (sample at previous scan position) >> S
  min_delta = −64
  if (coded_min − prev_ pel > −64)
    min_delta = coded_min − prev_pel
  else if (coded_max − prev_ pel < 63)
    min_delta = coded_max − prev_pel − 127
  delta = (cur_pel − prev_pel − min_delta)

## Slide 10: Coding Range for Excess-N
Block minimum already coded, so we additionally need to code block maximum.
Code range = max – min using fixed number of bits k (depends upon N). Code k-MSB of range.
Reserve range=0 to flag not to use DPCM.
N | bits for S | k | N | bits for S | k
9 | 2 | 8 | 13 | 3 | 3
10 | 2 | 7 | 14 | 3 | 2
11 | 3 | 5 | 15 | 4 | 0
12 | 3 | 4 |  |  | 

## Slide 11: USAO-D Storage Format
u(k) /* dpcm_flag_range */
u( ceil(log2(N−6)) ) /* S */
u(N−S) /* M */
u(S) /* offset */
u(4) /* M_index */
for (i=0; i<15; i++) u(7) /* P array excluding M */

## Slide 12: USAO-D Compression
Compute S* as with USAO
Attempt to use lower S with DPCM
  search for lowest S such that all deltas can be coded in 7 bits
  found that when DPCM mode is chosen, more than 99% of time S*-1 is used
  so can limit DPCM search to only S*-1 to reduce complexity

## Slide 13: USAO Results for LB-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class B | 0.28 | 0.23 | 0.15 | 0.28 | 0.18 | 0.28 | 0.27 | 0.07 | 0.39
Class C | 0.21 | 0.22 | 0.10 | 0.22 | 0.17 | 0.31 | 0.23 | 0.10 | 0.23
Class D | 0.17 | 0.38 | 0.64 | 0.16 | 0.29 | 0.01 | 0.17 | 0.37 | 0.06
Class E | 1.61 | 0.24 | 0.66 | 1.41 | 0.16 | 0.49 | 1.32 | 0.61 | 0.50
All | 0.48 | 0.27 | 0.36 | 0.45 | 0.20 | 0.26 | 0.43 | 0.25 | 0.29
Enc Time | 101% |  |  | 100% |  |  | 101% |  | 
Dec Time | 104% |  |  | 104% |  |  | 104% |  | 
Compared to HM-3.0-svn-memory anchor

## Slide 14: USAO-D Results for LB-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class B | 0.20 | 0.24 | 0.30 | 0.21 | 0.10 | 0.12 | 0.18 | 0.21 | 0.15
Class C | 0.18 | 0.18 | 0.07 | 0.16 | 0.07 | 0.29 | 0.20 | 0.05 | 0.01
Class D | 0.12 | 0.08 | 0.69 | 0.14 | 0.00 | 0.04 | 0.14 | 0.30 | 0.42
Class E | 1.11 | 0.31 | 0.08 | 1.09 | 0.25 | 0.61 | 0.98 | 0.03 | 0.32
All | 0.35 | 0.20 | 0.30 | 0.34 | 0.09 | 0.24 | 0.33 | 0.16 | 0.22
Enc Time | 99% |  |  | 99% |  |  | 99% |  | 
Dec Time | 104% |  |  | 105% |  |  | 105% |  | 
Compared to HM-3.0-svn-memory anchor

## Slide 15: USAO Results for RA-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class A | 0.00 | -0.13 | -0.26 | 0.02 | -0.24 | 0.23 | 0.10 | 0.08 | -0.23
Class B | 0.10 | -0.09 | -0.04 | 0.10 | 0.03 | 0.05 | 0.11 | 0.08 | 0.09
Class C | 0.12 | 0.07 | 0.02 | 0.11 | 0.19 | 0.10 | 0.15 | 0.06 | 0.18
Class D | 0.14 | 0.00 | -0.03 | 0.15 | 0.01 | 0.12 | 0.14 | 0.06 | 0.04
All | 0.09 | -0.04 | -0.07 | 0.09 | 0.00 | 0.12 | 0.12 | 0.07 | 0.03
Enc Time | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time | 103% |  |  | 103% |  |  | 101% |  | 
Compared to HM-3.0-svn-memory anchor

## Slide 16: USAO-D Results for RA-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class A | 0.00 | -0.22 | 0.05 | -0.01 | -0.07 | 0.01 | 0.09 | 0.21 | 0.11
Class B | 0.08 | -0.04 | 0.01 | 0.07 | 0.01 | -0.01 | 0.08 | 0.01 | 0.03
Class C | 0.08 | 0.07 | 0.01 | 0.12 | 0.15 | 0.09 | 0.11 | 0.06 | 0.19
Class D | 0.17 | -0.01 | -0.03 | 0.16 | 0.11 | 0.05 | 0.15 | 0.10 | -0.04
All | 0.08 | -0.05 | 0.01 | 0.08 | 0.08 | 0.03 | 0.11 | 0.09 | 0.07
Enc Time | 98% |  |  | 99% |  |  | 99% |  | 
Dec Time | 104% |  |  | 103% |  |  | 102% |  | 
Compared to HM-3.0-svn-memory anchor

## Slide 17: Conclusion
Designs can support wide range of internal bit depths: 8 < N < 15. Same algorithm is used for all chroma formats.
Coding loss for LB-HE of 0.48% (0.35%) for USAO (USAO-D).
Coding loss for RA-HE of 0.09% (0.08%) for USAO (USAO-D).
Recommend study in CE with goal of adopting some RFC scheme in next meeting.
We would like to thank Santa Clara University and MediaTek for cross checking.

## Slide 18: USAO Results for LB-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class B | -2.64 | -9.59 | -10.38 | -2.71 | -10.23 | -11.08 | -2.65 | -10.42 | -11.34
Class C | -1.30 | -4.80 | -5.59 | -1.29 | -5.22 | -5.86 | -1.23 | -5.24 | -5.88
Class D | -0.71 | -7.29 | -7.24 | -0.69 | -7.67 | -7.83 | -0.54 | -7.74 | -7.84
Class E | -4.80 | -14.75 | -11.07 | -5.60 | -15.38 | -12.72 | -5.93 | -14.50 | -13.12
All | -2.23 | -8.78 | -8.53 | -2.39 | -9.30 | -9.27 | -2.38 | -9.22 | -9.43
Enc Time | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time | 105% |  |  | 105% |  |  | 105% |  | 
Compared to HM-3.0 w/o IBDI

## Slide 19: USAO-D Results for LB-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class B | -2.72 | -9.57 | -10.21 | -2.79 | -10.30 | -11.28 | -2.74 | -10.28 | -11.56
Class C | -1.33 | -4.83 | -5.61 | -1.35 | -5.33 | -5.89 | -1.26 | -5.28 | -6.09
Class D | -0.75 | -7.59 | -7.24 | -0.70 | -7.92 | -7.83 | -0.57 | -7.81 | -7.51
Class E | -5.27 | -14.69 | -11.61 | -5.91 | -15.24 | -12.60 | -6.26 | -15.11 | -13.34
All | -2.36 | -8.85 | -8.58 | -2.49 | -9.39 | -9.32 | -2.48 | -9.32 | -9.51
Enc Time | 100% |  |  | 100% |  |  | 99% |  | 
Dec Time | 106% |  |  | 107% |  |  | 107% |  | 
Compared to HM-3.0 w/o IBDI

## Slide 20: USAO Results for RA-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class A | -1.41 | -4.58 | -5.08 | -1.43 | -4.79 | -5.24 | -1.39 | -4.76 | -5.52
Class B | -2.44 | -7.61 | -6.93 | -2.52 | -7.95 | -6.95 | -2.49 | -8.09 | -7.19
Class C | -1.24 | -3.74 | -3.88 | -1.27 | -3.83 | -4.06 | -1.21 | -3.79 | -4.07
Class D | -0.79 | -2.99 | -2.98 | -0.73 | -3.15 | -3.32 | -0.74 | -3.03 | -3.17
All | -1.54 | -4.94 | -4.82 | -1.57 | -5.15 | -4.98 | -1.53 | -5.15 | -5.06
Enc Time | 100% |  |  | 101% |  |  | 101% |  | 
Dec Time | 106% |  |  | 107% |  |  | 107% |  | 
Compared to HM-3.0 w/o IBDI

## Slide 21: USAO-D Results for RA-HE
 | internal bit depth 10 |  |  | internal bit depth 11 |  |  | internal bit depth 12 |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
Class A | -1.40 | -4.60 | -4.96 | -1.45 | -4.75 | -5.22 | -1.41 | -4.78 | -5.43
Class B | -2.47 | -7.56 | -6.89 | -2.56 | -7.97 | -7.02 | -2.52 | -8.16 | -7.24
Class C | -1.28 | -3.74 | -3.89 | -1.26 | -3.87 | -4.07 | -1.24 | -3.80 | -4.06
Class D | -0.76 | -2.99 | -2.98 | -0.72 | -3.05 | -3.39 | -0.73 | -2.99 | -3.25
All | -1.55 | -4.93 | -4.79 | -1.57 | -5.14 | -5.02 | -1.55 | -5.16 | -5.09
Enc Time | 99% |  |  | 99% |  |  | 99% |  | 
Dec Time | 107% |  |  | 107% |  |  | 108% |  | 
Compared to HM-3.0 w/o IBDI

## Slide 22: Cactus Luma MSE Histogram

## Slide 23: Cactus Luma MSE Histogram

## Slide 24: Cactus Chroma MSE Histogram

## Slide 25: Cactus Chroma MSE Histogram

## Slide 26: Comments on Cactus Histogram
Histograms indicate MSE=0 (very near lossless) coding for most blocks, especially for chroma.
Maximum Luma MSE = 13, which corresponds to PSNR of 49.03 dB
  PSNR = 10log(1020*1020/13) = 49.03
Maximum Chroma MSE = 3, which corresponds to PSNR of 55.40 dB

## Slide 27: Histogram Comparison
Compare histogram of USAO vs. Toshiba Adaptive Scaling with Offset (TASO)
Chosen sequences:
  BQSquare: TASO has lower coding loss
  Vidyo4: USAO has lower coding loss
What is behind the above behavior?

## Slide 28: BQSquare Histogram Comparison

## Slide 29: BQSquare Histogram Comparison

## Slide 30: BQSquare S Histogram Comparison

## Slide 31: Vidyo4 Histogram Comparison

## Slide 32: Vidyo4 Histogram Comparison

## Slide 33: Vidyo4 S Histogram Comparison

## Slide 34: Conclusion from Histogram Study
TASO benefits from putting a hard limit on the maximum MSE with fixed-rounding: observed with BQSquare
USAO and USAO-D benefit from potentially getting lower MSE even with higher S with use of offset: observed with Vidyo4.
Shows potential for merging TASO and USAO/USAO-D to get benefit from both.
Recommend studying USAO/USAO-D, TASO, and merging of them in a CE.
  Technical details of merging to be provided in CE document