## Slide 1: JCTVC-F077 Transform Skip Mode
R&D
© BBC MMXI
Marta Mrak, Andrea Gabriellini, Nikola Sprljan, David Flynn
BBC

## Slide 2: Transform Skip Mode (TSM)
Transform Skip Mode (TSM)
  defines transform skip in one or both directions on which a transform would be applied under common conditions
  main benefits
    enabling adaptation to underlying signal in the transformation stage of the coding
    reduced complexity required for the transformation stage at the decoder (computationally heavy transform not needed for some directions defined with TSM)
2D transform TS0 | transform on rows only TS1 | transform on columns only TS2 | no transform TS3

## Slide 3: Application of TSM
motion compensated (inter predicted) blocks
  not necessarily best compressed using 2D transform
  forcing the 2D transform can limit the effectiveness of DCT as a coding tool
  alternative low complexity tools can be considered
TSM and inter predicted blocks
  decided on TU-level
  encoder assigns one of four TS modes
    choice signalled to the decoder
TSM signalling
TSM |  | Code words
TS0 | 2D DCT | 1
TS1 | transform on rows | 01
TS2 | transform on columns | 001
TS3 | no transform | 000

## Slide 4: Implementation (encoder and decoder)
applied on TU-level
  TU correspond to a CU, except (as in HM3.x when RQT is off for inter blocks)
    for asymmetric partitions when a CU is split into 4 TUs
    for 64 x 64 CUs where a CU is split into 4 TUs (32 x 32)
compatible with HM3.x core transform [E243]
  main transform functions (void partialButterflyN( )) are left unchanged
  16 bit intermediate data representation is preserved
1D (row or column) transform skip applied as scaling
y = (x  scale + offset) >> shift
  scaling factors for N x N blocks
quantisation is left unchanged for all TSM choices,
coefficients scanning:
  zig-zag for TS0 and TS2
  vertical for TS1 (transform on rows skipped)
  horizontal for TS2 (transform on columns skipped)
N | 4 | 8 | 16 | 32
scale | 128 | 181 | 256 | 362

## Slide 5: Encoder side comparison with the current design
-
V
H
2D
CU residual

RDO search

coding decision
TSM
HM3.x (RQT)

## Slide 6: Results in HM3.2
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.5 | 0.6 | 0.3 | 1.1 | 0.1 | 0.4
Class B | 0.2 | -0.2 | 0.2 | 0.5 | -0.9 | 0.0
Class C | -0.1 | 0.1 | 0.4 | 0.2 | -0.3 | 0.4
Class D | -0.4 | 0.4 | 0.5 | 0.0 | 0.2 | 0.5
Class E |  |  |  |  |  | 
Overall | 0.0 | 0.2 | 0.3 | 0.4 | -0.3 | 0.3
Enc Time[%] | 99% |  |  | 109% |  | 
Dec Time[%] | 95% |  |  | 105% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.2 | 0.9 | 0.6 | -2.4 | 0.0
Class C | -0.5 | 0.0 | 0.5 | -0.1 | -0.6 | 1.0
Class D | -1.2 | 1.4 | 1.6 | -0.5 | 0.9 | 1.4
Class E | -0.5 | 0.5 | 0.0 | 0.0 | -0.5 | -0.9
Overall | -0.5 | 0.5 | 0.8 | 0.0 | -0.7 | 0.4
Enc Time[%] | 104% |  |  | 105% |  | 
Dec Time[%] | 100% |  |  | 102% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2 | -0.7 | -0.5 | 0.5 | -2.3 | 0.2
Class C | -0.6 | -0.3 | 0.2 | -0.3 | -0.6 | 0.7
Class D | -1.4 | 0.9 | 1.1 | -0.9 | 0.6 | 0.8
Class E | -0.8 | 0.2 | 0.2 | -0.1 | 0.4 | -0.5
Overall | -0.7 | 0.0 | 0.2 | -0.2 | -0.6 | 0.3
Enc Time[%] | 106% |  |  | 109% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1 | 0.0 | -0.2 | 0.3 | 0.0 | 0.2
Class B | -0.6 | -0.7 | -0.3 | -0.5 | -0.4 | 0.1
Class C | -0.8 | -0.2 | 0.0 | -0.7 | -0.1 | 0.3
Class D | -1.1 | 0.3 | 0.3 | -1.1 | 0.4 | 0.6
Class E |  |  |  |  |  | 
Overall | -0.6 | -0.2 | -0.1 | -0.5 | 0.0 | 0.3
Enc Time[%] | 119% |  |  | 122% |  | 
Dec Time[%] | 100% |  |  | 104% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.8 | -1.1 | -0.8 | -0.7 | -0.9 | -0.1
Class C | -1.5 | -0.7 | -0.1 | -1.4 | -0.4 | 0.6
Class D | -2.2 | 0.6 | 1.0 | -2.1 | 1.2 | 1.2
Class E | -0.8 | 1.0 | 0.3 | -0.8 | 0.9 | 0.4
Overall | -1.3 | -0.2 | 0.0 | -1.2 | 0.1 | 0.5
Enc Time[%] | 116% |  |  | 110% |  | 
Dec Time[%] | 99% |  |  | 96% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.9 | -1.6 | -1.5 | -0.5 | -0.6 | 0.2
Class C | -1.5 | -0.9 | -0.4 | -1.4 | -0.3 | 0.5
Class D | -2.2 | 0.5 | 0.3 | -2.2 | 0.9 | 0.5
Class E | -1.1 | 0.3 | 0.5 | -0.9 | 1.5 | 0.7
Overall | -1.4 | -0.5 | -0.4 | -1.2 | 0.2 | 0.4
Enc Time[%] | 128% |  |  | 127% |  | 
Dec Time[%] | 102% |  |  | 101% |  | 
TSM (in HM3.2 with Inter RQT off)
vs. HM3.2
TSM (in HM3.2 with Inter RQT off)
vs. HM3.2 with Inter RQT off

## Slide 7: Conclusions
benefits of Transform Skip Mode (TSM)
  enables adaptation to given residual block
    2D transform may not be always the best choice
  computationally heavy transform not needed when it is skipped
  non-recursive design