## Slide 1: MC boundary filter JCTVC-F100
Kenji Kondo and Teruhiko Suzuki
Sony Corp.

## Slide 2: Summary
Memory bandwidth is important because of
  Cost of DDR memory.
  Power consumption increases.
Explanation of MC boundary filter to reduce bandwidth
Experiment
  Check coding efficiency
    To simplify encoder, we checked the case of no use this boundary filter in motion search.
  Check visual quality
Conclusion

## Slide 3: The idea to reduce complexity
In order to reduce extend pixel of interpolation (pink), asymmetric filter coefficient is used for block boundary.
Extend pixel
Interpolated pixel
Unnecessary pixel
Conventional scheme
Proposal scheme

## Slide 4: Memory bandwidth
60% decrease for worst case
PU size
# of input pixel per 1 sub pel
For all PU, complexity decreases.

## Slide 5: Experiment
We checked the negative impact for coding efficiency and visual quality.
For Coding efficiency
  We tested two type for encoder issue.
    In motion estimation,
    1st step : Motion search each PU
      We tested two methods.
      MC only case : do interpolation using only DCTIF without boundary filter.
      MEMC case : do interpolation using boundary filter.
    2nd step : Mode decision each CU
      The boundary filter is used.
For visual quality
  Encoding condition
    RA_LC, LD_LC, LD P-only
    QP : 22 and 37
    Sequence: Nebuta, BQTerrace, BQMall, and BQsqure
  Environment for viewing
    EIZO monitor and High performance PC are used.
  Results
    The difference could not be found.

## Slide 6: Results and conclusion
MC boundary filter
  In worst case, 60% memory b/w can be reduced.
  It can be reduced for all PU size and both prediction modes (bi and uni-pred).
  In motion search, we can use simply designed filter with negligible coding loss (<0.05%).
  Visual quality is the same as DCTIF 8 tap.
 | Memory bandwidth |  | Computation |  | Avg. BD [%]
 | Worst | Average | Worst | Average | 
Case 1 | 67% | 79% | 93% | 101% | -0.03%
Case 2 | 64% | 78% | 72% | 89% | 0.06%
Case 3 | 40% | 61% | 71% | 89% | 0.17%

## Slide 7: Backup

## Slide 8: In actual case for 4x4 block
Memory locality
  With boundary filter, this means to use 4 tap for memory access.
Bandwidth decreases
  The memory b/w can be reduced for worst and average.
Computation decreases
  To interpolate yellow is not need.
For all PU size
  It can reduce Complexity.
MV
Extend pixel
Interpolated pixel
Unnecessary pixel by using boundary filter

## Slide 9: Filter coefficients
For test case 1
  1st MC block boundary
    { 0 , 2 , -9 , 56 , 20 , -8 , 4 , -2 , 1 } for quarter pel 0
    { 0 , 3 , -10 , 39 , 42 , -14 , 7 , -4 , 1 } for half pel
    { 0 , 2 , -6 , 18 , 58 , -11 , 5 , -3 , 1 } for quarter pel 1
For test case 2 and 3
  1st MC Block boundary
    { 0 , 0 , -5 , 54 , 21 , -9 , 5 , -3 , 1 } for quarter pel 0
    { 0 , 0 , -6 , 36 , 44 , -15 , 8 , -4 , 1 } for half pel
    { 0 , 0 , -3 , 16 , 59 , -12 , 6 , -3 , 1 } for quarter pel 1
  2nd MC block boundary
    { 0 , 2 , -9 , 56 , 20 , -8 , 4 , -1 , 0 } for quarter pel 0
    { 0 , 3 , -10 , 39 , 41 , -13 , 6 , -2 , 0 } for half pel
    { 0 , 2 , -6 , 18 , 58 , -11 , 4 , -1 , 0 } for quarter pel 1
  In case 2, only vertical filter is applied.

## Slide 10: Experiment
Test condition followed CE common test condition.
Additional test
  We tested two type for encoder issue.
    In motion estimation,
    1st step
      Motion search each PU
        We tested two methods.
        MC only case : do interpolation using only DCTIF.
        MEMC case : The boundary filter is used.
    2nd step
      Mode decision each CU
        The boundary filter is used.

## Slide 11: case 1
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.1 | 0.0 | 0.1 | -0.1 | 0.2
Class B | 0.0 | -0.1 | 0.0 | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0
Class D | 0.0 | -0.1 | 0.0 | 0.0 | -0.1 | -0.1
Class E |  |  |  |  |  | 
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 103% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | 0.3 | 0.2 | 0.0 | 0.1 | -0.1
Class C | -0.1 | -0.2 | -0.2 | -0.1 | 0.1 | -0.1
Class D | -0.2 | 0.0 | 0.2 | -0.2 | 0.0 | -0.3
Class E | 0.2 | 0.1 | -0.3 | 0.1 | -0.1 | -0.3
All | -0.1 | 0.1 | 0.0 | 0.0 | 0.0 | -0.2
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 | P-only |  |  | P-only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.2 | -0.2 | 0.0 | 0.1 | 0.2
Class C | 0.0 | 0.1 | -0.2 | 0.0 | -0.1 | 0.0
Class D | -0.1 | -0.2 | -0.5 | -0.1 | 0.3 | 0.0
Class E | 0.0 | 0.3 | 0.1 | 0.2 | 0.3 | 0.1
All | 0.0 | 0.1 | -0.2 | 0.0 | 0.1 | 0.1
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
Average: -0.03%

## Slide 12: case 1 without ME process
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.3
Class B | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class C | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | -0.1
Class D | 0.0 | -0.1 | 0.0 | -0.1 | -0.2 | -0.1
Class E |  |  |  |  |  | 
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 102% |  |  | 102% |  | 
Dec Time[%] | 102% |  |  | 104% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.2 | 0.2 | 0.0 | 0.0 | -0.1
Class C | -0.1 | -0.1 | -0.1 | -0.1 | 0.1 | -0.1
Class D | -0.2 | -0.2 | -0.2 | -0.3 | 0.0 | 0.1
Class E | 0.3 | 0.1 | -0.3 | 0.1 | -0.3 | -0.1
All | 0.0 | 0.0 | -0.1 | -0.1 | 0.0 | 0.0
Enc Time[%] | 102% |  |  | 102% |  | 
Dec Time[%] | 101% |  |  | 103% |  | 
 | P-only |  |  | P-only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | -0.1 | 0.0 | 0.1 | 0.1 | 0.1
Class C | 0.0 | 0.1 | -0.2 | 0.0 | -0.1 | -0.1
Class D | -0.1 | -0.3 | -0.1 | -0.2 | 0.0 | 0.0
Class E | 0.1 | -0.2 | -0.4 | 0.2 | -0.5 | -0.3
All | 0.0 | -0.1 | -0.2 | 0.0 | -0.1 | 0.0
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Average: -0.01%

## Slide 13: case 2
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.1
Class B | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0
Class C | 0.1 | 0.1 | 0.0 | 0.1 | 0.0 | 0.0
Class D | 0.2 | 0.1 | 0.1 | 0.2 | 0.0 | 0.0
Class E |  |  |  |  |  | 
All | 0.1 | 0.0 | 0.1 | 0.1 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.2 | 0.0 | -0.1 | 0.0 | -0.1
Class C | 0.1 | 0.0 | -0.1 | 0.0 | 0.2 | -0.1
Class D | 0.0 | 0.1 | 0.1 | 0.1 | 0.4 | -0.1
Class E | 0.2 | 0.0 | 0.0 | -0.1 | -0.2 | -0.6
All | 0.1 | 0.1 | 0.0 | 0.0 | 0.1 | -0.2
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 | P-only |  |  | P-only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.0 | -0.3 | -0.1 | 0.1 | 0.2
Class C | 0.2 | 0.1 | 0.0 | 0.1 | 0.0 | 0.0
Class D | 0.1 | -0.5 | -0.1 | 0.2 | -0.3 | 0.0
Class E | 0.0 | -0.2 | 0.0 | 0.0 | 0.0 | -0.2
All | 0.1 | -0.1 | -0.1 | 0.0 | 0.0 | 0.0
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
Average: 0.06%

## Slide 14: case 2 without ME process
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.1 | -0.1 | 0.0 | 0.1 | 0.1 | 0.2
Class B | 0.1 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1
Class C | 0.1 | 0.1 | 0.0 | 0.2 | 0.1 | 0.1
Class D | 0.2 | 0.0 | 0.0 | 0.3 | 0.0 | 0.1
Class E |  |  |  |  |  | 
All | 0.1 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.3 | 0.0 | 0.0 | 0.1 | -0.1
Class C | 0.1 | 0.2 | 0.0 | 0.1 | 0.0 | -0.1
Class D | 0.0 | -0.1 | 0.2 | 0.1 | 0.1 | 0.0
Class E | 0.1 | 0.2 | -0.6 | 0.0 | 0.1 | -0.4
All | 0.1 | 0.1 | -0.1 | 0.0 | 0.1 | -0.2
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 103% |  | 
 | P-only |  |  | P-only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.1 | -0.1 | 0.0 | 0.2 | 0.3
Class C | 0.2 | 0.2 | 0.1 | 0.1 | 0.1 | 0.2
Class D | 0.2 | 0.0 | 0.2 | 0.2 | 0.4 | 0.1
Class E | 0.1 | 0.0 | -0.3 | 0.0 | -0.2 | -0.3
All | 0.1 | 0.1 | 0.0 | 0.1 | 0.1 | 0.1
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Average: 0.09%

## Slide 15: case 3
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.1 | 0.2 | 0.1 | 0.0 | 0.2
Class B | 0.1 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1
Class C | 0.3 | 0.1 | 0.0 | 0.3 | 0.1 | 0.1
Class D | 0.5 | 0.2 | 0.2 | 0.6 | 0.2 | 0.2
Class E |  |  |  |  |  | 
All | 0.2 | 0.0 | 0.1 | 0.2 | 0.1 | 0.1
Enc Time[%] | 102% |  |  | 103% |  | 
Dec Time[%] | 101% |  |  | 104% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.1 | -0.1 | -0.1 | -0.1 | -0.2
Class C | 0.3 | 0.1 | 0.2 | 0.2 | 0.0 | -0.2
Class D | 0.3 | 0.1 | 0.3 | 0.2 | 0.7 | 0.4
Class E | 0.3 | 0.3 | -0.2 | 0.0 | -0.1 | -0.6
All | 0.2 | 0.1 | 0.1 | 0.1 | 0.1 | -0.1
Enc Time[%] | 102% |  |  | 103% |  | 
Dec Time[%] | 100% |  |  | 103% |  | 
 | P-only |  |  | P-only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.1 | -0.3 | -0.1 | 0.2 | 0.4
Class C | 0.3 | 0.0 | 0.1 | 0.1 | 0.0 | 0.0
Class D | 0.4 | 0.3 | 0.1 | 0.3 | 0.1 | 0.2
Class E | 0.2 | 0.2 | -0.3 | -0.1 | -0.5 | 0.0
All | 0.3 | 0.1 | -0.1 | 0.1 | 0.0 | 0.2
Enc Time[%] | 102% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
Average: 0.17%

## Slide 16: case 3 without ME process
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.1 | -0.1 | 0.1 | 0.0 | -0.1 | 0.3
Class B | 0.1 | -0.1 | 0.1 | 0.1 | 0.1 | 0.0
Class C | 0.3 | 0.1 | 0.1 | 0.3 | 0.1 | 0.1
Class D | 0.6 | 0.2 | 0.1 | 0.6 | 0.2 | 0.2
Class E |  |  |  |  |  | 
All | 0.3 | 0.0 | 0.1 | 0.2 | 0.1 | 0.2
Enc Time[%] | 102% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 103% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.1 | 0.2 | 0.1 | -0.1 | 0.0 | 0.0
Class C | 0.3 | 0.2 | 0.2 | 0.2 | 0.1 | 0.0
Class D | 0.4 | 0.7 | 0.4 | 0.3 | 0.2 | 0.3
Class E | 0.4 | 0.3 | -0.3 | 0.0 | -0.2 | -0.1
All | 0.3 | 0.3 | 0.1 | 0.1 | 0.0 | 0.1
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 102% |  | 
 | P-only |  |  | P-only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.2 | 0.2 | -0.2 | 0.0 | 0.2 | 0.5
Class C | 0.3 | 0.2 | 0.0 | 0.3 | 0.2 | 0.1
Class D | 0.5 | 0.1 | 0.2 | 0.4 | 0.3 | 0.0
Class E | 0.2 | -0.2 | -0.2 | 0.0 | -0.4 | -0.2
All | 0.3 | 0.1 | -0.1 | 0.2 | 0.1 | 0.1
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Average: 0.22%

## Slide 17: END