## Slide 1: Results on Bi/Uni MC filter JCTVC-F101
Kenji Kondo and Teruhiko Suzuki
Sony Corp.

## Slide 2: Summary
Explanation of Bi/Uni MC filter
Change from previous contribution E128
Experiment
Conclusion

## Slide 3: Reminder Bi/Uni MC filter
It switches filter coefficients by either prediction mode is bi-pred or uni-pred.
Merit of Bi/Uni switching
  If MC block is bi-pred, it works as averaging L0 and L1.
    This averaging can suppress some coding noise.
    Also, high frequency component such as edges will be reduced.
  On the other hand, if MC block is single pred,
    interpolation filter interpolates reference including coding noise.
  To effective, above some phenomenon suggest that
    For bi-prediction, the interpolation filter needs to protect high frequency components
    For single-prediction, interpolation filter should slightly suppress high frequency component to some de-nosing.

## Slide 4: Change from E128
Basically this proposal is same as previous contribution JCTVC-E128
Change from the JCTVC-E128
  To simplify encoder, the filter for only uni-prediction is used when motion search.
  Filter tap length is changed.
    In E128, 5 tap filter was used for uni-prediction.
    It is changed to 8 tap filter.
      To avoid coding loss in IPPP case, and to support simple motion search using only uni filter, 8 tap is used for uni-prediction.

## Slide 5: Filter coefficients
Prediction mode | Sub pel | Tap length | Filter coefficients
Uni- prediction | 1/2 pel | 8 | -1 , 4 , -10 , 39, 39, -10, 4, -1
 | 1/4 pel | 8 | -1 , 4 , -10 , 57 , 19, -7, 3, -1
Bi-prediction | 1/2 pel | 8 | -2 , 5 , -12 , 41, 41, -12, 5, -2
 | 1/4 pel | 7 | -2 , 6 , -13 , 62 , 15 , -5 , 1

## Slide 6: Experiment
Test condition follows JCTVC-D600
  So, Bi/Single filter is compared with DCTIF in HM2.0.
  4 test conditions
    RA_HE, RA_LC, LD_HE, and LD_LC
Simulation environment
  Used machines
    Core i7 CPU 2.93GHz, 8 GB memory.
    OS is Linux 64 bit.
  For encoder, a cluster of above machines was used.
  For decoder, only 1 machine in the cluster was used.
    Decoding time are measured without yuv output.

## Slide 7: Test results
 | Random access |  |  | Random access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.3 | 0.5 | 0.5 | 0.5 | 0.2 | 0.7
Class B | -0.1 | 0.1 | 0.2 | -0.3 | 0.2 | 0.2
Class C | -0.8 | -0.1 | -0.3 | -1.6 | -0.1 | -0.2
Class D | -1.6 | -0.7 | -0.8 | -3.3 | -0.9 | -0.8
Class E |  |  |  |  |  | 
All | -0.5 | -0.1 | -0.1 | -1.1 | -0.1 | 0.0
Enc Time[%] | 98% |  |  | 99% |  | 
Dec Time[%] | 97% |  |  | 99% |  | 
 | Low delay |  |  | Low delayLC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.2 | 0.6 | 0.1 | 0.2 | 0.0 | -0.3
Class C | -0.1 | 0.3 | 0.2 | -1.0 | 0.1 | 0.0
Class D | -0.1 | 0.0 | 0.7 | -1.3 | 0.2 | -0.1
Class E | 0.6 | 0.9 | 0.3 | 1.7 | -0.5 | 0.4
All | 0.1 | 0.5 | 0.3 | -0.2 | 0.0 | 0.0
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
 | Low delay P |  |  | Low delay LCP |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | -0.2 | -0.4 | -0.3 | -0.3 | -0.1
Class C | -0.1 | -0.1 | -0.1 | -0.2 | -0.3 | -0.3
Class D | 0.0 | -0.1 | -0.3 | 0.3 | 0.0 | -0.7
Class E | -0.2 | 0.0 | -0.6 | -1.3 | -0.8 | -0.6
All | -0.1 | -0.1 | -0.4 | -0.3 | -0.3 | -0.4
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 98% |  | 
Average BD%: -0.4%

## Slide 8: Complexity analysis
Operations | Worst case / pixel | 90%
 | Average of operations / pixel | 97%
Bandwidth | Worst case / pixel | 100%
 | Average of bytes / pixel | 100%
Complexity of computation is improved by reducing tap length.

## Slide 9: Conclusion
Bi/Uni filter was tested in CE3.
To simplify encoder, only uni-pred filter was studied for motion search.
In average, -0.4% gain can be obtained.
Proposal
  We propose further study that is to harmonize with other techniques.