## Slide 1: Redundancy removal of residual information for CAVLC in merge 2Nx2N
JCTVC-F107
Joonyoung Park
Byeongmoon Jeon

## Slide 2: Introduction
Merge skip has been adopted.
Skip mode and 2Nx2N_MRG mode share the motion representation method.
The only difference between two modes is
  whether the residual information is transmitted or not.
For redundancy removal,
  CABAC : no_residual_data_flag is inferred as 0 in 2Nx2N_MRG mode
  CAVLC : no consideration
We propose to
  remove redundancy in CAVLC

## Slide 3: Proposed method
In CAVLC, no syntax such as ‘no_residual_data_flag’
Syntax ‘cbp_and_split_transform’
  Jointly code split_transform_flag and coded block flags (CBFs) for YUV components
We propose to
  temporally disable all-CBF-zero case,
  when CU is coded with 2Nx2N_MRG and trafoDepth is zero.

## Slide 4: Proposed method
<An example of cbp_and_split_transform ranking table
when flag pattern is 15>
Luma | CbCr | Split | Rank | Modified rank
0 | 0 | 0 | 4 | NA
0 | 0 | 1 | NA | NA
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 5 | 4
1 | 0 | 0 | 3 | 3
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 2 | 2
1 | 1 | 1 | 6 | 5
Rank is temporally modified only when CU is coded with 2Nx2N_MRG and trafoDepth is zero
Proposed part
All-CBF-zero
Instead of the original rank, the modified rank is transmitted,
only when CU is coded with 2Nx2N_MRG and trafoDepth is zero

## Slide 5: Proposed method
Decoder needs the inverse process of modification.
Luma | CbCr | Split | Rank | Modified rank
0 | 0 | 0 | 4 | NA
0 | 0 | 1 | NA | NA
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 5 | 4
1 | 0 | 0 | 3 | 3
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 2 | 2
1 | 1 | 1 | 6 | 5
Inverse
modification
Parse rankcur
CU is coded with 2Nx2N_MRG and trafoDepth is zero ?
Obtain syntax values from rankcur
rankcur
>= rankall-cbf-zero?
rankcur = rankcur + 1
Y
Y
N
N

## Slide 6: Results
 | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.1 | -0.1 | 0.1
Class B | -0.1 | 0.0 | 0.0
Class C | -0.1 | 0.0 | -0.1
Class D | -0.1 | 0.0 | 0.0
Class E |  |  | 
All | -0.1 | 0.0 | 0.0
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -0.1 | -0.2 | -0.6
Class C | -0.2 | -0.1 | -0.3
Class D | -0.1 | 0.0 | -0.2
Class E | -0.1 | -0.5 | -0.8
All | -0.1 | -0.2 | -0.4
Enc Time[%] | 101% |  | 
Dec Time[%] | 100% |  | 
Anchor : HM 3.0
Common test condition is used.

## Slide 7: Conclusion
A change in cbp_and_split_transform syntax is proposed for CAVLC.
By proposed method,
  We can remove the redundancy in syntax structure.
  We can keep consistency between CAVLC and CABAC.
0.1% BD gain
Recommend to adopt in HM