## Slide 1: Remaining Mode Redundancy Removal
Jaehyun Lim
LG Electronics
JCTVC-F109

## Slide 2: Introduction
Intra prediction
  MPM_flag and MPM_index are used for signaling efficiency.
  If MPM_flag is 0, remaining mode is transmitted,
  excluding MPM candidates
Intra mode signaling process
Current
PU
B
A
above
MPM
candidate
MPM_flag
MPM_flag
=1?
MPM_index
Y
Y
remaining
mode
intra_mode
=A
intra_mode
=B
N
left
MPM
candidate

## Slide 3: Introduction
Intra prediction for 64x64 PU
  3 intra modes (VER/HOR/DC) are allowed.
  In current HM,
  regardless of the MPMCand number, a flag is signaled for remaining mode.
  If two intra modes are used for MPM candidates,
  the remaining mode can be inferred without signaling information.
Number of intra modes allowed for each PU size
PU size | intraPredModeNum
4x4 | 17
8x8 | 34
16x16 | 34
32x32 | 34
64x64 | 3
0
1
2
2 MPM candidates
Intra mode is
determined
without signaling
3 intra mode candidates
for 64x64 PU

## Slide 4: Proposed method
Prediction unit syntax table for the proposed method
prediction_unit( x0, y0, log2PUWidth, log2PUHeight, PartIdx , InferredMergeFlag ) { | Descriptor
if( skip_flag[ x0 ][ y0 ] ) { | 
if( NumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ue(v) ¦ ae(v)
} else if( PredMode = = MODE_INTRA ) { | 
prev_intra_luma_pred_flag[ x0 ][ y0 ] | u(1) ¦ ae(v)
if( prev_intra_luma_pred_flag[ x0 ][ y0 ] ) | 
if( NumMPMCand > 1 ) | 
mpm_idx[ x0 ][ y0 ] | u(1) ¦ ae(v)
else | 
if( NumRemCand > 1 ) | 
rem_intra_luma_pred_mode[ x0 ][ y0 ] | ue(v) ¦ ae(v)
intra_chroma_pred_mode[ x0 ][ y0 ] | ue(v) ¦ ae(v)
} else { /* MODE_INTER */ | 
︙ | 
} | 
} | 
Where the variable NumRemCand is derived as follows.
NumRemCand = intraPredModeNum - NumMPMCand

## Slide 5: Experimental Results
BD rate(%) reduction of the proposed method
BD-rate reduction & complexity
  - The performance is almost same as the anchor
  from the rare selection of 64x64 PU
  - No encoder/decoder complexity changes
 | Intra only HE |  |  | Intra only LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class B | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 6: Conclusion
Redundancy in signaling of the remaining mode is proposed in this contribution.
The redundancy on the remaining mode can be removed easily by
adding one simple condition.
It is recommended to adopt the proposed method into HM to remove the redundancy.

## Slide 7: Annex. Proposed WD changes
Prediction unit syntax table for the proposed method
prediction_unit( x0, y0, log2PUWidth, log2PUHeight, PartIdx , InferredMergeFlag ) { | Descriptor
if( skip_flag[ x0 ][ y0 ] ) { | 
if( NumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ue(v) ¦ ae(v)
} else if( PredMode = = MODE_INTRA ) { | 
prev_intra_luma_pred_flag[ x0 ][ y0 ] | u(1) ¦ ae(v)
if( prev_intra_luma_pred_flag[ x0 ][ y0 ] ) | 
if( NumMPMCand > 1 ) | 
mpm_idx[ x0 ][ y0 ] | u(1) ¦ ae(v)
else | 
if( NumRemCand > 1 ) | 
rem_intra_luma_pred_mode[ x0 ][ y0 ] | ue(v) ¦ ae(v)
intra_chroma_pred_mode[ x0 ][ y0 ] | ue(v) ¦ ae(v)
} else { /* MODE_INTER */ | 
︙ | 
} | 
} | 
Where the variable NumRemCand is derived as follows.
NumRemCand = intraPredModeNum - NumMPMCand

## Slide 8: Annex. Proposed WD changes
Semantic
prev_intra_luma_pred_flag[ x0 ][ y0 ], mpm_idx[ x0 ][ y0 ] and rem_intra_luma_pred_mode[ x0 ][ y0 ] specify the intra prediction mode for luma samples. The array indices x0, y0 specify the location ( x0, y0 ) of the top-left luma sample of the considered prediction block relative to the top-left luma sample of the picture. When prev_intra_luma_pred_flag[ x0 ][ y0 ] is equal to 1, the intra prediction mode is inferred from a neighbouring intra-predicted prediction unit according to subclause 8.3.1. When rem_intra_luma_pred_mode[ x0 ][ y0 ] is not present, it is inferred to be equal to 0.

## Slide 9: Annex. Derivation from remaining mode to intra mode
example
  Intra prediction mode = 1(HOR)
  MPM candidates = 0(VER), 2(DC)
  First, IntraPredMode is inferred to 0 from rem_intra_pred_mode
  In the first, loop IntraPredMode (0) >= 1st MPM candidate (0)
   IntraPredMode++;
  In the second loop IntraPredMode (1) >= 2nd MPM candidate (2)
   Final IntraPredMode = 1
IntraPredMode[ xB ][ yB ] = rem_intra_pred_mode
for (cIdx = 0; cIdx < NumMPMCand; cIdx++)
if (IntraPredMode[ xB ][ yB ]>= candModeList[cIdx]) IntraPredMode[ xB ][ yB ]++
IntraPredMode derivation process
Intra mode 0 1 2 3 4 5 6 7 8 9 …
Remaining mode 0 1 2 2 3 4 6 5 6 7 …
1st MPM Cand
2nd MPM Cand