## Slide 1: CE6.b4: LM mode harmonization on SDIP
Jaehyun Lim
LG Electronics
JCTVC-F110

## Slide 2: Introduction
Chroma prediction on SDIP
  SDIP defines its own chroma prediction.
  LM mode was adopted from JCT-VC E266 in the last meeting.
  LM mode harmonization was implemented in SDIP anchor (based on HM3.0)
idx | mode
0 | luma mode 1
1 | luma mode 2
2 | luma mode 3
3 | luma mode 4
4 | mode 0
5 | mode 1
6 | mode 2
7 | mode 3
Chroma mode candidate
(a) SDIP(based on HM2.0) (b) SDIP anchor (based on HM3.0)
5 modes
are
tested
6 modes
are
tested
idx | mode
0 | luma mode 1
1 | luma mode 2
2 | luma mode 3
3 | luma mode 4
4 | LM mode
5 | mode 0
6 | mode 1
7 | mode 2
8 | Planar mode

## Slide 3: Proposed method
Change the order of LM mode
  Positions are switched between luma modes and LM mode
SDIP
anchor
c
a
LM
d
b
2
0
1
2
0
4
3
1
7
5
6
idx
mode
Luma mode
c
a
LM
d
b
2
0
1
2
0
4
3
1
7
5
6
idx
mode
Luma mode
Proposed
method
Planar
8
Planar
8

## Slide 4: Experimental Results
BD rate(%) reduction of the proposed method vs SDIP anchor
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.1 | -0.1 | 0.0 | -0.5 | -0.1
Class B | 0.0 | -0.2 | -0.2 | 0.0 | -0.2 | -0.1
Class C | -0.1 | -0.3 | -0.2 | -0.1 | -0.3 | -0.3
Class D | -0.1 | -0.3 | -0.3 | -0.1 | -0.3 | -0.2
Class E | 0.1 | -0.4 | -0.5 | 0.0 | -0.1 | -0.2
All | 0.0 | -0.2 | -0.2 | 0.0 | -0.3 | -0.2
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 5: Conclusion
LM mode harmonization method for SDIP was proposed.
The proposed scheme showed more harmonized method
for the chroma mode decision on SDIP
without any encoder/decoder complexity changes.

## Slide 6: Annex. Experimental Results vs “SDIP chroma without LM mode”
SDIP anchor vs SDIP chroma without LM mode
Proposed method vs SDIP chroma without LM mode
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.3 | -0.4 | 0.0 | -1.0 | -0.5
Class B | 0.0 | -0.5 | -0.5 | -0.1 | -0.8 | -0.7
Class C | -0.1 | -1.0 | -1.0 | -0.2 | -1.2 | -1.3
Class D | -0.1 | -0.6 | -0.5 | -0.1 | -0.8 | -0.7
Class E | 0.0 | -0.5 | -0.5 | -0.1 | -0.9 | -1.1
All | -0.1 | -0.6 | -0.6 | -0.1 | -0.9 | -0.8
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | -0.4 | -0.4 | 0.0 | -1.5 | -0.6
Class B | 0.0 | -0.7 | -0.7 | -0.1 | -1.0 | -0.7
Class C | -0.2 | -1.3 | -1.2 | -0.3 | -1.6 | -1.6
Class D | -0.2 | -0.9 | -0.8 | -0.2 | -1.1 | -0.9
Class E | 0.0 | -0.9 | -0.9 | 0.0 | -1.0 | -1.2
All | -0.1 | -0.8 | -0.8 | -0.1 | -1.2 | -1.0
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  |