## Slide 1: Ericsson’s and MediaTek’s deblocking filter
JCTVC-F118
Andrey Norkin, Kenneth Andersson, Rickard Sjöberg, Qian Huang, Jicheng An, Xun Guo and Shawmin Lei
Ericsson and MediaTek
Notes: 2010-10-07
Ericsson AB 2010
<number>

## Slide 2: Filter description
Filter is based on CE12 contributions: E276 (Ericsson), E079 (MediaTek) and adopts spirit of F143 (Toshiba/Qualcomm)
Luma:
  Filter 1 or 2 pixels (decision for each side of 8-pel block boundary)
  Weak filter: different delta values for p1 and q1
  Check for natural edges
Chroma:
  Filter on 4x4 grid for 4:2:0 (corresponds to 8x8 luma grid)
  Filter inter chroma blocks with coefficients
  Filter chroma boundary if adjacent blocks are flat (a decision added on a block level)
  Filtering operation
Bs:
  Do not check for block coefficients if boundary is not a TU boundary
Tc:
  tc_offset = 2
Notes: 2010-10-07
Ericsson AB 2010
<number>

## Slide 3: Why we propose to adopt F118
Objective gains: BD-rate
  Luma: -1.2 %, Chroma U: -2.6%, Chroma V: -2.7%
Subjective quality
  Slightly better on average than HM3.0
The filter response is improved comparing to HEVC deblocking filter
  No amplification of high frequencies which is present in HEVC deblocking
Filter design is consistent with HM3.0 deblocking scheme
Deblocking of chroma inter predicted blocks (current HM – no chroma filtering for inter-predicted blocks with coefficients)
No filtering of chroma boundaries when high spatial activity on the sides of the block boundary

## Slide 4: Filter frequency response for p1 and q1 F118 vs HEVC
HEVC (green)
F118 (red)

## Slide 5: Filter frequency response for p0 and q0 F118 vs HEVC
HEVC (green)
F118 (red)

## Slide 6: Luma weak filter description
 = ( 9(q0 - p0) - 3(q1 - p1) ) /16
p0’ = p0 + 
q0’ = q0 - 
p1 = (p0 - 2p1+ p2 + 2)/4;
p1’ = p1 + p1
q1 = (q0 - 2q1 + q2 - 2)/4;
q1’ = q1 + q1
Filter features:
Different  values for p1 and q1
Modifications of p1 and q1 depend on local structure on each side
The ramp (gradient) it is not modified
p1
p0
q0
q1
q2
p2

## Slide 7: Number of pixels to be modified
Block P
Block Q
0
0
1
1
2
2
dp = |p22 - 2*p12 + p02| + |p25 - 2*p15 + p05|
dq = |q22 - 2*q12 + q02| + |q25 - 2*q15 + q05|
If dp < thr2
modify p1
If dq < thr2
modify q1
Modify p0 and q0
if the line is to be filtered
thr2= (β(QP)+(β(QP)>>1))>>3

## Slide 8: Check for natural edges example
  Filter a line across block boundary only if abs() < thr1
q0
q1
q2
p0
p1
p2
p2
p1
p0
q0
q1
q2
abs() = 0
abs() > 0
thr1 = tc(QP)*10

## Slide 9: Chroma changes
Filter when chroma Bs = 2
  Add filtering of chroma boundaries when at least one of adjacent blocks has chroma coefficients
Filtering grid size
  According to sampling format
    For 4:2:0, 4x4 is used
    For 4:2:2, 4x8 is used
    For 4:4:4, 8x8 is used
Add check for spatial activity
  filtering is performed if the spatial activity on the block boundary is below a threshold |p0-p1| is used.
Modified filtering operation
  The coefficients are slightly different with that of HM3.0

## Slide 10: Other adjustments
Boundary strength (Bs) derivation
  BS=2 only for TU boundary
    In HEVC, TU can cover more than one PU
    Currently it is possible that Bs = 2 for boundary between PU’s when PU’s are covered by one TU that has non-zero coefficients
Tc modification
  tc_offset = 2
    currently in HEVC tc_offset = 4, inherited from TENTM

## Slide 11: Compression performance All-intra
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -1.6 | -1.5 | -1.2 | -1.3 | -2.3 | -2.1
Class B | -1.2 | -1.4 | -1.6 | -1.0 | -2.6 | -2.7
Class C | -0.9 | -2.5 | -2.5 | -0.9 | -3.4 | -3.9
Class D | -0.9 | -2.3 | -2.4 | -0.8 | -3.5 | -3.8
Class E | -1.3 | -0.4 | -0.6 | -1.1 | -2.2 | -3.0
Overall | -1.2 | -1.7 | -1.7 | -1.0 | -2.8 | -3.1
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 12: Compression performance Random access
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -1.4 | -2.3 | -1.8 | -1.4 | -2.6 | -2.0
Class B | -1.2 | -2.6 | -2.3 | -1.3 | -2.8 | -2.3
Class C | -1.0 | -3.5 | -3.3 | -1.0 | -3.5 | -3.8
Class D | -0.8 | -2.9 | -3.3 | -0.8 | -2.9 | -3.0
Class E |  |  |  |  |  | 
Overall | -1.1 | -2.8 | -2.6 | -1.1 | -2.9 | -2.8
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 100% |  |  | 102% |  | 

## Slide 13: Compression performance Low delay
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -1.4 | -2.7 | -2.8 | -1.4 | -2.4 | -2.3
Class C | -1.1 | -2.9 | -2.8 | -1.0 | -2.3 | -3.0
Class D | -0.9 | -1.7 | -1.8 | -0.8 | -1.7 | -2.3
Class E | -2.8 | -3.1 | -3.7 | -2.4 | -6.6 | -6.2
Overall | -1.5 | -2.6 | -2.7 | -1.3 | -3.0 | -3.2
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 99% |  |  | 102% |  | 

## Slide 14: Comments on decoding time
A small decoding time increase is caused by current implementation of parallel decoding decisions in deblocking
In HM3.0, a copy of luma picture is created and used to calculate decoding decisions. Another copy is used for actual filtering. Reading is done from two places in the memory instead of one.
To make decision for chroma components, the same procedure needs to be applied to chroma  increase in decoding time
If chroma decisions are done on the filtered data, no increase in decoding time has been observed (the results for three standard configurations have already been obtained)

## Slide 15: Decoding time for F118 without parallel chroma decisions
 | F118 (vs HM3.0) | F118 without parallel chroma decisions (vs HM3.0)
AI | 100.0 % | 99.3 %
AILC | 101.3 % | 100.0 %
RA | 100.1 % | 99.2 %
RALC | 101.7 % | 100.4 %
LD | 99.3 % | 98.6 %
LDLC | 101.8 % | 99.9 %
Average | 100.7 % | 99.6 %

## Slide 16: Conclusions
BD-rate = -1.2 % for luma, -2.6% for U and -2.7% for V components on average for six standard configurations
Decoding time increase is on average below 1% of HM3.0 and is due to implementation of parallel deblocking decisions in HM3.0
Subjective quality is slightly better on average than in HEVC
Thanks to Toshiba, Panasonic, SKKU, Samsung for cross checking and review of source code
It is proposed to adopt F118 in the next version of HM

## Slide 17
Notes: 2010-10-07
Ericsson AB 2010
<number>