## Slide 1: Extended Mode-Dependent Coefficient Scanning
Xin Zhao, Xun Guo, Mei Guo, Shawmin Lei, Siwei Ma and Wen Gao
MediaTek Inc.
Copyright © MediaTek Inc. All rights reserved.
Presented by Xun Guo
6th JCT-VC Meeting in Torino
14-22 July, 2011
Notes: <number>

## Slide 2: Overall Summary
An extended Mode-dependent coefficients scanning (MDCS) method is proposed
  Two extensions of MDCS
    Extend to TUs of 16x16 and 32x32
      Modified horizontal and vertical scanning orders
    Extend to level scanning in CABAC
Experimental results
  Based on HM3.0 and conditions of JCTVC-E700
  Average BD-rate reductions of 0.3% and 0.6% for HE-AI and LC-AI
Run time
  Almost the same as that of HM3.0
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 3: Outline
Introduction
Proposed method
Simulation results
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 4: Three Scanning Orders in HM3.0
Zigzag, Horizontal and Vertical
The scanning order for each TU is determined by it’s intra prediction mode
Copyright © MediaTek Inc. All rights reserved.
<number>
Zigzag: 0
Horizontal: 1
Vertical: 2

## Slide 5: MDCS Selection
Scanning pattern is selected according to a look-up-table
  For 16x16 and 32x32, zigzag is always used
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 6: MDCS for CABAC in HM3.0
Significance map
  MDCS is used
Absolute value of coefficients
  A TU is split into 4x4 sub-blocks
  Only reverse 4x4 zigzag is used for each sub-block
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 7: Outline
Introduction
Proposed method
Simulation results
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 8: Extension 1 – Modified MDCS
A modified MDCS
  Zigzag, modified horizontal scanning order, modified vertical scanning order
  New mapping table for TUs of 16x16 and 32x32
Offline derivation of modified horizontal and vertical scanning orders
  To retrieve the scanning pattern analytically, coefficient variances are calculated based on image correlation model
  Scanning pattern is obtained by sorting the variance values in descending order
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 9: An Example for 8x8 TU
ρx=0.4, ρy=0.9
  For 16x16 and 32x32, the optimal performance is located at “ρx=0.45, ρy=0.99” and “ρx=0.6, ρy=0.99”, respectively
Copyright © MediaTek Inc. All rights reserved.
<number>
8.087 | 6.312 | 4.876 | 3.601 | 2.744 | 2.213 | 1.901 | 1.737
2.068 | 1.614 | 1.247 | 0.921 | 0.702 | 0.566 | 0.486 | 0.444
0.712 | 0.555 | 0.429 | 0.317 | 0.241 | 0.195 | 0.167 | 0.153
0.341 | 0.266 | 0.206 | 0.152 | 0.116 | 0.093 | 0.080 | 0.073
0.215 | 0.168 | 0.130 | 0.096 | 0.073 | 0.059 | 0.051 | 0.046
0.156 | 0.122 | 0.094 | 0.069 | 0.053 | 0.043 | 0.037 | 0.033
0.127 | 0.099 | 0.076 | 0.056 | 0.043 | 0.035 | 0.030 | 0.027
0.112 | 0.088 | 0.068 | 0.050 | 0.038 | 0.031 | 0.026 | 0.024
larger scan index

## Slide 10: Proposed Scanning Orders for 16x16 TU
Horizontal scanning order
Vertical scanning order is the transposition of horizontal scanning order
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 11: Proposed Scanning Order for 32x32 TU
Horizontal scanning order
Vertical scanning order is the transposition of horizontal scanning order
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 12: Proposed Mapping Table
0: zigzag
1: modified horizontal scanning order
2: modified vertical scanning order
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 13: Extension 2 – MDCS for CABAC
The 4x4 sub-block partition for absolute value is kept
Reverse 4x4 MDCS is applied for each sub-block
Copyright © MediaTek Inc. All rights reserved.
<number>
Zigzag: 0
Horizontal: 1
Vertical: 2

## Slide 14: Outline
Introduction
Proposed method
Simulation results
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 15: Simulation Results
Anchor – HM3.0
Test two extensions
  A: modified MDCS for 16x16 and 32x32
  B: MDCS for coding absolute values in CABAC
Three experiments: “A”, “B” and “A+B” for HE-AI and LC-AI
Thank Samsung for crosschecking (JCTVC-F646)
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 16: Simulation Results
Experimental results of A
Copyright © MediaTek Inc. All rights reserved.
<number>
 | HE-AI |  |  | LC-AI |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.2% | -0.2% | -0.3% | -0.7% | -0.6%
Class B | -0.1% | -0.6% | -0.6% | -0.9% | -1.4% | -1.4%
Class C | -0.1% | -0.3% | -0.3% | -0.2% | -0.5% | -0.6%
Class D | -0.1% | -0.3% | -0.2% | -0.4% | -0.5% | -0.4%
Class E | -0.5% | -1.0% | -1.0% | -1.2% | -1.8% | -1.5%
All Avg | -0.1% | -0.5% | -0.4% | -0.6% | -1.0% | -0.9%
Enc Time (%) | 100% |  |  | 100% |  | 
Dec Time (%) | 101% |  |  | 100% |  | 
Crosscheck | HE-AI | LC-AI
Enc Time (%) | 100% | 100%
Dec Time (%) | 100% | 99%

## Slide 17: Simulation Results
Experimental results of B
Copyright © MediaTek Inc. All rights reserved.
<number>
 | HE-AI |  | 
 | Y | U | V
Class A | -0.1% | 0.0% | -0.1%
Class B | -0.1% | 0.0% | -0.1%
Class C | -0.1% | -0.1% | -0.1%
Class D | -0.2% | -0.1% | -0.1%
Class E | -0.1% | -0.1% | 0.0%
All Avg | -0.1% | -0.1% | -0.1%
Enc Time (%) | 100% |  | 
Dec Time (%) | 101% |  | 
Crosscheck | HE-AI
Enc Time (%) | 100%
Dec Time (%) | 100%

## Slide 18: Simulation Results
Experimental results of A+B
Copyright © MediaTek Inc. All rights reserved.
<number>
 | HE-AI |  |  | LC-AI |  | 
 | Y | U | V | Y | U | V
Class A | -0.1% | -0.3% | -0.2% | -0.3% | -0.7% | -0.6%
Class B | -0.2% | -0.8% | -0.7% | -0.9% | -1.4% | -1.4%
Class C | -0.2% | -0.4% | -0.4% | -0.2% | -0.5% | -0.6%
Class D | -0.2% | -0.5% | -0.4% | -0.4% | -0.5% | -0.4%
Class E | -0.6% | -1.1% | -1.1% | -1.2% | -1.8% | -1.5%
All Avg | -0.3% | -0.6% | -0.5% | -0.6% | -1.0% | -0.9%
Enc Time (%) | 100% |  |  | 100% |  | 
Dec Time (%) | 102% |  |  | 100% |  | 
Crosscheck | HE-AI | LC-AI
Enc Time (%) | 99% | 100%
Dec Time (%) | 99% | 100%

## Slide 19: Conclusions
An extended MDCS method is proposed
  Modified MDCS is applied for 16x16 and 32x32
  MDCS is also applied for scanning absolute values in CABAC
Average BD-rate reductions of 0.3% and 0.6% for HE-AI and LC-AI respectively
The run time is almost the same as that of HM3.0
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 20
Copyright © MediaTek Inc. All rights reserved.
Thank you
Notes: <number>