## Slide 1: Progressive MV Resolution
Jicheng An, Xiang Li, Xun Guo and Shawmin Lei
JCTVC-F125
Copyright © MediaTek Inc. All rights reserved.
Presented by X. Li
6th JCT-VC Meeting in Torino
14-22 July, 2011
Notes: <number>

## Slide 2: Overall Summary
Higher MV resolution is employed when MV is close to MVP
  MV resolution is adaptively selected among 1/2 , 1/4, and 1/8-pixel
  Predefined thresholds are used to delimit regions with different MV resolutions.
  The thresholds can be adaptively adjusted for each reference picture at slice level.
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Mandatory Tests |  |  |  |  | Optional Tests |  | 
 | RAHE | RALC | LBHE | LBLC | Aver | LPHE | LPLC | Aver
Y | -0.7 | -1.1 | -0.8 | -1.3 | -1.0 | -3.0 | -2.6 | -2.8
U | -1.1 | -1.2 | -1.1 | -0.9 | -1.1 | -2.7 | -0.5 | -1.6
V | -1.1 | -1.2 | -1.5 | -0.6 | -1.1 | -2.8 | -0.1 | -1.4
Enc. T. | 97% | 95% | 94% | 92% | 95% | 98% | 97% | 98%
Dec. T. | 102% | 105% | 99% | 102% | 102% | 101% | 102% | 102%

## Slide 3: Outline
General idea
Region Centers of Different MV Resolutions
MV resolution adaptation based on thresholds
Interpolation for 1/8-pixel resolution
Threshold adaptation at slice level
Simulation results
Conclusions
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 4: General Idea
Copyright © MediaTek Inc. All rights reserved.
<number>
Higher MV resolution is employed when MV is close to MV predictor
Not all 1/8-pixel and 1/4-pixel positions for MVD have to be coded. Thus more efficient MVD representation can be obtained.

## Slide 5: Region Centers of Different MV Resolutions
Region centers of different MV resolutions are derived from MVP
Note that the centers may not coincide with MVP
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 6: MV Resolution Adaptation based on Thresholds
Skip and merge modes always have the highest MV resolution (1/8-pixel) since MVD is always 0 and doesn’t need to be sent.
MV resolution based on thresholds (TH1, TH0)
  TH1=TH0=0,
    - 1/8-pixel resolution for skip and merge modes
    - 1/2-pixel resolution for normal inter modes
    - MVP of normal inter mode has to be converted to 1/2-pixel accuracy if the MVP has higher MV accuracy
  TH1>TH0=0,
    - 1/8-pixel resolution for skip and merge modes
    - Up to 1/4-pixel resolution for normal inter modes
    - MVP of normal inter mode has to be converted to 1/4-pixel accuracy if the MVP has higher MV accuracy
  TH1>TH0 >0,
    - 1/8-pixel resolution for skip and merge modes
    - Up to 1/8-pixel resolution for normal inter modes
    - No accuracy conversion is needed for MVP of normal inter mode
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 7: Interpolation for 1/8-Pixel Resolution
8-tap 6-bit DCT-IF for 1/8-pixel luma interpolation
4-tap 6-bit DCT-IF for 1/16-pixel chroma interpolation
The filters are similar to the current interpolation filters
Copyright © MediaTek Inc. All rights reserved.
<number>
Position | Filter Coefficients |  |  |  |  |  |  | 
1/8 | {-1, | 3, | -6, | 62, | 9, | -4, | 2, | -1}
3/8 | {-2, | 5, | -12, | 50, | 30, | -10, | 4, | -1}
Position | Filter Coefficients |  |  | 
1/16 | {-2, | 63, | 4 | -1}
3/16 | {-5, | 59, | 13 | -3}
5/16 | {-6, | 52, | 23, | -5}
7/16 | {-7, | 43, | 34, | -6}

## Slide 8: Threshold Adaptation at Slice Level
To further improve the coding efficiency, threshold pair (TH1, TH0) is adaptively selected among (4, 2), (4, 0) and (0, 0) for each reference picture at slice level.
  For low-delay configurations, reference pictures whose QPs are larger than that of the current slice, the threshold pair is always set to (0, 0).
  For other cases, R-D cost reduction by sub-pixel ME of previously coded same-type slice is employed as selection criteria.
  In general, the larger the RD cost reduction by sub-pixel ME, the larger the MV resolution threshold pair is selected.
  See JCTVC-F125.doc for details.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 9: Simulation Results
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 10: Conclusions
Progressive MV resolution (PMVR) is proposed. MV resolution is progressively adjusted based on the magnitude of MV difference.
Performance of PMVR
  Mandatory tests (RA-HE, RA-LC, LB-HE, and LB-LC)
    1.0 luma BD-rate reduction
    5% encoding time saving
    2% decoding time increase
  Optional tests (LP-HE, and LP-LC)
    2.8 luma BD-rate reduction
    2% encoding time saving
    2% decoding time increase
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 11
Copyright © MediaTek Inc. All rights reserved.
Thank you !
Notes: <number>

## Slide 12
Copyright © MediaTek Inc. All rights reserved.
<number>
Algorithm 1: MVD encoding
input : MVD8, MVP8, CTR0, CTR1, TH0 and TH1 ouput : MVDc begin If ¦MVD8_x-CTR0_x¦<=TH0 and ¦MVD8_y-CTR0_y¦<=TH0, MVDc_x = MVD8_x; MVDc_y = MVD8_y; Else if the ¦MVD8_x-CTR1_x ¦ <=TH1 and ¦MVD8_y-CTR1_y ¦<=TH1, If ¦MVD8_x-CTR0_x¦>TH0, If MVD8_x-CTR0_x>=0 MVDc_x = (MVD8_x+CTR0_x+TH0)/2; Else MVDc_x = (MVD8_x+CTR0_x-TH0)/2; MVDc_y = (MVD8_y-CTR0_y)/2; Else If MVD8_y-CTR0_y>=0 MVDc_y = (MVD8_y+CTR0_y+TH0)/2; Else MVDc_y = (MVD8_y+CTR0_y-TH0)/2; MVDc_x = (MVD8_x-CTR0_x)/2; Else If ¦MVD8_x-CTR1_x¦>TH1, If MVD8_x-CTR1_x>=0, MVDc_x = (MVD8_x+2(CTR0_x+TH0)+CTR1_x+TH1)/4; Else MVDc_x = (MVD8_x+2(CTR0_x-TH0)+CTR1_x-TH1)/4; MVDc_y = (MVD8_y-CTR1_y)/4; Else If MVD8_y-CTR1_y>=0, MVDc_y = (MVD8_y+2(CTR0_y+TH0)+CTR1_y+TH1)/4; Else MVDc_y = (MVD8_y+2(CTR0_y-TH0)+CTR1_y-TH1)/4; MVDc_x = (MVD8_x-CTR1_x)/4.
end

## Slide 13
Copyright © MediaTek Inc. All rights reserved.
<number>
Algorithm 2: MV Resolution Threshold Adaptation at Slice Level
input : RDCost0, RDCost2, RDCost4, RDCost8 output : TH1, TH0 begin if the first inter slice set (TH1, TH0) to (4,0) else set (TH1, TH0) to that of the previously coded slice RDCReduc0=(RDCost0-RDCost2)/RDCost0; RDCReduc1=(RDCost2-RDCost4)/RDCost2; RDCReduc2=(RDCost4-RDCost8)/RDCost4; if (TH1, TH0) of the previously coded slice is (4, 0) RDTH = max(RDCReduc0*0.2,0.5%); if RDCReduc1<RDTH && RDCReduc0<8% set (TH1, TH0) to (0, 0); set RDTH= RDCReduc0*min(RDTH/ RDCReduc1, 1.5); //used for following inter slices else if (RDCReduc1>6%) ¦¦ (RDCReduc1>3% && RDCReduc1> RDCReduc0*0.4) set (TH1, TH0) to (4, 2). else if (TH1, TH0) of the previously coded slice is (0, 0) if RDCReduc0>min(RDTH, 8%) set (TH1, TH0) to (4, 0) else if (TH1, TH0) of the previously coded slice is (4, 2) if (RDCReduc2<1%) ¦¦ ((RDCReduc2<2% && RDCReduc2< RDCReduc1*0.4) set (TH1, TH0) to (4, 0)
end

## Slide 14: PMVR with Fixed Threshold (4, 2)
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 15: PMVR with Fixed Threshold (4, 0)
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 16: PMVR with Fixed Threshold (0, 0)
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 17: PMVR without 1/8-Pixel Resolution and Threshold Adaptation (TH1=2)
Copyright © MediaTek Inc. All rights reserved.
<number>