## Slide 1: JCTVC-F126: CE6.e Mode-dependent intra smoothing modifications
Geert Van der Auwera, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Introduction
CE6.e on intra smoothing
MDIS modifications proposed:
  Updated decision mapping table
  Inclusion of planar mode

## Slide 3: Intra Smoothing Decision Mapping
Statistics collected from RDO mode decision of intra smoothing filtering ([1 2 1] or no filtering)

## Slide 4: Intra Smoothing Decision Mapping
Updated MDIS table:
PU\Mode | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34
4x4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8x8 |  |  |  | 1 |  |  | 1 |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1
16x16 |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  | 1 | 1 | 1 | 1 | 1 | 1 |  |  | 1 | 1 | 1 | 1
32x32 |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 5: Results
Compared to HM3:
  “BasketballDrill” sequence (class C): -0.9% (HE), -1.8% (LC)
Compared to HM3 with HM3-MDIS off:
Proposed to adopt modifications for MDIS into HM4
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.5 | -0.7 | -0.9 | -0.8 | -0.6 | -0.9
Class B | -0.3 | -0.5 | -0.4 | -0.4 | -0.3 | -0.2
Class C | -0.1 | -0.3 | -0.3 | -0.1 | -0.2 | -0.3
Class D | -0.1 | -0.2 | -0.2 | -0.1 | -0.1 | -0.1
Class E | -0.4 | -0.8 | -0.7 | -0.6 | -0.8 | -0.7
Overall | -0.3 | -0.5 | -0.5 | -0.4 | -0.4 | -0.4
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.09 | -0.28 | -0.23 | -0.13 | -0.14 | -0.19
Class B | -0.11 | -0.19 | -0.17 | -0.06 | -0.11 | -0.07
Class C | -0.23 | -0.33 | -0.32 | -0.43 | -0.34 | -0.46
Class D | -0.06 | -0.07 | -0.05 | -0.05 | -0.02 | -0.05
Class E | -0.11 | -0.28 | -0.22 | -0.06 | -0.31 | -0.29
Overall | -0.12 | -0.22 | -0.20 | -0.15 | -0.17 | -0.20
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 99% |  |