## Slide 1: Support of very low delay coding in Tile (JCTVC-F140, m20558)
6th JCT-VC meeting, Torino/Italy
2011/7/14-22
K.Kazui, S.Shimada, J.Koyama, and A.Nakagawa
FUJITSU LABORATORIES LTD.

## Slide 2: Summary
We have proposed the high-level syntax/semantics for minimizing the loss of coding efficiency in very low delay coding.
  The proposal is motivated by the request of interoperable high-quality low delay coding from the broadcasting industry.
  The minimal loss is achieved by the restriction of reference from the refreshed area to the non-refreshed area in a picture.
The tile scheme and our proposal have the common feature of sub-picture partitioning.
The tile scheme can support very low delay coding by extending the specification of the coding order of a CU.
  The current specification defines the coding order as the raster-scan within a tile for ease of the parallel tile processing. It has 1 frame delay.
  1 frame delay is removed by the raster-scan within a picture.
We propose the enhancement of the tile scheme.
  Additional low delay operation mode in which the coding order is the raster-scan within a picture.
  Additional syntax which flexibly describes the restriction of reference.

## Slide 3: Very low delay coding (1/2)
Low delay operation less than 1 frame period.
  The delay less than 100ms is required for real-time bi-directional communication.
  Equipments with 10ms delay have emerged for better user experience.
The vertical intra MB line refresh scheme
  Picture refresh is realized by circulating an intra MB line inside a picture.
    #bits of each picture is averaged. Minimum delay B is ( bitrate / frame_rate ).
    The use of I-Picture is not suitable because the fluctuation of #bits of picture is large.
  The intra MB line is inserted vertically in a picture for the delay less than 10ms.
    #bits of each MB line is averaged. Minimum delay B’ is (B / num_MBlines ).
Vertical Intra MB Line Refresh

## Slide 4: Very low delay coding (2/2)
Problem of very low delay coding in HEVC
  The restriction of reference at the area boundary is necessary.
    Pixels in the non-refreshed area may not be correctly decoded when the decoding process starts from a recovery point.
    Reference from the refreshed area to the non-refreshed area is prohibited for intra prediction, inter-prediction, and in-loop filtering for correct reconstruction.
  In-loop filtering needs the restriction both in encoder and decoder.
  The loss of coding efficiency caused by the restriction is large.
    Two possible means to do the restriction, 1) the insertion of slice boundary at each LCU line, and 2) disabling in-loop filtering in a picture, cause the significant loss.
Chart: BQMall
| 8009.5602000000044 | 4099.2505000000001 | 2196.5328 | 1155.9686000000011
Conventional (Case 1) | 39.8553 | 36.8872 | 33.7843 | 30.6985
Proposed | 39.8513 | 36.8834 | 33.8031 | 30.7674
Degradation by inserting slice per LCU row (JCTVC-C021)
Degradation by enabling in-loop filtering at area boundary (JCTVC-E061)
Slice per LCU line
No slice

## Slide 5: Proposal in JCTVC-D053
A picture is divided into a refreshed area and a non-refreshed area.
  refresh_direction@SPS and boundary_position@SH are added.
  Both areas and their index IdxR, IdxN (< IdxR) are derived.
The asymmetric restriction of reference among areas is introduced.
  A neighboring LCU LcuNeighbor is defined as “not available” if ( getIndex(LcuCurr) < getIndex(LcuNeighbor) ) is true.
    Function getIndex(LcuX) returns the index of the area to which LCU LcuX belongs.
New buffer model for interoperable very low delay coding
  The nominal removal time of each LCU line(s) dtg( n, i ) is defined.
Proposed syntax and semantics
Proposed new buffer model

## Slide 6: Support of very low delay coding in Tile (1/2)
Tile proposal (JCTVC-E408, JCTVC-F335)
  A picture is divided into rectangle regions.
  The reference among regions is restricted. (globally controlled by a flag)
Tile can describe the sub-picture partitioning in JCTVC-D053.
The tile scheme (Example of 4 sub-pictures)
Sub-picture partitioning in JCTVC-D052 described by tile syntax

## Slide 7: Support of very low delay coding in Tile (2/2)
Tile can support very low delay coding by extending the specification of the coding order.
  The definition of the coding order in JCTVC-F335
    The coding order is the raster-scan order within a tile.
    This is necessary when the coding of each tile is processed independently in parallel.
    There is 1 frame delay (> 10ms@60Hz).
  The raster-scan order within a picture mitigates the delay.
Mitigation of coding delay by raster-scan order within a picture

## Slide 8: Proposed enhancement of tile (1/2)
Enhancement on entropy coding order
  Optional low delay operation mode in which the coding order is the raster-scan order within a picture is added.
    This optional mode is signaled in SPS or PPS.
    This optional mode does not enforce an entropy coder to initialize at a tile boundary.
  This optional mode makes scene for the parallel processing application if the processing of entropy coding and the processing of the rest of the encoding process are performed in different processing engines.
Example of low delay operation in parallel processing

## Slide 9: Proposed enhancement of tile (2/2)
Enhancement on restriction of reference between tiles
  Flexible restriction is realized.
    This mode is signaled using tile_boundary_independence_idc with a new value.
    This restriction supports the restriction according to the causality among tiles.
  Each tile is associated with an index signaled in SPS or PPS.
  The restriction is defined according to the indexes of tiles.
    A LCU in a tile with index A can refer to a LCU in a tile with index B if (B >= A)
Example of enhanced description of dependency among tiles

## Slide 10: Conclusion
We propose the enhancement of the tile scheme for supporting low delay coding.
Optional low delay operation mode in which the entropy coding order is the raster-scan order within a picture is added.
  Real-time bi-directional communication can be supported in addition to the existing tile applications such as encoder-side parallel processing, reduction of memory usage in ME, and bitstream packetization.
We request to adopt the proposed enhancement when the tile scheme is adopted.