## Slide 1
Improvement on the derivation process for luma motion vector prediction(JCTVC-F142, m20560)
S.Shimada, K.Kazui, J.Koyama, and A.Nakagawa
FUJITSU LABORATORIES LTD.
Copyright 2011 FUJITSU LIMITED
Notes: <number>

## Slide 2: Overview
We propose two modifications for the motion vector prediction of AMVP/Merge/Skip.
  Scheme1： minor modification of the scaling mv predictor
  Proposed scheme rounds half towards zero.
  Scheme2： modification of the derivation process of temporal mv predictor
  Select the temporal mv predictor between two candidates.
Performance
  Coding gain is up to 2.0%.
  Average coding gain in Class D RA(HE, LC) is 0.9%.
  Average coding gain in overall RA(HE, LC) is 0.5%.
  Increase of Enc/Dec time is negligible.
Sign(DistScaleFactor ・ mv) ・ (( abs(DistScaleFactor ・ mv )+ 127 ) >> 8 )
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 3: Scheme1: Modification of scaling mv predictor
  Modify rounding process of the scaling mv predictor
  Rounding control is important to obtain a precise mv predictor.
  DistScaleFactor ： scaling factor
HM3 | ( DistScaleFactor ・ mv + 128 ) >> 8
Proposed Scheme | Sign(DistScaleFactor ・ mv) ・ (( abs(DistScaleFactor ・ mv ) + 127 ) >> 8 )
  HM3 rounds half towards plus infinity.
  Proposed scheme rounds half towards zero.
  Our modification is very simple.
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 4: Scheme2: Modification of temporal mv predictor
Outline
  Select the temporal mv predictor between two MvCol candidates.
Select two colPu candidates TA and TB
  4x4 blocks share the same mv of a representative block (MV Buffer Compression:JCTVC-D072)
  TA： the nearest representative block of center block C
  TB： the right-below representative block of center block C ( if TA is right-below block, TB is left-above block)
TA
TB
TA
TB
TA
TB
TB
TA
C
C
C
C
C
Position of TA and TB according to the position of C
Position of Center Block C
Current PU
Representative block of Mv Buffer Compression
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 5: Scheme2: Modification of temporal mv predictor
  LA
  LB
  Determine temporal mv predictor between two MvCol candidates MvColCandA / MvColCandB of TA and TB.
  Calculate a cross-point between MvColCandA / MvColCandB and current picture, and then calculate the distance LA / LB between the cross-point and center block C, respectively.
  Select the MvCol candidate that has a smaller L value as the temporal mv predictor.
TA
TB
Col-Picture
Current Picture
C
MvColCandA
MvColCandB
MvCol = LA > LB ? MvColCandB : MvColCandA
Copyright 2011 FUJITSU LIMITED
<number>
Notes: <number>

## Slide 6: Simulation Results（each sequence）
HM3.0(Anchor) vs. Proposed Schemes
BDBitrate(%)
Copyright 2011 FUJITSU LIMITED
<number>

## Slide 7: Simulation Results（Scheme1）
HM3.0(Anchor) vs. Scheme1
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1 | -0.3 | -0.1 | 0.0 | 0.0 | 0.1
Class B | -0.2 | -0.2 | -0.1 | -0.3 | 0.0 | 0.0
Class C | -0.4 | -0.2 | -0.1 | -0.4 | -0.1 | -0.3
Class D | -0.8 | -0.3 | -0.4 | -0.8 | -0.4 | -0.4
Class E |  |  |  |  |  | 
Overall | -0.4 | -0.2 | -0.2 | -0.4 | -0.1 | -0.1
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.3 | 0.0 | 0.0 | 0.0 | -0.1
Class C | -0.1 | 0.1 | 0.0 | -0.1 | 0.0 | 0.0
Class D | -0.1 | 0.2 | 0.2 | 0.0 | -0.1 | 0.1
Class E | 0.0 | 0.0 | -0.1 | 0.0 | -0.1 | -0.2
Overall | -0.1 | 0.2 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 103% |  |  | 102% |  | 
Copyright 2011 FUJITSU LIMITED
<number>
Notes: <number>

## Slide 8: Simulation Results（Scheme1＋Scheme2）
HM3.0(Anchor) vs. Scheme1+Scheme2
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1 | -0.2 | 0.2 | -0.1 | 0.0 | 0.1
Class B | -0.4 | -0.2 | -0.1 | -0.4 | -0.1 | -0.1
Class C | -0.6 | -0.3 | -0.3 | -0.5 | -0.3 | -0.4
Class D | -0.9 | -0.7 | -0.8 | -0.9 | -0.6 | -0.5
Class E |  |  |  |  |  | 
Overall | -0.5 | -0.3 | -0.2 | -0.5 | -0.3 | -0.2
Enc Time[%] | 101% |  |  | 99% |  | 
Dec Time[%] | 95% |  |  | 95% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1 | 0.0 | 0.2 | 0.0 | -0.1 | -0.4
Class C | -0.1 | -0.1 | -0.1 | -0.1 | -0.1 | -0.2
Class D | -0.1 | -0.1 | 0.6 | 0.0 | 0.0 | -0.1
Class E | -0.1 | 0.3 | -0.5 | -0.3 | -0.6 | -0.8
Overall | -0.1 | 0.0 | 0.1 | -0.1 | -0.2 | -0.4
Enc Time[%] | 102% |  |  | 99% |  | 
Dec Time[%] | 97% |  |  | 97% |  | 
Copyright 2011 FUJITSU LIMITED
<number>
Notes: <number>

## Slide 9: Conclusion
We proposed two modifications for the motion vector prediction of AMVP/Merge/Skip.
Performance
  Coding gain is up to 2.0%.
  Average coding gain in Class D RA(HE, LC) is 0.9%.
  Average coding gain in overall RA(HE, LC) is 0.5%.
  Increase of Enc/Dec time is negligible.
Cross-verified with JCTVC-F183 from Mitsubishi Electric
We suggest to adopt the proposed modifications to HM.
Copyright 2011 FUJITSU LIMITED
<number>
Notes: <number>

## Slide 10
<number>

## Slide 11: Appendix: Scheme1 vs Scheme1+Scheme2
Scheme1(Anchor) vs Scheme1+Scheme2
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0 | 0.0 | 0.3 | 0.0 | 0.0 | 0.0
Class B | -0.2 | 0.0 | 0.0 | -0.1 | -0.1 | -0.1
Class C | -0.2 | -0.1 | -0.1 | -0.1 | -0.2 | -0.1
Class D | -0.2 | -0.4 | -0.4 | -0.2 | -0.2 | -0.1
Class E |  |  |  |  |  | 
Overall | -0.1 | -0.1 | -0.1 | -0.1 | -0.1 | -0.1
Enc Time[%] | 102% |  |  | 100% |  | 
Dec Time[%] | 96% |  |  | 94% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0 | -0.3 | 0.2 | 0.0 | -0.1 | -0.3
Class C | 0.0 | -0.3 | -0.2 | 0.0 | -0.2 | -0.2
Class D | 0.0 | -0.3 | 0.4 | 0.0 | 0.1 | -0.3
Class E | 0.0 | 0.2 | -0.3 | -0.3 | -0.6 | -0.7
Overall | 0.0 | -0.2 | 0.1 | -0.1 | -0.2 | -0.3
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 94% |  |  | 95% |  | 
Copyright 2011 FUJITSU LIMITED
<number>