## Slide 1: Signaling of Max and Min QP in slice
Kazuo Sugimoto, Shun-ichi Sekiguchi
Mitsubishi Electric Corporation
JCTVC-F174

## Slide 2: Summary
Proposed method
  Signal Maximum and Minimum QP within a slice at the slice header
  dQP Indexing is done by assigning smaller index value to possible smaller absolute value
  VLC table or binarization of the size of dQP dynamic range in a slice is used
Results (delta QP bit reduction)
2.6%, 3.5% and 4.4% for AI/RA/LD(HE)
8.2%,10.3% and 11.0% for AI/RA/LD(LC)

## Slide 3: Proposed method
Signal Maximum and Minimum QP within a slice at the slice header
Signal dQP
  New indexing exploiting dynamic range of dQP specified by MaxQP and MinQP
    MaxQP – MinQP = dQP_range
    Current_QP = Ref_QP + dQP
  VLC table or binarization table with maximum index is dQP_range is used

## Slide 4: Indexing exploiting dynamic range of dQP in a slice
Example: Max QP=37, Min QP = 25, Ref_QP = 23
dQP value | Conventional Indexing | Proposed Indexing
0 | 0 | 0
1 | 1 | 1
-1 | 2 | 2
2 | 3 | 3
-2 | 4 | 4
3 | 5 | 5
4 | 7 | 6
5 | 9 | 7
6 | 11 | 8
7 | 13 | 9
8 | 15 | 10
9 | 17 | 11
10 | 19 | 12

## Slide 5: CABAC coding
Use Trancated Unary binarization instead of Unary binarization.
Max value = MaxQP-MinQP

## Slide 6: CAVLC coding
Use concatenated truncated Golomb code instead of SVLC

## Slide 7
1
010
011
00100
00101
00110
00111
0001000
0001001
0001010
0001011
0001100
0001101
0001110
0001111
000010000
000010001
：
：
Max Value
Concatinated Truncated Golomb Code

## Slide 8
1
010
011
00100
00101
00110
00111
0001000
0001001
0001010
0001011
0001100
0001101
0001110
0001111
000010000
000010001
：
：
First, delete this code
Max Value

## Slide 9
1
010
011
00100
00101
00110
00111
Delete the “1”
Max Value

## Slide 10
1
010
011
0000
0001
0010
0011
Max Value
Truncated Golomb code

## Slide 11
1
010
011
0000
0001
0010
0011
0011
0011
0011
0011
0011
0011
Max Value
truncated Golomb of Max=6
1
010
011
0000
0001
0010
0011

## Slide 12
1
010
011
0000
0001
0010
0011
0011
0011
0011
0011
0011
0011
Max Value
1
010
011
0000
0001
0010
0011

## Slide 13
1
010
011
0000
0001
0010
0011
0011
0011
0011
0011
0011
0011
1
010
011
0000
0001
0010
0011
dQP | Conventional Index | Proposed Index | Bits for Conventional method | Bits with only change of indexing | Bits for proposed method
0 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 3 | 3 | 3
-1 | 2 | 2 | 3 | 3 | 3
2 | 3 | 3 | 5 | 5 | 4
-2 | 4 | 4 | 5 | 5 | 4
3 | 5 | 5 | 5 | 5 | 4
4 | 7 | 6 | 7 | 5 | 5
5 | 9 | 7 | 7 | 7 | 7
6 | 11 | 8 | 7 | 7 | 7
7 | 13 | 9 | 7 | 7 | 8
8 | 15 | 10 | 9 | 7 | 8
9 | 17 | 11 | 9 | 7 | 8
10 | 19 | 12 | 9 | 7 | 8

## Slide 14: Simulations
software for CE4 (with TM5 step 3) is used
MaxCuDQPDepth = 3

## Slide 15: Test results

## Slide 16: Test results

## Slide 17: Test results

## Slide 18: Conclusion
Proposed method
  Signal Maximum and Minimum QP within a slice at the slice header
  dQP Indexing is done by assigning smaller index value to possible smaller absolute value
  VLC table or binarization of the size of dQP dynamic range in a slice is used
Results (delta QP bit reduction)
2.6%, 3.5% and 4.4% for AI/RA/LD(HE)
8.2%,10.3% and 11.0% for AI/RA/LD(LC)
Propose signaling MaxQP and MinQP at the slice header