## Slide 1: Improved PIPE/V2F for low complexity entropy coding
Ryoji Hattori, Kazuo Sugimoto,
Shun-ichi Sekiguchi, Kohtaro Asai
Mitsubishi Electric Corporation
JCTVC-F176

## Slide 2: Introduction
In the 19th century, Morse initiated to use VLC for transmitting textual information as series of on-off tones.
In the 20th century, people began using arithmetic coding, and one of them is adopted to the state-of-the-art video coding standard “MPEG-4 AVC/H.264”.

## Slide 3: Introduction
Now we are in 21st century, and here is an entropy coding for this century instead of legacy codings.
This proposal realizes it with PIPE/V2F
High Efficient
Fixed Length Coding

## Slide 4: Summary
Proposed method
  11 V2F coders generating 4bit fixed length code and 2 V2F coders generating 8bit fixed length code are used.
  The 8bit-V2F coders does not need memory to store the VLC tables, as the input are 8-bit fixed length bins or unary bins which are easily converted to bits.
  Context derivations, probability state updates, etc., are identical to those of CABAC.
Results for AI/RA/LD(LC)
BD-rate: -3.9%, -4.3% and -3.2%
DEC time: 110%, 101% and 100%

## Slide 5: Summary cont.
V2F coders are used on top of HE-PIPE in JCTVC-F268
six 4bit-V2F coders and two 8bit-V2F coders are used
Results for AI/RA/LD(LC)
BD-rate: -3.0%, -3.2% and -2.3%
DEC time: 101%, 99% and 97%

## Slide 6: Proposed method

## Slide 7: PIPE / V2F in JCTVC-D106
Same as CABAC
All V2F coders generate 4 bit FLC.
binarization
state
update
input bin
generation
：
：
bin buffer
bin buffer
bin buffer
：
V2F
coder#0
V2F
coder#10
V2F
Coder#11
MUX
0000
000000
0001
000001
0010
00001
0011
00010
0100
00011
0101
00100
0110
00101
0111
0011
1000
0100
1001
0101
1010
011
1011
1000
1100
1001
1101
101
1110
110
1111
111
FLC
bin
0000
000000
0001
000001
0010
00001
0011
00010
0100
00011
0101
00100
0110
00101
0111
0011
1000
0100
1001
0101
1010
011
1011
1000
1100
1001
1101
101
1110
110
1111
111
bins
0000
0000
0001
0001
0010
0010
0011
0011
0100
0100
0101
0101
0110
0110
0111
0111
1000
1000
1001
1001
1010
1010
1011
1011
1100
1100
1101
1101
1110
1110
1111
1111
FLC
bin
0000
0000
0001
0001
0010
0010
0011
0011
0100
0100
0101
0101
0110
0110
0111
0111
1000
1000
1001
1001
1010
1010
1011
1011
1100
1100
1101
1101
1110
1110
1111
1111
bins
V2F
Table#0
V2F
Table #1
V2F
Table #
10
V2F
Table #11
0000
000000000
0001
000000001
0010
00000001
0011
0000001
0100
000001
0101
00001
0110
0001
0111
0010
1000
0011
1001
0100
1010
0101
1011
011
1100
1000
1101
1001
1110
101
1111
11
FLC
bin
0000
000000000
0001
000000001
0010
00000001
0011
0000001
0100
000001
0101
00001
0110
0001
0111
0010
1000
0011
1001
0100
1010
0101
1011
011
1100
1000
1101
1001
1110
101
1111
11
bins
0000
000000000000000
0001
000000000000001
0010
00000000000001
0011
0000000000001
0100
000000000001
0101
00000000001
0110
0000000001
0111
000000001
1000
00000001
1001
0000001
1010
000001
1011
00001
1100
0001
1101
001
1110
01
1111
1
FLC
bin
0000
000000000000000
0001
000000000000001
0010
00000000000001
0011
0000000000001
0100
000000000001
0101
00000000001
0110
0000000001
0111
000000001
1000
00000001
1001
0000001
1010
000001
1011
00001
1100
0001
1101
001
1110
01
1111
1
bins
…

## Slide 8
V2Fテーブル11
15bin  4bit
= 0.267 bit/bin
The loss in the highest probability is large.
V2F
Table #11
0000
000000000000000
0001
000000000000001
0010
00000000000001
0011
0000000000001
0100
000000000001
0101
00000000001
0110
0000000001
0111
000000001
1000
00000001
1001
0000001
1010
000001
1011
00001
1100
0001
1101
001
1110
01
1111
1
FLC
bin
0000
000000000000000
0001
000000000000001
0010
00000000000001
0011
0000000000001
0100
000000000001
0101
00000000001
0110
0000000001
0111
000000001
1000
00000001
1001
0000001
1010
000001
1011
00001
1100
0001
1101
001
1110
01
1111
1
bins

## Slide 9: PIPE / V2F in F176
V2F #12 | 
1 (no ‘0’s and a ‘1’) 01 (a ‘0’ and a ‘1’) 001 (2 ‘0’s and a ‘1’) 0001 (3 ‘0’s and a ‘1’) 00001 (4 ‘0’s and a ‘1’) 000001 (5 ‘0’s and a ‘1’) : : 00000000000000000000…..00000000000000000001 (254 ‘0’s and a ‘1’) 00000000000000000000…..00000000000000000000 (255 ‘0’s) | 00000000 00000001 00000010 00000011 00000100 00000101 : : 11111110 11111111
255bin  8bit
= 0.031 bit/bin
An additional V2F coder for the highest probability

## Slide 10: Other modifications
V2F coder #0 also generates 8bit FLC
V2F coder #0 and #12 does not use tables.
  V2F #0 simply copy input bins as output bits
    Successive equal probability bins are converted to bits at once
  V2F #12 counts the number of successive“0”s. The number becomes output bits
Context derivations, probability state updates, etc., are identical to those of CABAC.

## Slide 11: Simulations
Improved V2F on top of HM-3.0
Improved V2F on top of HE-PIPE in F268

## Slide 12: Results vs HM-3.0

## Slide 13: Results vs HM-3.0

## Slide 14: Results vs HM-3.0

## Slide 15: Results HE-PIPE/V2F vs HM-3.2

## Slide 16: Results HE-PIPE/V2F vs HM-3.2

## Slide 17: Results HE-PIPE/V2F vs HM-3.2

## Slide 18: Conclusion
Proposed method
  An additonal 8bit-V2F coder for the highest probability bins is introduced.he 8bit-V2F coders does not need memory to store the VLC tables, as the input are 8-bit fixed length bins or unary bins.
  Context derivations, probability state updates, etc., are identical to those of CABAC.
Results of HM-3.0 PIPE/V2F for AI/RA/LD(LC)
BD-rate: -3.9%, -4.3% and -3.2%
DEC time: 110%, 101% and 100%
Results of F268 HE-PIPE with V2F for AI/RA/LD(LC)
BD-rate: -3.0%, -3.2% and -2.3%
DEC time: 101%, 99% and 97%
Propose CAVLC to be replaced by PIPE/V2F