## Slide 1: JCTVC –F184 Evaluation of PU-level vs TU-level intra prediction
R&D
© BBC MMXI
Andrea Gabriellini, Marta Mrak
BBC

## Slide 2: Intra prediction in HM3.1
intra prediction direction signalled at PU level
actual prediction performed at TU level, from neighbouring TUs
  serial dependencies at both encoder and decoder side
evaluation of performance of intra prediction performed at PU-level while maintaining TU quadtree split
  remove dependencies at TU level
prediction direction
PU
 4 TUs
Luma block coding example

## Slide 3: PU-level intra prediction
one intra prediction choice per PU
intra prediction signal generated for the whole PU
TU partitioning applied to residual from PU-level intra prediction
PU
prediction direction
 4 TUs

## Slide 4: Results for PU-level intra prediction
HM3.1 vs HM3.1 with PU-level intra prediction
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.2 | -0.7 | -0.8 | 0.3 | -1.2 | -1.1
Class B | 0.2 | 0.1 | 0.4 | 0.6 | -0.2 | -0.1
Class C | 0.2 | 0.1 | 0.1 | 0.3 | 0.1 | 0.0
Class D | 0.1 | 0.1 | 0.2 | 0.2 | 0.1 | 0.1
Class E | 0.4 | 0.4 | 0.5 | 0.8 | -1.0 | -0.8
Overall | 0.2 | 0.0 | 0.0 | 0.4 | -0.4 | -0.3
Enc Time[%] | 98% |  |  | 97% |  | 
Dec Time[%] | 96% |  |  | 92% |  | 
decoding complexity reduction
  related to processing of decoded samples from which a prediction signal is generated

## Slide 5: Conclusions
an evaluation of TU-level and PU-level prediction strategies is reported
  expected loss in performance is observed, however, limited to the luminance only
the bottleneck in intra prediction can be partially reduced by PU-level prediction
some of the related topics
  luma and chroma prediction strategies
  SDIP
  parallel intra