## Slide 1: A further improvement of inter prediction direction and reference frame index combined coding in CAVLC
Bin Li, Jizheng Xu, Houqiang Li
University of Science and Technology of China
Microsoft

## Slide 2: Combined coding of inter prediction direction and reference frame index
Improved by JCTVC-E381
Current Design
  NumPredRefLC = Min( 4, num_lc ) NumPredRefL0 = Min( 2, num_l0 ) NumPredRefL1 = Min( 2, num_l1 )
  MaxPredRef = NumPredRefLC + NumPredRefL0 * NumPredRefL1

## Slide 3: Small bug
In calculating maximum value
Last entry (exception) does not exist all the time
num_lc <= 4 && num_l0 <= 2 && num_l1 <= 2 no exception, the maximum value should be decreased by 1

## Slide 4: Experimental Results
Default Configuration, no gain or loss
 | RA_LC | LD_LC
Class A | 0.0 | 
Class B | 0.0 | 0.0
Class C | 0.0 | 0.0
Class D | 0.0 | -0.1
Class E |  | 0.0
All | 0.0 | 0.0
Enc Time | 100% | 101%
Dec Time | 101% | 101%

## Slide 5: One reference frame Result
The maximum value is small, 0.2% gain
 | RA_LC | LD_LC
Class A | -0.2 | 
Class B | -0.2 | -0.2
Class C | -0.3 | -0.1
Class D | -0.3 | -0.2
Class E |  | -0.1
All | -0.2 | -0.2
Enc Time | 101% | 101%
Dec Time | 101% | 101%

## Slide 6: Adaptive combined coding
In HM3, to combined code ref idx/dir or not depends on the upper and left CUs
It is more natural to make it PU-based, i.e., based on the upper and left Pus, since ref idx/dir are on PU level

## Slide 7: Results for PU-based adaptation
 | RA_LC | LD_LC
Class A | 0.0 | 
Class B | 0.0 | 0.0
Class C | 0.0 | 0.0
Class D | 0.0 | -0.1
Class E |  | 0.1
All | 0.0 | 0.0
Enc Time | 102% | 100%
Dec Time | 99% | 99%

## Slide 8: Conclusion
Suggest to accept this bug fix on the calculation of maximum value
Suggest to use PU-based adaptation instead of CU-based adaptation
Thank Samsung for cross-checking

## Slide 9
Thank you!