## Slide 1
<number>
JCTVC-F216 (CE3): eBrisk’s Adaptive Interpolation Filtering Technique
Michael Horowitz, eBrisk Video
6th JCTVC Meeting in Torino
14-22 July 2011
Notes: <number>

## Slide 2: HM 3.0 Interpolation (Luma)
<number>
¼ | -1, 4, -10, 57, 19, -7, 3, -1
½ | -1, 4, -11, 40, 40, -11, 4, -1
Sub-sample position | Vertical | Horizontal
ai.j | None | F_1/4
bi.j | None | F_1/2
ci.j | None | F_3/4
di.j | F_1/4 | None
ei.j | F_1/4 | F_1/4
fi.j | F_1/4 | F_1/2
gi.j | F_1/4 | F_3/4
hi.j | F_1/2 | None
ii.j | F_1/2 | F_1/4
ji.j | F_1/2 | F_1/2
ki.j | F_1/2 | F_3/4
ni.j | F_3/4 | None
pi.j | F_3/4 | F_1/4
qi.j | F_3/4 | F_1/2
ri.j | F_3/4 | F_3/4

## Slide 3: Proposed AIF Technique (Luma)
<number>
For each referenced video slice, select between the ½-pel default and new filters, and between the ¼-pel default and new filters.
Convey selected filters through luma_filter_mode_flag as follows:
The new filters are used only when the first picture of the most-referenced list (indicated by aif_ref_pic_list) is referenced.
¼ | {a0, a1, a2, a3, a4, a5, a6, a7}
½ | {b0, b1, b2, b3, b3, b2, b1, b0}
Luma_filter_mode_flag | F_1/4 | F_1/2
0 | Default | Default
1 | Default | AIF (New)
2 | AIF (New) | Default
3 | AIF (New) | AIF (New)
Same HM 3.0 Filtering Structure
Notes: Filter selection occurs at the slice level, Luma_filter_mode_flag is sent in slice header
<number>

## Slide 4: Proposed AIF Technique (Luma)
<number>
AIF Filter Generation:
  Step 1: Estimate MVs using HM 3.0 filters
  Step 2: Determine most-referenced list
  Step 3: Estimate filter coefficient values by minimizing the energy of prediction errors after performing MC using MVs from Step 1
AIF Filter Transmission:
  Clip the filter coefficient values:
  Compute differences between the filter coefficient values and the corresponding HM 3.0 filter coefficient values
  Transmit differences
Coefficient index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
clip value | 7 | 15 | 31 | 63 | 63 | 31 | 15 | 7
Notes: Coefficients sent in the the slice header
<number>

## Slide 5: Simulation Results (Luma)
<number>
Class | Low Delay (P) HE |  |  | Low Delay (P) LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.14 | -0.16 | -0.25 | -2.65 | 0.29 | 0.12
Class C | -0.29 | -0.13 | -0.29 | -1.09 | -0.25 | -0.13
Class D | 0.01 | 0.01 | 0.01 | -0.61 | -0.27 | -0.13
Class E | -0.39 | 0.35 | -0.39 | -5.38 | -0.85 | -0.82
All | -0.25 | -0.01 | -0.31 | -2.26 | -0.20 | -0.18
Enc Time[%] | 104% (102%) |  |  | 107% (108%) |  | 
Dec Time[%] | 100% (100%) |  |  | 100% (100%) |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 6: Simulation Results (Luma)
<number>
Class | Low Delay (B) HE |  |  | Low Delay (B) LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.12 | 0.25 | -0.11 | -1.34 | 0.53 | 0.11
Class C | -0.13 | -0.15 | 0.03 | -0.61 | 0.04 | 0.04
Class D | 0.01 | 0.01 | 0.01 | -0.30 | -0.14 | 0.20
Class E | -0.16 | 0.32 | -0.41 | -2.78 | 0.04 | -0.51
All | -0.10 | 0.10 | -0.10 | -1.17 | 0.15 | 0.00
Enc Time[%] | 103%(103%) |  |  | 106% (108%) |  | 
Dec Time[%] | 100% (100%) |  |  | 100% (100%) |  | 

## Slide 7: Simulation Results (Luma)
<number>
Class | Random Access HE |  |  | Random Access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.33 | -0.35 | -0.14 | -1.31 | -0.25 | -0.42
Class B | 0.01 | -0.10 | -0.07 | -0.19 | -0.09 | -0.12
Class C | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Class D | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Class E |  |  |  |  |  | 
All | -0.07 | -0.11 | -0.05 | -0.36 | -0.08 | -0.13
Enc Time[%] | 102% (102%) |  |  | 103% (103%) |  | 
Dec Time[%] | 100% (100%) |  |  | 100% (100%) |  | 
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 8: Proposed AIF Technique (Chroma)
<number>
For each referenced video slice & for each of the ½-, ¼-, 1/8- and 3/8-pel filters, select between the default filter and the new filter (the new filters are used only when the first picture of the most-referenced list is referenced).
Convey selected filters through chroma_filter_mode_flag as follows:
Same HM 3.0 Filtering Structure
1/8 | {a0, a1, a2, a3}
1/4 | {b0, b1, b2, b3}
3/8 | {c0, c1, c2, c3}
1/2 | {d0, d1, d1, d0}

## Slide 9: Proposed AIF Technique (Chroma)
<number>
Chroma_filter_mode_flag | F_1/8 | F_1/4 | F_3/8 | F_1/2
0 | Default | Default | Default | Default
1 | Default | Default | Default | AIF (New)
2 | Default | Default | AIF (New) | Default
3 | Default | Default | AIF (New) | AIF (New)
4 | Default | AIF (New) | Default | Default
5 | Default | AIF (New) | Default | AIF (New)
6 | Default | AIF (New) | AIF (New) | Default
7 | Default | AIF (New) | AIF (New) | AIF (New)
8 | AIF (New) | Default | Default | Default
9 | AIF (New) | Default | Default | AIF (New)
10 | AIF (New) | Default | AIF (New) | Default
11 | AIF (New) | Default | AIF (New) | AIF (New)
12 | AIF (New) | AIF (New) | Default | Default
13 | AIF (New) | AIF (New) | Default | AIF (New)
14 | AIF (New) | AIF (New) | AIF (New) | Default
15 | AIF (New) | AIF (New) | AIF (New) | AIF (New)
Notes: We tried decoupling luma and chroma and the gains were not significant so we designed the algorithm to couple the decision as described.
<number>

## Slide 10: Proposed AIF Technique (Chroma)
<number>
AIF Filter Generation:
  Step 1 & Step 2 already performed in the Luma case
  Step 3: Estimate filter coefficient values by minimizing the energy of chroma prediction errors after performing MC using MVs from Step 1
AIF Filter Transmission:
  Compute differences between the filter coefficient values and the corresponding HM 3.0 default values
  Transmit differences
Notes: Step 1 = determine MVs and step 2 = determine most referenced list
<number>

## Slide 11: Simulation Results (Luma + Chroma)
<number>
Class | Low Delay (P) HE |  |  | Low Delay (P) LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.15 | -0.29 | -0.46 | -2.66 | -2.19 | -2.35
Class C | -0.25 | -0.01 | -0.23 | -1.00 | -0.47 | -0.50
Class D | 0.01 | 0.01 | 0.01 | -0.54 | -0.35 | -0.47
Class E | -0.24 | -1.60 | -2.20 | -4.84 | -13.49 | -8.85
All | -0.15 | -0.39 | -0.61 | -2.13 | -3.42 | -2.63
Enc Time[%] | 104% (102%) |  |  | 108% (109%) |  | 
Dec Time[%] | 100% (100%) |  |  | 100% (100%) |  | 

## Slide 12: Simulation Results (Luma + Chroma)
<number>
Class | Low Delay (B) HE |  |  | Low Delay (B) LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.11 | -0.07 | -0.03 | -1.34 | -1.04 | -1.17
Class C | -0.10 | -0.10 | -0.15 | -0.57 | -0.27 | -0.15
Class D | 0.01 | 0.01 | 0.01 | -0.21 | -0.34 | -0.12
Class E | -0.01 | -1.25 | -1.94 | -2.27 | -8.74 | -6.75
All | -0.06 | -0.28 | -0.41 | -1.04 | -2.12 | -1.67
Enc Time[%] | 104%(103%) |  |  | 107% (109%) |  | 
Dec Time[%] | 100%(100%) |  |  | 100% (100%) |  | 

## Slide 13: Simulation Results (Luma + Chroma)
<number>
Class | Random Access HE |  |  | Random Access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.37 | -0.28 | -0.33 | -1.32 | -0.68 | -0.67
Class B | 0.03 | 0.03 | 0.09 | -0.17 | 0.11 | 0.11
Class C | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Class D | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Class E |  |  |  |  |  | 
All | -0.08 | -0.05 | -0.05 | -0.36 | -0.12 | -0.12
Enc Time[%] | 102% (102%) |  |  | 103% (103%) |  | 
Dec Time[%] | 100% (100%) |  |  | 100% (100%) |  | 

## Slide 14: AIF-ALF Interaction
<number>
There is a strong AIF-ALF interaction:
  ALF substantially reduces AIF gain.
  For HE configurations w/o ALF, AIF gain averages 1.6%.
  For LC configurations with ALF, AIF gain averages 0.1%.
AIF can allow for a less complex ALF to achieve similar BD-Rate numbers to those of HM 3.0:
  For AIF + low complexity ALF (e.g., F041), average Y BD-rate same as HM 3.0 with decoder complexity of 95%
  For AIF + low complexity ALF (e.g., F042), average U/V BD-rate reduced by 1.7% and 1.3% (respectively) with decoder complexity of 93%
Notes: SAO = Sample adaptive offset
<number>

## Slide 15: Conclusion
<number>
AIF yields 0.7%, 1.1% and 0.9% average Y, U and V BD-rate reductions (respectively) compared to those of HM 3.0.
Decoder & encoder complexity relative to HM 3.0
  Decoder: 100% (i.e. same as HM 3.0)
  Encoder: 102% to 109% (average of 104%)
AIF-ALF interaction
  AIF allows for the reduction of ALF complexity while achieving a similar Y BD-Rate to that of HM 3.0 and substantially better U/V BD-Rates than those of HM 3.0.