## Slide 1: JCTVC-F247 CE3: DCT derived interpolation filter test by Samsung
Elena Alshina, Alexander Alshin
Samsung Electronics Ltd

## Slide 2: Filter coefficients generation
Mmax
Mmin
Valid for both odd and even filter length
Smoothing effect is controlled by window size N
JCTVC-F247 CE3: DCT derived interpolation filter test by Samsung

## Slide 3: Solid filter: 7(Q)+6(H)
Statistics |  |  | 
 | Y | U | V
Avg 6 cases: | 0.07 | 0.06 | 0.04
Min | -3,52 | -1,70 | -2,12
Max | 3,04 | 3,21 | 2,48
Mult | 85% |  | 
Adds | 83% |  | 
MemBand | 95% |  | 
WC Memory BW | 83% |  | 
7(Q)+6(H) filter (symmetric):
Q: {-2, 5, -11, 58, 18, -6, 2,}
H: {2, -9, 39, 39, -9, 2}
Conclusion:
avg 16% computations reduction
avg 5% memory BW reduction
WC 17% memory BW reduction
only 0.07% performance drop
no need to change chroma filter
JCTVC-F247 CE3: DCT derived interpolation filter test by Samsung
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0,0 | -0,3 | -0,2 | -0,2 | 0,0 | 0,1
Class B | 0,0 | -0,1 | 0,0 | 0,0 | 0,1 | 0,0
Class C | 0,1 | 0,1 | 0,1 | 0,2 | 0,1 | 0,1
Class D | 0,1 | 0,1 | 0,1 | 0,5 | 0,2 | 0,3
Overall | 0,0 | -0,1 | 0,0 | 0,1 | 0,1 | 0,1
Mult[%] | 87% |  |  | 86% |  | 
Adds[%] | 84% |  |  | 84% |  | 
MemBand[%] | 96% |  |  | 96% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
Class B | 0,0 | 0,1 | 0,1 | -0,4 | -0,3 | -0,6
Class C | 0,2 | 0,0 | 0,1 | 0,2 | 0,1 | 0,1
Class D | 0,5 | 0,3 | 0,4 | 0,8 | 0,4 | 0,6
Class E | -0,2 | -0,7 | -0,4 | -1,0 | -0,8 | -0,7
Overall | 0,2 | 0,0 | 0,1 | -0,1 | -0,1 | -0,1
Mult[%] | 86% |  |  | 85% |  | 
Adds[%] | 83% |  |  | 83% |  | 
MemBand[%] | 96% |  |  | 95% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
Class B | 0,2 | 0,1 | -0,1 | -0,8 | -0,2 | 0,1
Class C | 0,6 | 0,5 | 0,3 | 0,2 | 0,3 | 0,3
Class D | 1,2 | 1,1 | 0,6 | 1,0 | 0,8 | 0,6
Class E | 0,0 | 0,1 | -0,5 | -1,8 | -1,1 | -1,0
Overall | 0,5 | 0,4 | 0,1 | -0,3 | 0,0 | 0,1
Mult[%] | 85% |  |  | 84% |  | 
Adds[%] | 83% |  |  | 82% |  | 
MemBand[%] | 95% |  |  | 95% |  | 

## Slide 4: Compare to 7(Q)+6(H) form Motorola
Statistics |  |  | 
 | Y | U | V
Avg 6 cases: | 0.07 | 0.06 | 0.04
Min | -3,52 | -1,70 | -2,12
Max | 3,04 | 3,21 | 2,48
Mult | 85% |  | 
Adds | 83% |  | 
MemBand | 95% |  | 
WC Memory BW | 83% |  | 
Asymmetry of “1/4-pel” leads to
8% more computations
2% memory BW reduction
only 0.02% performance improvement
0.8% chroma drop
need to change chroma filter
JCTVC-F247 CE3: DCT derived interpolation filter test by Samsung
Statistics |  |  | 
 | Y | U | V
Avg 6 cases: | 0,05 | 0,77 | 0,87
Min | -7,81 | -4,91 | -2,68
Max | 8,45 | 11,54 | 12,23
Mult | 93% |  | 
Adds | 91% |  | 
MemBand | 97% |  | 
WC Memory BW | 83% |  | 

## Slide 5: ¼ or α≠ ¼ ?
0
1/2
α
0
1/2
1/4
Attraction area of integer pel positions in MC is much smaller if asymmetrical filter with is used  hit-ration of integer pel MC is lower
For α=3/16 reduction of integer pel positions number should be ~1/16 (6%)
Hit ratio for α=3/16: “0” = 3/16, “1/4” = ¼, : “1/2” = 5/16, “3/4” = ¼,
Hit ratio: “0” = ¼, “1/4” = ¼, : “1/2” = ¼, “3/4” = ¼,

## Slide 6: ¼ or α≠ ¼ ?
4:2:0
4:4:4
0
1/2
α
1/2
1/4
0
0
1/2
α
1/2
1/4
0
If α=1/4 Luma & Chroma IF are synchronized both in 4:2:0 and other
sampling modes
Otherwise Chroma filter synchronized with Luma in 4:2:0 cannot be applied
for other sampling modes.
the same MV but different phase shift!
phase shift synchronized for points with the same MV

## Slide 7: From CE3 BoG test results summary
 | 7q8h F-599 Motorola | 7q6h F-247 Samsung
Avg BD-rate Luma | -0.48% | 0.07%
Avg BD-rate Chroma | 0.12% | 0.05%
Min | -5.9% | -3.5%
Max | 2.0% | 3.0%
Avg Mults | 101% | 85%
Avg Adds | 99% | 83%
Avg MemBand | 100% | 95%
WorstCase MemoryBand | 100% | 83%
16% reduction of computations vs 0.5% performance improvement

## Slide 8: Conclusion
Modify the complexity measurement in CE3:
  Mandatory report for the worst memory band-width and complexity case
  Mandatory of average memory band-width and complexity
  Actual number of operations according to hit-ratio of each filter
  Chroma MC operations count should be included
Based on test results:
  only 0.07% average performance drop
  16% less average number of computations
  5% less average memory band-width
  17% reduction of memory band-width in the worst case
we propose to adopt proposed 7(Q) + 6 (H) solid (non-switch) Luma interpolation filter for next version of HM s/w and WD
JCTVC-F247 CE3: DCT derived interpolation filter test by Samsung