## Slide 1: JCTVC-F248
Memory bandwidth is most problematic for small bi-predicted PU’s
  For a block of 32x32, decoder needs to load (32+7).(32+7) = 1521 pixels (~ 1.5 times more than the block size)
  For a block of 4x4, decoder needs to load (4+7).(4+7) = 121 pixels (~ 7.5 times more than the block size)
We propose to use 4-tap filter for bi-predicted PU’s as follows:
  Block sizes of 4x4, 8x4, 4x8  use 4-tap filter
  Larger block sizes  use 8-tap DCT-IF filter
We always use the 8-tap filter during ME stage.
  We don’t use two different filters during ME search.
Worst-case memory bandwidth is significantly reduced with practically no penalty on coding efficiency.

## Slide 2: JCTVC-F248
Two sets of filter coefficients are tested:
Set 1:
½ pel : [-6 38 38 -6]
¼ pel : [-6 56 18 -4]
Set 2 (same coefficients as interpolating the chroma samples):
½ pel : [-4 36 36 -4]
¼ pel : [-4 54 16 -2]
In addition, it was decided in the CE to test some harmonization of various proposals.
  Results of this proposal with respect to other proposals in the CE are also presented

## Slide 3: Results
Test | Average coding efficiency
F248-filter set 1 | +0.03%
F248-filter set 2 | +0.05%
F248-filter set 2 with respect to Samsung’s filter coefficients | +0.09%
F248-filter set 2 with respect to Motorola’s filter coefficients | +0.08%
The summary of the results are presented below. As seen below, the coding efficiency is relatively unchanged on all of these cases.
  If ME also used the 4-tap filter for small PU’s, it is expected the coding efficiency would increase slightly