## Slide 1: JCTVC-F252: Block-size and pixel position independent boundary smoothing for non-directional Intra prediction
Elena Alshina, Alexander Alshin
Samsung Electronics Ltd

## Slide 2: Motivation
Boundary smoothing is applied in HM3.0 for non-directional prediction
Pros
  Overall gain from this tool is 0.1%
  Was noticed that boundary smoothing is beneficial for block artifacts illumination
Cons
  Smoothing filter depends on PU size
  Smoothing filter depends on pixel position
JCTVC-F252: Block-size and pixel position independent boundary smoothing for non-directional Intra prediction

## Slide 3: Proposed changes:
Mult-free implementation: yi,j = (yi,j-1 + yi-1,j +(yi,j<<1)+1) >>1;
JCTVC-F252: Block-size and pixel position independent boundary smoothing for non-directional Intra prediction

## Slide 4: Test 1: Intra PU 4x4…16x16
Resume:
  No Luma drop
  Chroma gain was observed for high resolution  test 2
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0 | -0.1 | -0.1 | 0.0 | -0.1 | -0.1
Class B | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | 0.0
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.1
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Overall | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
All Intra test, following JCTVC-E700
JCTVC-F252: Block-size and pixel position independent boundary smoothing for non-directional Intra prediction

## Slide 5: Test 2: All Intra PU
Resume:
  No Luma drop
  Average chroma gain (compared to overall gain from this tool)
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1 | -0.2 | -0.2 | -0.1 | -0.3 | -0.3
Class B | 0.0 | -0.1 | -0.2 | 0.1 | -0.1 | -0.1
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.1
Class D | 0.0 | -0.1 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.0 | -0.1 | -0.1 | 0.0 | -0.1 | -0.1
Overall | 0.0 | -0.1 | -0.1 | 0.0 | -0.1 | -0.1
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
All Intra test, following JCTVC-E700
JCTVC-F252: Block-size and pixel position independent boundary smoothing for non-directional Intra prediction

## Slide 6: Test 3: independent pixel processing
predSamples[ 0, 0 ] = ( p[ -1, 0 ] + (DCVal <<1)+ p[ 0, -1 ] + 2 ) >> 2
predSamples[ x, 0 ] = ( p[ x, -1 ] + (DCVal<<1)+ DCVal + 2 ) >> 2,
predSamples[ 0, y ] = ( p[ -1, y ] + (DCVal<<1)+ DCVal + 2 ) >> 2, predSamples[ x, y ] = DCVal,
predSamples[ 0, 0 ] = ( p[ -1, 0 ] + (DCVal <<1)+ p[ 0, -1 ] + 2 ) >> 2
predSamples[ x, 0 ] = ( p[ x, -1 ] + (DCVal<<1)+ DCVal + 2 ) >> 2, predSamples[ 0, y ] = ( p[ -1, y ] + (DCVal<<1)+ DCVal + 2 ) >> 2, predSamples[ x, y ] = DCVal,

## Slide 7: Test 3 results
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0,2 | -0,3 | -0,2 | -0,1 | -0,2 | -0,2
Class B | 0,0 | -0,1 | -0,2 | 0,0 | -0,1 | -0,1
Class C | 0,0 | -0,1 | 0,0 | 0,0 | 0,0 | 0,0
Class D | 0,0 | 0,0 | 0,0 | 0,0 | 0,0 | 0,0
Class E | 0,0 | -0,1 | -0,1 | 0,0 | -0,1 | -0,1
Overall | -0,04 | -0,12 | -0,12 | -0,02 | -0,09 | -0,10
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
Additional gain provided by unification is comparable with gain this tool provides (0.1%).

## Slide 8: Conclusion
Based on presented test results
Avg. BD-rate: 0.0%/-0.1%/-0.1% (Y/U/V)
we propose to adopt proposed unification for boundary smoothing design.
Benefits:
46 lines of code  2 lines
removal of one LUT
no conditions check
multiplication-free realization
JCTVC-F252: Block-size and pixel position independent boundary smoothing for non-directional Intra prediction