## Slide 1: JCTVC-F265 Weighted Prediction
P.Bordes
4th JCTVC Meeting: Daegu, 20-29 January, 2011
6th JCTVC Meeting: Torino, July 14th-22nd, 2011

## Slide 2: Overall summary
  Work conducted in AHG18
  Provide WP implementation in HM3.0 and HM3.3 (Encoder/Decoder)
    Identical to WP in AVC
  Provide WP parameters estimator (encoder)
  Provide a simple Fading tool:
    To create Fade sequences
    To create Explicit WP parameters
  Report experiments (HM3.0) on Fading sequences
    Using estimated WP parameters (cross-checks F436 and F331)

## Slide 3: Introduction
Weighted Prediction (WP)
  WP is an AVC tool
  Originally designed to compensate Illumination variation in video sequences
  Used by video encoder and splicers too
  Syntax has limited overhead in PPS (3 bits), WP switched-on only when necessary: slice header contains only non default WP scaling values (wi,oi).
  Simple design principle:
    Uni-ref prediction: P’ = w × P + o
    Bi-ref prediction: P’ = (w0 × P0 + o0 + w1 × P1 + o1) / 2
  Better efficiency when combined with flexible reference pictures list management (ex: MMCO)
  Local illumination variations can be managed with duplicate references in reference pictures list

## Slide 4: WP principle
Weighted Prediction (WP)
  (1) pred= ( ( predL0×W0 + shift/2) >> shift ) + O0
  (2) pred=(( predL0×W0 + predL1×W1 + shift ) >> (shift+1)) + ((O0+O1+1)>>1)
  Several WP algorithms:
    Default: default HEVC uni or bi prediction.
    Explicit: weighting factors transmitted explicitly in the slice header.
    Implicit: weighting factors for bi prediction are derived from the distance of the current POC with the POC of the ref. pictures (B_SLICE only):
    W0 = (1 – α) W1=α where: , Oi=0
PPS P_SLICE |  |  | PPS B_SLICE | 
Weighted_pred_flag | Weighting method |  | Weighted_bipred_idc | Weighting method
0 | Default |  | 0 | Default
1 | Explicit |  | 1 | Explicit
 |  |  | 2 | Implicit

## Slide 5: WP results
Fading-to-black, fading-to-white
Fade-to-black
Fade-to-white

## Slide 6: WP parameters estimation
Features extraction:
  DC, AC (F326)
  Histogram matching (F265)
WP param. Estimation:
  W=ACcur/ACref; O=DCcur-W.DCref (F326)
  LMS cumulated histo. error (F265)
Confidence test :
  Estimated cumul. histo. error (F265 method-1)
  SAD (F326), (F265 method-2)
Chart: 
Chart: 

## Slide 7: WP parameters estimated (method 2)
Fade-to-black
 | High-Efficiency – Fade-Black |  |  |  |  |  |  |  | 
 | Random access |  |  | Low Delay B |  |  | Low Delay P |  | 
 | Y BD-rate | U BD-rate | Y BD-rate | Y BD-rate | Y BD-rate | V BD-rate | Y BD-rate | Y BD-rate | V BD-rate
Class A | -17,3 | -19,4 | -19,6 |  |  |  |  |  | 
Class B | -18,1 | -17,7 | -18,4 | -23,8 | -17,5 | -17,0 | -22,9 | -14,5 | -13,3
Class C | -13,6 | -11,8 | -11,9 | -11,7 | -8,7 | -8,1 | -12,2 | -8,2 | -7,1
Class D | -13,5 | -10,1 | -12,1 | -11,8 | -8,5 | -11,0 | -14,2 | -9,5 | -12,9
Class E |  |  |  | -42,1 | -27,0 | -24,1 | -42,6 | -27,0 | -24,2
All | -15,8 | -14,9 | -15,7 | -21,2 | -14,8 | -14,6 | -21,7 | -14,0 | -13,7
Enc. time | 120% |  |  | 116% |  |  | 102% |  | 
Dec. time | 99% |  |  | 91% |  |  | 98% |  | 
 | Low-Complexity – Fade-Black |  |  |  |  |  |  |  | 
 | Random access |  |  | Low Delay B |  |  | Low Delay P |  | 
 | Y BD-rate | U BD-rate | Y BD-rate | Y BD-rate | Y BD-rate | V BD-rate | Y BD-rate | Y BD-rate | V BD-rate
Class A | -18,8 | -18,5 | -19,3 |  |  |  |  |  | 
Class B | -19,5 | -17,1 | -18,7 | -30,9 | -34,1 | -29,6 | -28,9 | -31,1 | -23,8
Class C | -15,9 | -13,3 | -12,8 | -17,1 | -27,4 | -22,7 | -17,4 | -25,7 | -21,7
Class D | -15,8 | -12,5 | -14,7 | -17,0 | -24,1 | -23,2 | -19,2 | -24,5 | -22,7
Class E |  |  |  | -49,0 | -41,5 | -41,6 | -49,1 | -40,9 | -40,2
All | -17,6 | -15,4 | -16,5 | -27,3 | -31,3 | -28,6 | -27,4 | -29,9 | -26,1
Enc. time | 127% |  |  | 126% |  |  | 108% |  | 
Dec. time | 90% |  |  | 83% |  |  | 82% |  | 

## Slide 8: WP parameters estimated (method 2)
Fade-to-white
 | High-Efficiency – Fade-White |  |  |  |  |  |  |  | 
 | Random access |  |  | Low Delay B |  |  | Low Delay P |  | 
 | Y BD-rate | U BD-rate | Y BD-rate | Y BD-rate | Y BD-rate | V BD-rate | Y BD-rate | Y BD-rate | V BD-rate
Class A | -21,2 | -24,0 | -24,6 |  |  |  |  |  | 
Class B | -21,9 | -22,9 | -22,6 | -26,9 | -20,2 | -18,3 | -25,7 | -17,4 | -13,7
Class C | -15,4 | -14,7 | -14,8 | -13,8 | -10,6 | -9,9 | -14,2 | -10,5 | -10,1
Class D | -14,7 | -11,8 | -12,9 | -11,5 | -9,9 | -12,3 | -14,3 | -9,4 | -11,9
Class E |  |  |  | -43,0 | -31,4 | -24,2 | -42,8 | -27,2 | -26,8
All | -18,5 | -18,6 | -19,0 | -22,8 | -17,3 | -15,8 | -23,2 | -15,5 | -14,8
Enc. time | 116% |  |  | 113% |  |  | 97% |  | 
Dec. time | 103% |  |  | 89% |  |  | 89% |  | 
 | Low-Complexity – Fade-White |  |  |  |  |  |  |  | 
 | Random access |  |  | Low Delay B |  |  | Low Delay P |  | 
 | Y BD-rate | U BD-rate | Y BD-rate | Y BD-rate | Y BD-rate | V BD-rate | Y BD-rate | Y BD-rate | V BD-rate
Class A | -22,2 | -21,2 | -22,3 |  |  |  |  |  | 
Class B | -23,6 | -22,8 | -23,3 | -35,3 | -37,2 | -34,0 | -33,6 | -33,6 | -27,3
Class C | -17,8 | -15,9 | -15,8 | -20,1 | -29,9 | -25,0 | -20,2 | -27,6 | -23,9
Class D | -17,3 | -14,9 | -18,2 | -17,6 | -26,1 | -25,2 | -20,0 | -28,0 | -25,1
Class E |  |  |  | -51,5 | -46,1 | -44,6 | -51,4 | -44,5 | -41,1
All | -20,4 | -18,9 | -20,1 | -30,1 | -34,3 | -31,5 | -30,2 | -32,7 | -28,5
Enc. time | 123% |  |  | 121% |  |  | 102% |  | 
Dec. time | 99% |  |  | 84% |  |  | 85% |  | 

## Slide 9: Comparison F265-F326
 |  | Random access |  |  | Low Delay B |  |  | Low Delay P |  | 
 |  | Y BD-rate | U BD-rate | Y BD-rate | Y BD-rate | Y BD-rate | V BD-rate | Y BD-rate | Y BD-rate | V BD-rate
 |  | High-Efficiency – Fade-White |  |  |  |  |  |  |  | 
F265 | All | -15,8 | -14,9 | -15,7 | -21,2 | -14,8 | -14,6 | -21,7 | -14,0 | -13,7
 | Enc. time | 120% |  |  | 116% |  |  | 102% |  | 
 | Dec. time | 99% |  |  | 91% |  |  | 98% |  | 
F326 | All | -16,9 | -17,4 | -17,6 | -22,7 | -18,9 | -18,6 | -23,9 | -19,0 | -18,4
 | Enc. time | 119% |  |  | 114% |  |  | 100% |  | 
 | Dec. time | 98% |  |  | 98% |  |  | 89% |  | 
 |  | Low-Complexity – Fade-White |  |  |  |  |  |  |  | 
F265 | All | -17,6 | -15,4 | -16,5 | -27,3 | -31,3 | -28,6 | -27,4 | -29,9 | -26,1
 | Enc. time | 127% |  |  | 126% |  |  | 108% |  | 
 | Dec. time | 90% |  |  | 83% |  |  | 82% |  | 
F326 | All | -17,9 | -11,2 | -14,9 | -27,8 | -28,7 | -32,7 | -28,1 | -28,5 | -29,1
 | Enc. time | 127% |  |  | 124% |  |  | 108% |  | 
 | Dec. time | 89% |  |  | 82% |  |  | 86% |  | 
Fade-to-Black

## Slide 10: Comparison F265-F326
 |  | Random access |  |  | Low Delay B |  |  | Low Delay P |  | 
 |  | Y BD-rate | U BD-rate | Y BD-rate | Y BD-rate | Y BD-rate | V BD-rate | Y BD-rate | Y BD-rate | V BD-rate
 |  | High-Efficiency – Fade-White |  |  |  |  |  |  |  | 
F265 | All | -18,5 | -18,6 | -19,0 | -22,8 | -17,3 | -15,8 | -23,2 | -15,5 | -14,8
 | Enc. time | 116% |  |  | 113% |  |  | 97% |  | 
 | Dec. time | 103% |  |  | 89% |  |  | 89% |  | 
F326 | All | -19,9 | -21,2 | -21,1 | -24,3 | -21,4 | -20,5 | -25,4 | -20,8 | -20,4
 | Enc. time | 115% |  |  | 110% |  |  | 95% |  | 
 | Dec. time | 101% |  |  | 86% |  |  | 86% |  | 
 |  | Low-Complexity – Fade-White |  |  |  |  |  |  |  | 
F265 | All | -20,4 | -18,9 | -20,1 | -30,1 | -34,3 | -31,5 | -30,2 | -32,7 | -28,5
 | Enc. time | 123% |  |  | 121% |  |  | 102% |  | 
 | Dec. time | 99% |  |  | 84% |  |  | 85% |  | 
F326 | All | -20,9 | -14,8 | -18,5 | -30,3 | -30,9 | -34,6 | -31,2 | -30,5 | -31,6
 | Enc. time | 122% |  |  | 119% |  |  | 101% |  | 
 | Dec. time | 100% |  |  | 86% |  |  | 84% |  | 
Fade-to-White

## Slide 11: WP proposal
  Provide WP implementation in HM3.3 (Encoder/Decoder)
    Identical to WP in AVC
  Propose to adopt WP in HEVC
  Propose to add F326 (F265) in HM to estimate the WP parameters automatically (encoder)