## Slide 1: Grid displacements for filtering
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
6th JCT-VC meeting, Torino 14.-22. July 2011

## Slide 2: Outline
LCU-based filtering in HM3.0 and problems
Proposed solution: grid displacements for filtering
Experimental results
Conclusion

## Slide 3
LCU-based filtering in HM3.0: Non-deblocked LCU
LCU

## Slide 4
Copy line memory to LCU borders
Line memory
LCU

## Slide 5
Horizontal deblocking of vertical edges
Line memory
LCU

## Slide 6
Vertical deblocking of horizontal edges
Line memory

## Slide 7
Delayed deblocking at LCU borders
Line memory
3 lines
3 lines
Samples at the LCU boundaries cannot be processed at the moment since the right and bottom neighboring LCUs are not available.

## Slide 8
Delayed deblocking at LCU borders
Line memory
3 lines
LCU
Region that is not yet deblocked
3 lines

## Slide 9
LCU-based processing of SAO
Line memory
SAO design window
SAO application window
LCU
In the Encoder
A different SAO parameter set is designed for each LCU (SAO design window).
In the Decoder
SAO is applied on the red region (SAO application window) due to delayed deblocking filtering.
SAO design and application windows are not aligned.
3 lines
3 lines

## Slide 10
1. Problems with SAO application
LCU 1
SAO pattern 1
Offset values 1
1
2
3
4
SAO application window in decoder
LCU 2
SAO pattern 2
Offset values 2
LCU 3
SAO pattern 3
Offset values 3
LCU 4:
SAO pattern 4
Offset values 4
Problems in the Decoder:
SAO application window intersects 4 different LCUs.
Application of SAO requires frequent parameter set switching at LCU borders.
2 lines of increase in line memory.
3 lines
3 lines

## Slide 11
LCU-based processing of region-based ALF
ALF application window
ALF design window
ALF design and application windows are not aligned.
Line memory
7 lines
6 lines

## Slide 12
2. Problems with region-based ALF application
LCU 2
ALF set2
LCU 1
ALF set 1
LCU 3
ALF set 3
LCU 4
ALF set 4
1
2
3
4
Problems in the Decoder:
ALF application window intersects 4 different LCUs.
Application of ALF requires frequent filter switching at LCU borders.
ALF application window in decoder
7 lines
6 lines

## Slide 13: Summary of the problems
Frequent filter switching during LCU-based processing of
  SAO and
  Region-based ALF
Line memory is increased by 2 lines as a result of the misaligment in SAO grid.

## Slide 14: Proposed solution: Grid displacements for SAO and ALF
Goal:
Frame partitioning for filtering suited for both frame-based and LCU-based decoding.
Main principle:
„Align the filter application window in decoder and the filter design window in encoder.“

## Slide 15
Proposed solution: Grid displacement for SAO
SAO application window
SAO design window
Shift 3 pixels up
Shift 3 pixels left
Shift SAO design window 3 pixels up and 3 pixels to the left.
SAO design window is aligned with SAO application window.
LCU

## Slide 16
Proposed solution: Grid displacement for ALF
ALF application window
ALF design window
Shift 6 pixels up
Shift 7 pixels left
Shift ALF design filter 6 pixels up and 7 pixels to the left.
ALF design window is aligned with ALF application window.
LCU

## Slide 17: Experimental results
Average change in bitrate < 0.01%

## Slide 18: Conclusion
Motivation:
Frame partitioning for filtering suited to both frame-based and LCU-based decoding.
Benefits:
Line memory requirement is reduced by 2 lines.
In the decoder no filter switching is required for SAO and region-based ALF during the decoding of an LCU.
Proposal:
Adopt into the next version of HM.