## Slide 1: CE8.3: Line memory reduction for in-loop filtering
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
6th JCT-VC meeting, Torino 14.-22. July 2011

## Slide 2: Outline
Introduction
LCU-based filtering in HM3.0 and proposed solution
Experimental results
Subjective evaluation
Conclusion

## Slide 3: Introduction
Problem:
In HM3.0, LCU-based decoding requires
  12 lines of line memory for luma
  9 lines of line memory for each chroma components
Line memory is on-chip memory which is costly to implement
Solution:
Line memory reduction for in-loop filters by “using the partially deblocked signal at the bottom LCU borders”
Benefits:
Significant reduction of decoder line memory:
  6 lines reduction for luma
  1 line reduction for each chroma components
Improved subjective quality and coding efficiency
Almost no impact on runtimes

## Slide 4: LCU-based filtering: Non-deblocked LCU
LCU (16x16)
Note: In the proposal only horizontal line memory is considered.
HM3.0
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 5: Deblocking filter (horizontal filtering)
LCU (16x16)
HM3.0
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 6: Deblocking filter (vertical+horizontal)
LCU
Line memory for DF: 4 lines
Last 3 lines cannot be fully deblocked at the current time instant since neighboring LCU below is not yet decoded.
HM3.0
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 7: Sample adaptive offset
HM3.0
Proposed
Use partially deblocked pixels.
Delay of SAO is reduced by 1 line.
Line memory for DF and SAO: 5 lines
Line memory for DF and SAO: 4 lines
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 8: Block based filter decision method of ALF
Filter Decision
possible
Filter Decision
NOT possible
Filter Decision
possible
Filter Decision
NOT possible
HM3.0
Proposed
Use partially deblocked pixels.
2. Extend filter decision block by 1 line.
Delay of filter decision method is reduced by 5 lines.
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 9: ALF filter application in HM3.0
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code
HM3.0
Filter Decision
possible
Filter Decision
NOT possible
Line Memory for ALF
7 lines
Line Memory for DF and SAO
5 lines

## Slide 10: Proposed ALF filter application
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code
Proposed
Filter Decision
possible
Filter Decision
NOT possible
Use partially deblocked pixels.
Delay of ALF is reduced by 5 lines.
Line Memory for ALF 2 lines
Line Memory for DF and SAO 4 lines

## Slide 11: Summary
Delay of SAO is reduced by 1 line.
Delay of ALF is reduced by 5 lines.
As a result total line memory reduction for luminance component is 6 lines.
Same method applied to the chroma component. 1 line of reduction for each chrominance component.

## Slide 12: Experimental results
Increase in coding gain.
Only minor increase in decoding times due to first time implementation of line memory in the software.

## Slide 13: Subjective evaluation
Proposed
HM3.0
The proposal eliminates line memory requirements of SAO.
Processing of LCU borders no longer need to be skipped.
Increase in subjective quality by elimination of LCU grid artifact.

## Slide 14: Conclusion
A significant reduction of line memory for SAO and ALF:
  6 lines reduction for luma.
  1 line reduction for chroma.
Clean and Simple principle:
substitution of input samples that are not available at the instant of filtering with available counterparts in the memory.
Improvement in subjective quality and coding efficiency.
Almost no impact on runtimes.
Proposal: Adoption into the next version of the HM

## Slide 15: Usage of the Line Memory

## Slide 16: Deblocking filter (horizontal filtering)
LCU
Line Memory
LCU Border
3
4
5
6
1
2
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 17: Deblocking filter (horizontal + vertical)
3
4
5
6
1
2
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 18: Sample adaptive offset
3
4
5
6
1
2
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 19
Use Deblocked pixels in Filter Decision
3
4
5
6
1
2
Block based filter decision method of ALF
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code

## Slide 20
ALF filter application
Non-deblocked pixel
Partially-deblocked pixel
Deblocked pixel
SAO-processed pixel
ALF-filtered pixel
Color Code
Use Deblocked pixels in ALF Filtering
3 Lines
3 Lines
3
4
5
6
1
2