## Slide 1: Wavefront and Cabac Flush: Different Degrees of Parallelism Without Transcoding JCTVC-F275
Gordon Clare, Félix Henry, Stéphane Pateux – ORANGE LABS
Notes: presentation title
<number>

## Slide 2: The importance of transcoding to different levels of parallelism
First trend
  Towards heterogenous and increasing number of cores in devices
   There is a need to serve different levels of parallelism while maintaining Rate-Distortion efficiency
Second trend
  The average consumer is becoming an important content producer of videos (YouTube, DailyMotion, etc.)
  We have no control over the compressed bitstream he provides
   There is need to transcode his content to different levels of parallelism
JCTVC-F275
Notes: presentation title
<number>

## Slide 3: Parallelism and spatial/MV dependencies
If dependencies are broken to achieve parallel processing (eg. Slices, Tiles), it is not practically possible to:
  transcode a sequential bitstream to a parallel bitstream
  increase the level of parallelism
Therefore we are either stuck with an original sequential bitstream (unable to parallel decode) or a stuck with a given level of parallelism
or, even if we have control over bitstream production, we need to prepare the bitstream for the highest expected level of parallelism (incurring high R/D loss because many dependencies are broken)
JCTVC-F275
Notes: presentation title
<number>

## Slide 4: Wavefront Parallel processing
Wavefront Parallel Processing (JCTVC-E196/F274 ) has been proposed for high-level parallelism
  Spatial/MV dependencies are preserved
  R/D performance does not depend on level of parallelism
  Transcoding between levels (including sequential) is possible and consists of entropy decoding and re-encoding
JCTVC-F275
X
X
X
X
Pixel and MV dependency
Probabilties dependency
X
Block(s) being encoded
CABAC probabilitites
KEY
Notes: presentation title
<number>

## Slide 5: Proposal
1
X
X
2
3
4
5
6
7
8
9
10
Cabac synchro
(from WPP – JCTVC-F274)
Cabac flush &
internal state init
(current proposal)
Chunks
At the end of each LCU line:
  Perform a CABAC flush LCU line (write remaining bits + stop bit, no byte stuffing)
  Re-initialise CABAC status (codIRange and codIOffset )
Thus, each line produces a « chunk » of compressed data

## Slide 6: Proposal
Bitstream organization
  lcu_lines_mode=0
  lcu_lines_mode=1
    num_substreams_minus1 =1
or
JCTVC-F275
1
2
3
4
5
6
7
8
9
10
SEI
may provide chunks entry point
1
2
3
4
5
6
7
8
9
10
Slice Header
provides substreams entry points
( )

## Slide 7: Bitstream organisation and transcoding
lcu_lines_mode = 0
  the bitstream matches any level of parallelism up to the number of LCU lines
  Entry points in SEI message because the large number of entry points may reduce R/D efficiency (especially for highly compressed sequences).
    If entry point are available in SEI, transcoding to lcu_lines_mode=1 bitstream is only a chunk re-ordering operation
    If entry point are not available in SEI, conversion to a higher level of parallelism is only a parsing and chunk re-ordering operation
lcu_lines_mode=1
  only the entry points that are useful to achieve the desired level of parallelism are written in the bitstream.
  conversion to a higher level of parallelism is only a parsing and chunk re-ordering operation
JCTVC-E275

## Slide 8: Use case
Content distribution server
JCTVC-E275
…
Sequential
bitstream
2-// bitstream
Transcoding to WPP
lcu_lines_mode = 0
SEI provides entry points
4-// bitstream
Chunks re-ordering
lcu_lines_mode = 1
Each transmission is R/D optimal for the desired level of parallelism

## Slide 9: Use case
A power encoder can use more threads than the capabilities of the decoder, without sacrifying R/D performance
  An encoder can use its 16 cores to generate a 2-// bitstream
16-cores encoder
JCTVC-E275
…
Live
content
2-// bitstream
Chunk encoding
using 16 cores
2-// bitstream
2-// bitstream
Chunk re-ordering
Entry points for 2-//
lcu_lines_mode = 1

## Slide 10: Tests
Test conditions
  HM3.0, JCTVC-E700 conditions, High Efficiency
  Performance presented for 2 substreams (Lcu_lines_mode=1) for comparison with WPP (JCTVC-F274)
  Impact of Cabac Flush is about +0.2%
JCTVC-F275
 | Intra |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0,0 | 0,0 | 0,0
Class B | 0,0 | 0,0 | 0,0
Class C | 0,0 | 0,0 | 0,0
Class D | 0,0 | 0,0 | 0,0
Class E | 0,1 | 0,0 | 0,1
All | 0,0 | 0,0 | 0,0
 |  | Random access | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0,1 | 0,2 | 0,2
Class B | 0,2 | 0,1 | 0,3
Class C | 0,2 | 0,2 | 0,2
Class D | 0,3 | 0,2 | 0,1
Class E |  |  | 
All | 0,2 | 0,2 | 0,2
 | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | 0,2 | 0,4 | 0,4
Class C | 0,2 | 0,2 | 0,3
Class D | 0,2 | 0,3 | 0,5
Class E | 1,0 | 1,1 | 1,7
All | 0,4 | 0,5 | 0,6
Proposal vs HM3.0+WPP anchors
Proposal vs HM3.0 anchors
Notes: presentation title
<number>

## Slide 11: Advantages
JCTVC-E275
Compressed content can be converted to/from any level of parallelism (including sequential)
  Using only chunk re-ordering
Highly parallel server can use more threads than substreams

## Slide 12: Conclusion
Combination of Wavefront Parallel Processing (WPP) with an end-of-LCU-line CABAC flush
  Optimal R/D performance for target level of parallelism
  Possibility to serve any level of parallelism without entropy transcoding (simple chunk re-ordering).
Proposed for adoption
  Syntax and WD description are provided
  Crosscheck by LGE (JCTVC-F351)
JCTVC-F275
Notes: presentation title
<number>