## Slide 1: Redundancy removal for Run-mode in CAVLC
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
CAVLC for transform coefficients in HM3.0
  Last non-zero position
  Run-mode
  Level-mode
Current HM3.0 technology
  Run-mode employs various VLC tables
  Index 0 VLC table is unary-like
  The maximal code number can be derived based on “maxrun”.
    Redundancy for unary codes in run-mode for “maxrun”.
codenumber | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Bit length | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 9 | 9

## Slide 4: Proposals
Solutions
  Use truncated unary code to replace index 0 VLC table
Implementations
  Identify where index 0 VLC table is used
    const UInt g_auiVlcTable8x8Inter[29] = {8,0,0,5,5,5,5,5,5,5,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,3};
    const UInt g_auiVlcTable8x8Intra[29] = {8,0,0,5,5,5,5,5,5,5,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,3};
    const UInt g_auiVlcTable16x16Intra[29] = {8,0,0,0,0,5,5,5,5,5,5,5,5,5,5,5,5,5,1,1,1,1,1,1,1,1,1,1,2};
    const UInt g_auiVlcTable16x16Inter[29] = {8,0,1,1,1,1,2,2,2,2,2,2,2,6,6,6,6,6,6,3,3,3,3,3,3,3,3,3,3};
  Replace with truncated unary codes (index 14~17).
    const UInt g_auiVlcTable8x8Inter[29] = {8,14,15,5,5,5,5,5,5,5,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,3};
    const UInt g_auiVlcTable8x8Intra[29] = {8,14,15,5,5,5,5,5,5,5,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,3};
    const UInt g_auiVlcTable16x16Intra[29] = {8,14,15,16,17,5,5,5,5,5,5,5,5,5,5,5,5,5,1,1,1,1,1,1,1,1,1,1,2};
    const UInt g_auiVlcTable16x16Inter[29] = {8,14,1,1,1,1,2,2,2,2,2,2,2,6,6,6,6,6,6,3,3,3,3,3,3,3,3,3,3};
  Alternative implementation
    Void TEncCavlc::xWriteUnaryMaxSymbol( UInt uiSymbol, UInt uiMaxSymbol )
  Savings are marked as yellow.
codenumber | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit length VLC-0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 9 | 9 | 11 | 11
Bit length VLC-14 | 1 | 2 | 3 | 4 | 4 | - | - | - | - | - | -
Bit length VLC-15 | 1 | 2 | 3 | 4 | 5 | 6 | 6 | - | - | - | -
Bit length VLC-16 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | - | -
Bit length VLC-17 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 10

## Slide 5: Results
Cross-check by MediaTek, JCTVC-F676
 | All intra LC |  | 
 | Y | U | V
Class A | 0.0 | 0.0 | -0.1
Class B | -0.1 | -0.1 | -0.1
Class C | -0.1 | -0.1 | -0.1
Class D | -0.1 | -0.1 | -0.1
Class E | -0.1 | 0.0 | -0.1
Overall | -0.1 | -0.1 | -0.1
Enc Time[%] | 101% |  | 
Dec Time[%] | 102% |  | 
 | Random access LC |  | 
 | Y | U | V
Class A | 0.0 | -0.3 | 0.2
Class B | -0.1 | 0.0 | 0.0
Class C | -0.1 | -0.1 | -0.2
Class D | -0.1 | -0.2 | -0.1
Class E |  |  | 
Overall | -0.1 | -0.1 | 0.0
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
 | Low delay (B) LC |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.1 | 0.0 | -0.2
Class C | -0.1 | -0.2 | -0.3
Class D | 0.0 | 0.1 | -0.2
Class E | 0.0 | 0.1 | -0.5
Overall | 0.0 | 0.0 | -0.3
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 

## Slide 6: Conclusion
Presented solutions to remove redundancy of run-mode coding
0.1% BD-rate savings observed, no complexity
Proposed to adopt in HM4.0