## Slide 1: JCTVC-F288 CE11: Unified scans for the significance map and coefficient level coding in high efficiency
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Summary
CE11 proposal consisting of two parts
  Unification of scans for significance map and coefficient level in high efficiency
Part 1
  Coefficient level scan uses the scan employed by the significance map
    Reverse zig-zag, horizontal or vertical
Part 2
  Both, significance map and coefficient level scan use the same reverse scan
BD-rate | AI – HE | RA – HE | LB – HE
Part 1 | -0.05% | 0.07% | -0.01%
Part 2 | -0.25% | -0.19% | -0.07%

## Slide 3: Background
HEVC uses 3 scans for significance map coding
  Forward zig-zag, vertical and horizontal
  Scan depends on prediction mode
Coefficient level coding uses a different scan
  Forward zig-zag scan on 4×4 sub-blocks
  Backward zig-zag scan within each sub-block
  Problem: mismatch between scans

## Slide 4: Part 1: Unified scan pattern
Use the scan applied to the significance map for coefficient level coding
Scan follows backward direction
  From the last significant coefficient to the first coefficient (DC)
Context sets
  Set consists of 16 consecutive coefficients in scan order
    Instead of 4x4 sub-blocks in HEVC
  Unification: same context derivation for all blocks sizes
    Same number of contexts as in HEVC

## Slide 5: Part 1: Advantages
No need to store additional scans for the coefficient level coding
  Avoid backward-forward scan within the block
  Harmonization with LC case
Less processing
  More coefficient levels have to be checked when the scans are different
Harmonization of context sets for coefficient level of all block sizes
Parsing: coefficient level parsing depends on the intra mode
  Proposed solution makes parsing independent of the intra mode
Avoid 4×4 sub-block processing: easier harmonization with non-square blocks and blocks with side of length less than 4

## Slide 6: Part 1: BD-rate
  * Thanks to Samsung for the cross-check
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.11 | 0.10 | 0.15 | 0.27 | 0.06 | 0.41 |  |  | 
Class B | -0.10 | 0.05 | 0.03 | 0.02 | -0.18 | 0.04 | 0.05 | -0.58 | -0.97
Class C | -0.14 | -0.04 | -0.01 | 0.02 | -0.03 | -0.20 | -0.02 | -0.72 | -0.79
Class D | -0.18 | -0.10 | -0.10 | -0.03 | -0.27 | -0.33 | -0.11 | -1.52 | -1.34
Class E | 0.08 | 0.11 | 0.23 |  |  |  | 0.04 | -0.99 | -2.88
All | -0.05 | 0.02 | 0.05 | 0.07 | -0.11 | -0.02 | -0.01 | -0.93 | -1.38
Enc T[%] | 99% |  |  | 99% |  |  | 99% |  | 
Dec T[%] | 97% |  |  | 98% |  |  | 99% |  | 

## Slide 7: Part 2: Unified reverse scan pattern
Use the scan applied to the significance map for coefficient level coding
Both scans are backward
  From the last significant coefficient to the first coefficient (DC)
Use the reverse of current contexts of the significance map for large blocks
HEVC
Proposal

## Slide 8: Part 2: Advantages
Reduction of the number of context derivation methods for significance map
  Currently, there 4 different methods depending on the location of the coefficient in the block
  Reduction in the number of contexts
Parallelization: harmonizing scans in the same direction allows for an earlier availability of the contexts

## Slide 9: Part 2: BD-rate
  * Thanks to Panasonic and TI for the cross-check
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.47 | -0.49 | -0.44 | -0.66 | -0.81 | -1.43 |  |  | 
Class B | -0.20 | -0.60 | -0.60 | -0.11 | -0.78 | -0.58 | -0.01 | -1.38 | -1.72
Class C | -0.20 | -0.43 | -0.45 | 0.02 | -0.62 | -0.65 | -0.04 | -1.41 | -1.52
Class D | -0.17 | -0.48 | -0.45 | -0.03 | -0.82 | -0.85 | -0.14 | -2.12 | -2.07
Class E | -0.20 | -0.83 | -0.84 |  |  |  | -0.14 | -3.15 | -2.37
All | -0.25 | -0.55 | -0.55 | -0.19 | -0.76 | -0.86 | -0.07 | -1.90 | -1.88
Enc T[%] | 99% |  |  | 97% |  |  | 94% |  | 
Dec T[%] | 97% |  |  | 98% |  |  | 99% |  | 

## Slide 10: Conclusions
Proposed a unification of the scan pattern
  Part 1: coefficient level scan same as significance map scan pattern
  Part 2: additional unification of scanning order (reverse)
Improved performance and several additional advantages

## Slide 11
Thank you!

## Slide 12: Context sets for coefficient level
Set consists of 16 consecutive coefficients in scan order
  Instead of 4x4 sub-blocks in HEVC
Same contexts derivation for all blocks sizes
  Same number of contexts as in HEVC
Context Set (for 4x4 sub-blocks) | 
0 | For block size 4x4 only
1 | 0-3 LargerT1 in previous sub-block
2 | 4-7 LargerT1 in previous sub-block
3 | 8-11 LargerT1 in previous sub-block
4 | 12-15 LargerT1 in previous sub-block
5 | First 4x4 sub-block (for blocks>4x4) 16 LargerT1 in previous sub-block
HEVC
Proposal
Context Set (inverse 16 scan) |  | 
0 | Sub-set 0 | 0 LargerT1 in previous sub-set
1 |  | 1-3 LargerT1 in previous sub-set
2 |  | >3 LargerT1 in previous sub-set
3 | Other sub-sets | 0 LargerT1 in previous sub-set
4 |  | 1-3 LargerT1 in previous sub-set
5 |  | >3 LargerT1 in previous sub-set

## Slide 13: Additional results
Combination with fixed diagonal scan and enhanced parallelization
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.51 | -0.55 | -0.57 | -0.80 | -1.53 | -1.85 |  |  | 
Class B | -0.28 | -0.72 | -0.66 | -0.11 | -0.91 | -0.59 | 0.06 | -1.37 | -1.63
Class C | -0.26 | -0.51 | -0.47 | 0.02 | -0.63 | -0.53 | -0.03 | -1.72 | -1.43
Class D | -0.21 | -0.48 | -0.47 | 0.02 | -0.74 | -0.77 | -0.09 | -1.99 | -1.39
Class E | -0.28 | -1.02 | -0.99 |  |  |  | -0.09 | -3.23 | -2.87
All | -0.31 | -0.64 | -0.62 | -0.21 | -0.95 | -0.92 | -0.03 | -1.96 | -1.75
Enc T[%] | 95% |  |  | 94% |  |  | 95% |  |