## Slide 1
JCT-VC F295
Harmonizing ROT and SDIP
Samsung Electronics Co.,
Zhan Ma, Felix Fernandes, Elena Alshina, Alexander Alshin
July 2011

## Slide 2: 8x8 Rotational Transform
ROT = secondary transform applied to 8x8,16x16, 32x32, intra blocks
8x8 sub-block at top-left corner of DCT block is input to ROT.
For code in HM SDIP dev branch:
DCT
ROT
(8x8 Rotational Transform)
Quantization
residuals
quantized
coefficients
coefficients
8
8
16
16
 | Square TUs (8x8 and larger) | Non-square TUs
ROT | Yes | No
SDIP | No | Yes

## Slide 3: ROT Definition (A124)
mi = input residuals,
mo = ROT coefficients,
D = DCT matrix,
Rh = horizontal ROT matrix,
Rv = vertical ROT matrix,
Rx, Rz = compound Given’s
rotation matrices.

## Slide 4: Structure of Rh and Rv

## Slide 5: Complexity Reduction Using Lifting Matrices (C096)
Consider the planar rotation matrix R(θ):
Factorize R(θ) into lifting matrices:
where and
Approximate u, v, w by rationals of the form k/32 to replace multipliers with adders and shifters.

## Slide 6: Rx(θ) Complexity Reduction

## Slide 7: Rz(θ) Complexity Reduction

## Slide 8: Final Lifting Multipliers (F294)
U | 0 | 1 | 2 | 3 | 4 | 5
idx = 0 | -7 | -7 | 5 | -4 | -2 | -2
idx = 1 | 4 | -22 | 9 | -7 | -4 | 5
idx = 2 | -3 | -5 | -3 | 2 | -29 | 5
idx = 3 | -10 | -6 | -4 | -1 | -29 | 6
V | 0 | 1 | 2 | 3 | 4 | 5
idx = 0 | 14 | 13 | -10 | 8 | 3 | 4
idx = 1 | -8 | 30 | -17 | 13 | 7 | -10
idx = 2 | 5 | 9 | 6 | -5 | 32 | -10
idx = 3 | 18 | 11 | 8 | 1 | 32 | -12
W | 0 | 1 | 2 | 3 | 4 | 5
idx = 0 |  |  |  |  | -1 | 
idx = 1 |  |  |  |  |  | 
idx = 2 |  |  |  |  |  | 
idx = 3 |  |  |  |  |  | 
Multipliers have 5-bit precision
Only 49 bytes storage (encoder + decoder)
15 multipliers (red) implementable with left shifts
  ZERO cost in hardware

## Slide 9: ROT + SDIP (Samsung F295)
 | Intra |  |  | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.0 | 0.4 | 0.5 | -1.1 | 0.0 | -0.1
Class B | -1.0 | 0.8 | 0.9 | -1.1 | 0.4 | 0.5
Class C | -0.5 | 0.5 | 0.5 | -0.6 | 0.3 | 0.3
Class D | -0.4 | 0.6 | 0.5 | -0.5 | 0.3 | 0.3
Class E | -0.7 | 0.7 | 0.8 | -0.9 | 0.6 | 0.5
All | -0.7 | 0.6 | 0.6 | -0.8 | 0.3 | 0.3
Enc Time[%] | 127% |  |  | 137% |  | 
Dec Time[%] | 108% |  |  | 101% |  | 
 |  | Random access |  |  | Random access LC | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.4 | 0.1 | 0.3 | -0.5 | -0.5 | -0.6
Class B | -0.5 | 0.5 | 0.6 | -0.6 | 0.2 | 0.2
Class C | -0.3 | 0.2 | 0.3 | -0.4 | 0.1 | 0.1
Class D | -0.2 | 0.3 | 0.5 | -0.3 | -0.1 | 0.1
Class E |  |  |  |  |  | 
All | -0.4 | 0.3 | 0.5 | -0.4 | 0.0 | 0.0
Enc Time[%] | 104% |  |  | 104% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 

## Slide 10: ROT + SDIP (Cross checker: Huawei F535)
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.0 | 0.4 | 0.5 | -1.1 | 0.0 | -0.1
Class B | -1.0 | 0.8 | 0.9 | -1.1 | 0.4 | 0.5
Class C | -0.5 | 0.5 | 0.5 | -0.6 | 0.3 | 0.3
Class D | -0.4 | 0.6 | 0.5 | -0.5 | 0.3 | 0.3
Class E | -0.7 | 0.7 | 0.8 | -0.9 | 0.6 | 0.5
All | -0.7 | 0.6 | 0.6 | -0.8 | 0.3 | 0.3
Enc Time[%] | 119% |  |  | 136% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.4 | 0.1 | 0.3 | -0.5 | -0.5 | -0.6
Class B | -0.5 | 0.5 | 0.6 | -0.6 | 0.2 | 0.2
Class C | -0.3 | 0.2 | 0.3 | -0.4 | 0.1 | 0.1
Class D | -0.2 | 0.3 | 0.5 | -0.3 | -0.1 | 0.1
Class E |  |  |  |  |  | 
All | -0.4 | 0.3 | 0.5 | -0.4 | 0.0 | 0.0
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 98% |  |  | 98% |  |