## Slide 1: Run-level Table Reduction for CAVLC
Liwei Guo, Xianglin Wang, Marta Karczewicz
Jul. 2011

## Slide 2: Introduction
  Run level coding in current HM
    2D run-level index mapping table for maxrun = 0 … 27
    434 bytes needed

## Slide 3: Proposed scheme
Restrict the 2D run-level mapping table only for maxrun < 10, for luma and chroma separately
  65 * 2 = 130 byte
For maxrun = 10…27
  Luma
    For levelID==0, cn = run or run+1, depending on cn for maxrun+1
    For levelID==1, cn = maxrun+2+run
    18 bytes needed for index of maxrun+1 for luma
  Chroma
    For levelID==0 cn = run+1, with cn of 0 for maxrun+1
    For levelID==1, cn = maxrun+2+run
All together 148 bytes

## Slide 4: Simulation
Common test condition in JCTVC E700 was used. Encoding was performed on cluster with same CPU; decoding was performed on a single PC.
 | All Intra LC |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.00 | 0.05 | 0.09 | -0.13 | -0.13 | 0.04
Class B | 0.00 | 0.01 | 0.03 | -0.18 | 0.05 | -0.10
Class C | 0.00 | 0.02 | -0.02 | -0.13 | 0.04 | -0.07
Class D | 0.00 | 0.01 | 0.02 | -0.10 | -0.11 | -0.06
Class E | 0.00 | 0.03 | 0.02 |  |  | 
Overall | 0.00 | 0.02 | 0.03 | -0.14 | -0.03 | -0.05
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 98% |  | 
 | Low delay B LC |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.06 | 0.12 | -0.28 | -0.01 | 0.27 | 0.14
Class C | 0.00 | 0.19 | -0.27 | 0.02 | -0.13 | -0.18
Class D | 0.01 | -0.07 | -0.28 | 0.01 | -0.06 | -0.69
Class E | 0.25 | 0.03 | -0.25 | 0.33 | -0.28 | -0.54
Overall | 0.03 | 0.07 | -0.27 | 0.06 | -0.02 | -0.28
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 98% |  | 

## Slide 5: Conclusion
Reducing table size from 434 to 148
No performance loss for luma or chroma
Recommend to adopt the table reduction method in HM.
Thanks to Yonsei Univ. and Samsung for the cross-checking (JCTVC-F406).