## Slide 1
<number>
<number>
JCT-VC F301
CE8 Subtest 1 Block-based Filter Adaptation (BA) with Features on Subset of Pixels
6th JCT-VC Meeting, July 2011
PoLin Lai
Felix C. A. Fernandes Il-Koo Kim Samsung Electronics Co., Ltd
Notes: <number>
겉표지 ( 타이틀 : Tahoma 46, Date : Arial 24 )

## Slide 2: BA: Features computed on subset of pixels
<number>
H(i,j) = abs ( X(i,j)<<1 - X(i,j-1) - X(i,j+1) ) 4 pixels
V(i,j) = abs ( X(i,j)<<1 - X(i-1,j) - X(i+1,j) ) 4 * [1 shift + 2*(2 adds+1 abs) ]  28 operations
H’B = ∑i=0,2 ∑j=0,2 H(i,j) 3 adds
V’B = ∑i=0,2 ∑j=0,2 V(i,j) 3 adds
L’B = H’B + V’B 1 add
Total: 28 + 6 + 1 = 35 (add/shift/abs) per 4x4 block, i.e. 2.2 (add/shift/abs) per luma pixel
This is significantly reduced from over 11 operations per luma pixel as in HM 3.0 [F342].
Notes: <number>

## Slide 3: Results
<number>
HM3.0 RA/BA |  |  |  |  |  | HM3.1-dev-adcs RA/BA |  |  |  | 
 | Intra |  |  |  |  |  | Intra |  |  | 
 | Y BD | U BD | V BD |  |  |  | Y BD | U BD | V BD | 
Class A | 0.1 | 0.0 | 0.0 |  |  | Class A | 0.2 | 0.0 | 0.0 | 
Class B | 0.1 | 0.0 | 0.0 |  |  | Class B | 0.1 | 0.0 | 0.0 | 
Class C | 0.2 | 0.0 | 0.0 |  |  | Class C | 0.2 | 0.0 | 0.0 | 
Class D | 0.1 | -0.1 | -0.1 |  |  | Class D | 0.1 | -0.1 | -0.1 | 
Class E | 0.2 | -0.1 | -0.1 |  |  | Class E | 0.2 | -0.1 | -0.1 | 
All | 0.1 | 0.0 | 0.0 |  |  | All | 0.2 | 0.0 | 0.0 | 
Enc [%] | 99% (99%) |  |  |  |  | Enc [%] | 99% (99%) |  |  | 
Dec [%] | 96% (96%) |  |  |  |  | Dec [%] | 97% (96%) |  |  | 
 | Random access |  |  |  |  |  | Random access |  |  | 
 | Y BD | U BD | V BD |  |  |  | Y BD | U BD | V BD | 
Class A | 0.2 | 0.1 | 0.2 |  |  | Class A | 0.1 | 0.0 | 0.1 | 
Class B | 0.3 | 0.0 | 0.1 |  |  | Class B | 0.3 | 0.0 | 0.0 | 
Class C | 0.2 | 0.1 | 0.0 |  |  | Class C | 0.2 | -0.1 | 0.0 | 
Class D | 0.1 | 0.0 | -0.2 |  |  | Class D | 0.1 | 0.0 | 0.0 | 
Class E |  |  |  |  |  | Class E |  |  |  | 
All | 0.2 | 0.0 | 0.0 |  |  | All | 0.2 | 0.0 | 0.0 | 
Enc [%] | 100% (100%) |  |  |  |  | Enc [%] | 100% (100%) |  |  | 
Dec [%] | 98% (99%) |  |  |  |  | Dec [%] | 99% (99%) |  |  | 
 | Low delay |  |  |  |  |  | Low delay |  |  | 
 | Y BD | U BD | V BD |  |  |  | Y BD | U BD |  | V BD
Class A |  |  |  |  |  | Class A |  |  |  | 
Class B | 0.2 | 0.2 | 0.0 |  |  | Class B | 0.2 | -0.1 |  | -0.2
Class C | 0.2 | 0.0 | -0.1 |  |  | Class C | 0.3 | 0.1 |  | 0.0
Class D | 0.1 | 0.0 | 0.2 |  |  | Class D | 0.1 | -0.2 |  | -0.4
Class E | 0.3 | 0.1 | 0.0 |  |  | Class E | 0.2 | -0.3 |  | -0.5
All | 0.2 | 0.1 | 0.0 |  |  | All | 0.2 | -0.1 |  | -0.2
Enc [%] | 100% (100%) |  |  |  |  | Enc [%] | 100% (99%) |  |  | 
Dec [%] | 98% (98%) |  |  |  |  | Dec [%] | 98% (99%) |  |  | 
Notes: <number>

## Slide 4: Results (BA-Only)
<number>
HM 3.0 BA-ONLY Proposed simplified BA |  |  |  |  |  |  | HM 3.0 BA-ONLY No Classification (sup. Info) |  |  |  |  |  |  | HM 3.1 dev BA-ONLY Proposed simplified BA |  |  |  |  | 
 | Intra |  |  |  |  |  |  | Intra |  |  |  |  |  |  | Intra |  |  |  | 
 | Y |  | U |  | V |  |  | Y | U |  | V |  |  |  | Y |  | U |  | V
Class A | 0.2 |  | 0.0 |  | 0.0 |  | Class A | 0.7 | 0.0 |  | 0.0 |  |  | Class A | 0.2 |  | 0.0 |  | 0.0
Class B | 0.2 |  | 0.0 |  | 0.0 |  | Class B | 0.6 | -0.2 |  | -0.1 |  |  | Class B | 0.2 |  | 0.0 |  | 0.0
Class C | 0.3 |  | -0.1 |  | -0.1 |  | Class C | 0.6 | -0.3 |  | -0.3 |  |  | Class C | 0.2 |  | 0.0 |  | 0.0
Class D | 0.1 |  | -0.1 |  | -0.1 |  | Class D | 0.2 | -0.2 |  | -0.2 |  |  | Class D | 0.1 |  | -0.1 |  | -0.1
Class E | 0.2 |  | -0.1 |  | -0.1 |  | Class E | 0.6 | -0.4 |  | -0.4 |  |  | Class E | 0.2 |  | -0.1 |  | -0.1
All | 0.2 |  | -0.1 |  | -0.1 |  | All | 0.5 | -0.2 |  | -0.2 |  |  | All | 0.2 |  | 0.0 |  | 0.0
Enc[%] | 99% |  |  |  |  |  | Enc[%] | 99% |  |  |  |  |  | Enc[%] | 100% |  |  |  | 
Dec[%] | 97% |  |  |  |  |  | Dec[%] | 95% |  |  |  |  |  | Dec[%] | 97% |  |  |  | 
 | Random access |  |  |  |  |  |  | Random access |  |  |  |  |  |  | Random access |  |  |  | 
 | Y |  | U |  | V |  |  | Y | U |  | V |  |  |  | Y |  | U |  | V
Class A | 0.3 |  | 0.2 |  | 0.1 |  | Class A | 1.0 | 0.2 |  | 0.6 |  |  | Class A | 0.2 |  | 0.0 |  | 0.1
Class B | 0.4 |  | 0.0 |  | 0.1 |  | Class B | 1.2 | -0.1 |  | 0.0 |  |  | Class B | 0.4 |  | 0.0 |  | -0.1
Class C | 0.2 |  | -0.1 |  | -0.2 |  | Class C | 0.5 | -0.3 |  | -0.3 |  |  | Class C | 0.2 |  | -0.1 |  | -0.1
Class D | 0.1 |  | 0.1 |  | 0.2 |  | Class D | 0.2 | -0.2 |  | -0.1 |  |  | Class D | 0.1 |  | -0.1 |  | -0.1
Class E |  |  |  |  |  |  | Class E |  |  |  |  |  |  | Class E |  |  |  |  | 
All | 0.2 |  | 0.1 |  | 0.1 |  | All | 0.7 | -0.1 |  | 0.1 |  |  | All | 0.2 |  | 0.0 |  | 0.0
Enc[%] | 100% |  |  |  |  |  | Enc[%] | 100% |  |  |  |  |  | Enc[%] | 100% |  |  |  | 
Dec[%] | 96% |  |  |  |  |  | Dec[%] | 95% |  |  |  |  |  | Dec[%] | 96% |  |  |  | 
 | Low delay |  |  |  |  |  |  | Low delay |  |  |  |  |  |  | Low delay |  |  |  | 
 | Y |  | U |  | V |  |  | Y | U |  | V |  |  |  | Y |  | U |  | V
Class A |  |  |  |  |  |  | Class A |  |  |  |  |  |  | Class A |  |  |  |  | 
Class B | 0.3 |  | -0.1 |  | -0.1 |  | Class B | 0.8 | -0.2 |  | -0.5 |  |  | Class B | 0.2 |  | 0.0 |  | -0.4
Class C | 0.2 |  | 0.0 |  | -0.2 |  | Class C | 0.5 | -0.4 |  | -0.5 |  |  | Class C | 0.2 |  | -0.1 |  | -0.1
Class D | 0.0 |  | 0.0 |  | -0.2 |  | Class D | 0.2 | -0.2 |  | -0.8 |  |  | Class D | 0.1 |  | 0.3 |  | 0.0
Class E | 0.2 |  | 0.1 |  | -0.3 |  | Class E | 0.7 | -0.5 |  | -0.5 |  |  | Class E | 0.3 |  | 0.3 |  | -0.1
All | 0.2 |  | 0.0 |  | -0.2 |  | All | 0.5 | -0.3 |  | -0.6 |  |  | All | 0.2 |  | 0.1 |  | -0.1
Enc[%] | 100% |  |  |  |  |  | Enc[%] | 100% |  |  |  |  |  | Enc[%] | 100% |  |  |  | 
Dec[%] | 96% |  |  |  |  |  | Dec[%] | 94% |  |  |  |  |  | Dec[%] | 97% |  |  |  | 
Notes: <number>