## Slide 1: JCTVC-F302 Merge Candidate Selection in 2NxN, Nx2N mode
Y. Zheng, X. Wang, W.-J. Chien, M. Karczewicz

## Slide 2: Introduction
Merge mode: motion information is borrowed and directly used from neighboring blocks
2NxN and Nx2N mode: 2nd PU
Some merge candidates may be set as invalid to avoid the redundant mode
In HM3.0, candidate with the same motion information as PU_0 will be avoided
In our proposal, in some case, such candidate can be used
If PU_0 is merge and L is used

## Slide 3: How it works
An example:
  Nx2N mode
  PU_0 is merge mode
  PUIdx = 1 ( second PU )
  When checking candidate L
    HM3.0, L will be avoided
    However …

## Slide 4: Proposed method
Nx2N mode:
  If PU_0 is merge mode and with merge index = T or RA,
  candidate L of PU_1 is valid
  Otherwise
  it is invalid
2NxN mode:
  If PU_0 is merge mode with merge index = T or BL,
  candidate A of PU_1 is valid
  Otherwise
  it is invalid

## Slide 5: Simulation Results (I)
HM 3.0 with bug 146 fixed (CE9 anchor)
Common test condition defined in JCTVC-E700
BD bitrate saving (%)
Encoding and decoding time ratio
 | HE |  |  | LC |  | 
 | Y | U | V | Y | U | V
RA | -0.1 | -0.1 | -0.1 | 0.0 | 0.0 | 0.1
LB | -0.1 | -0.1 | 0.0 | -0.1 | -0.1 | 0.0
 | HE |  | LC | 
 | Encoder | Decoder | Encoder | Decoder
RA | 100% | 99% | 101% | 99%
LB | 99% | 100% | 100% | 99%

## Slide 6: Simulation Results (II)
Combined with Rob02 in CE9 to solve the parsing issue (JCTVC-F474)
0.1% gain is observed when compared with JCTVC-F474
 | JCTVC-F474+ Proposed |  |  |  |  | 
 | HE |  |  | LC |  | 
 | Y | U | V | Y | U | V
RA | -0.1 | -0.1 | -0.1 | -0.1 | -0.1 | -0.1
LB | -0.1 | -0.1 | 0.0 | -0.1 | 0.1 | -0.3

## Slide 7: Conclusion
Minor change to modify the rules of avoiding redundant mode.
The proposed solution improves coding performance with little complexity overhead.
It also helps to solve parsing issue.
The proposal was cross-verified by Canon in JCTVC-F690.
We recommend the proposed changes to be adopted into HM.