## Slide 1
<number>
Cisco, eBrisk, Sharp, and TI
6th JCT-VC Meeting: Torino, IT
July 14-22, 2011
Tiles
Notes: <number>

## Slide 2: Introduction
<number>
Picture partitioning introduces coding loss
Why partition a picture?
  High-level parallel processing
  MTU size matching
  Motion estimation with constrained on-chip memory
Goal: reduce coding loss due to partitioning
Notes: <number>

## Slide 3: Tiles Overview
<number>
Vertical and horizontal boundaries partition picture into columns and rows
Boundary locations may be specified individually or uniformly spaced
Always rectangular with an integer number of LCUs
Notes: <number>

## Slide 4: Tiles Overview (continued)
<number>
Tile bounds may or may not break dependencies
Slice & tile boundaries may or may not coincide
Notes: <number>

## Slide 5: Mods to HM 3.0 Source
<number>
LCU decoding order:
  Raster scan within tiles
  Tiles raster scan within the picture
CU (un)availability across tile bounds
Entropy coding reset across tile bounds
PPS & SPS syntax
  Tile boundaries
  Cross-boundary dependence
Notes: <number>

## Slide 6: Syntax (PPS and SPS)
<number>
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
if (num_tile_columns_minus1 != 0 ¦¦ num_tile_rows_minus1 != 0) { | 
tile_boundary_independence_idc | u(1)
uniform_spacing_idc | u(1)
if (uniform_spacing_idc != 1) { | 
for (i=0; i < num_tile_columns_minus1; i++) | 
column_width[i] | ue(v)
for (i=0; i < num_tile_rows_minus1; i++) | 
row_height[i] | ue(v)
} | 
} | 
Notes: <number>

## Slide 7: High-level Parallel Processing
<number>
Several processors encode one picture
Picture partition table
Notes: <number>
One slice per picture for the tiles case

## Slide 8: Results
<number>
 | Intra HE |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -1.7 | -2.6 | -2.1 | -1.7 | -3.3 | -2.6
 | Random Access HE |  |  | Random Access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -3.1 | -4.5 | -3.7 | -3.1 | -4.5 | -3.8
 | Low Delay HE |  |  | Low Delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -4.8 | -5.4 | -5.3 | -4.7 | -5.0 | -5.0
Notes: <number>

## Slide 9: Conclusions and Recommendation
<number>
High-level parallel processing
  Coding gains vs. HM 3.0 slice reference
    Intra: 1.7%
    Random access: 3.1%
    Low delay: 4.8%
  Gains from slice shape & low header overhead
No additional computational complexity
Separates frame partitioning mechanisms
  Support for partitioning for packetization
  Support for partitioning for parallelization
Notes: <number>

## Slide 10: Conclusions and Recommendation
<number>
Tiles minimize loss when partitioning required
Complementary with fine granularity slices, entropy slices, and wavefront processing
Cross-verification
  Qualcomm and Ericsson
Recommendation: adopt Tiles into the HM
Notes: <number>

## Slide 11: Back-up Slides
<number>
Notes: <number>

## Slide 12: Initial QPY & cabac_init_idc
Initial QPY value in a tile
  QPY = 26 + pic_init_qp_minus26 + slice_qp_delta
  pic_init_qp_minus26 & slice_qp_delta values are conveyed in header of slice containing 1st LCU in the tile
  cabac_init_idc value is conveyed in header of slice containing 1st LCU in the tile
<number>